Fecal Coliform TMDL Assessment for

High Island Creek and Rush River

Submitted by:

Water Resources Center,

Minnesota State University, Mankato

&

Sibley County

October 2008

Minnesota State University, Mankato

Water Resources Center

Publication No. 07-01

Wq-iw7-12b

## Acknowledgements

Submitted by:

Water Resources Center

Minnesota State University, Mankato

184 Trafton Science Center South

Mankato, MN  56001

Project Manager:

Scott Maclean, Minnesota Pollution Control Agency

Project Coordinators:

Scott Kudelka, High Island Creek/Rush River Watershed Coordinator

Scott Matteson, Water Resources Center

TMDL Project technical team:

Terry Bovee, Minnesota Department of Health

Tom Fisher, Minnesota Board of Soil and Water Resources

Al Fox, City of Lafayette

Ryan Freitag, McLeod Soil and Water Conservation District

Mark Hiles, McLeod Environmental Services

Carle Karg, Citizen

Scott MacLean, Minnesota Pollution Control Agency

Jeff Majeski, Sibley County Environmental Services

Diane Mitchell, Renville County Water Management

Dave Pfarr, University of Minnesota Extension

Kevin Pioske, Sibley County Soil and Water Conservation District

Dave Trebelhorn, Corn Producers & Sibley Co. SWCD

Charlie Woehler, Sibley County Commissioner

| Waterbody ID | High Island Creek Watershed |  |  | Page #: |
| --- | --- | --- | --- | --- |
|  | Buffalo Creek: Unnamed Cr to High Island Cr | Fecal coliform | 07020012-578 | 2 |
|  | Buffalo Creek/County Ditch 59: High Island Ditch 5 to Unnamed Stream | Fecal coliform | 07020012-598 |  |
|  | High Island Creek: JD 15 to Unnamed Cr | Fecal coliform | 07020012-535 |  |
|  | High Island Creek: Unnamed Cr to Minnesota R | Fecal coliform | 07020012-589 |  |
|  | High Island Creek Ditch 2: Unnamed Cr to High Island Cr | Fecal coliform | 07020012-588 |  |
|  | Rush River Watershed |  |  |  |
|  | Rush River, South Branch: Unnamed Ditch to Rush R | Fecal coliform | 07020012-553 |  |
|  | Rush River: S Br Rush R to Minnesota R | Fecal coliform | 07020012-521 |  |
| Location | The High Island Creek and Rush River watersheds are located in the Lower Minnesota watershed in south central Minnesota. The watersheds are located across 410,000 acres in portions of McLeod, Nicollet, Renville and Sibley Counties. High Island Creek and the Rush River outlet into the Minnesota River near Henderson, Minnesota. | 1,2 |
| 303(d) Listing Information | The MPCA’s projected schedule for TMDL completions, as indicated on Minnesota’s 303(d) impaired waters list, reflects Minnesota’s priority ranking of this TMDL. Reaches addressed by this project were scheduled to begin between 2002 and 2006 and completed between 2008 and 2009. The impaired reach watersheds include all of High Island Creek and Rush River Watersheds covering a total of 410,997 acres (642 square mile) across portions of Renville, McLeod, Sibley and Nicollet Counties. Four upstream reaches of High Island Creek are also listed as impaired for pathogens. JD 15 to Unnamed Creek is an 83,121 acre watershed located across portions of Renville, Sibley and McLeod Counties (listed in 2002). High Island Ditch 2: Unnamed Cr to High Island Cr drains 10,517 acres in Sibley County (listed in 2008). Buffalo Creek: Unnamed Creek to High Island Creek is an 18,003 acre watershed in Sibley County (listed in 2006). Buffalo Creek/County Ditch 59: High Island Ditch 5 to Unnamed Stream drains 12,350 acres in Sibley County (listed in 2006). One upstream reach of the Rush River is listed as impaired for pathogens. Rush River, South Branch: Unnamed Ditch to Rush River is a 117,918 acre watershed across Sibley and Nicollet Counties (listed in 2008). | 2,4 |
| Impairment / TMDL Pollutant(s) of Concern | Fecal coliform bacteria | 4 |
| Impaired Beneficial Use(s) | The applicable water body classifications and water quality standards are specified in Minnesota Rules Chapter 7050. Minnesota Rules Chapter 7050.0407 lists water body classifications and Chapter 7050.2222 subp. 5 list applicable water quality standards for the impaired reaches for Aquatic Recreation. | 3,4 |
| Applicable Water Quality Standards/ Numeric Targets | Minnesota Rules Chapter 7050 provides the water quality standards for Minnesota waters. The rules are as follows for Class 2B surface waters for fecal coliform bacteria: The quality of Class 2B surface waters shall be such as to permit the propagation and maintenance of a healthy community of cool or warm water sport or commercial fish and associated aquatic life, and their habitats. These waters shall be suitable for aquatic recreation of all kinds, including bathing, for which the waters may be usable. Fecal coliform organisms not to exceed 200 organisms per 100 milliliters as a geometric mean of not less than five samples in any calendar month, nor shall more than ten percent of all samples taken during any calendar month individually exceed 2000 organisms per 100 milliliters. The standard applies only between April 1 and October 31. | 4,12,13 |

TMDL Summary Table 1 of 5

TMDL Summary Table 2 of 5

| Loading Capacity (expressed as daily load) | Flow regimes were determined for high, moist, mid-range, dry and low flow conditions. The mid-range flow value for each flow regime was then used to calculate the total monthly loading capacity (TMLC). Thus, for the "high flow" regime, the loading capacity is based on the monthly flow value at the 5th percentile. The flow used to determine loading capacity for each flow regime was multiplied by a conversion factor of 146,776,126,400. Fecal coliform TMDLs are expressed in both monthly and maximum daily terms. This is to ensure that both the monthly geometric mean and upper tenth percentile portions of the water quality standard are addressed. All maximum daily loading capacity and allocation values are set at a third the monthly loading capacity. In conceptual terms, three days of bacteria loads that approach the maximum daily capacities will "use up" most of the monthly capacity. A greater percentage of days would be considered dry; however the majority of bacterial loading to streams occurs during wet conditions. | Page# |
| --- | --- | --- |
|  |  | 22-29 |
| Wasteload Allocation Fecal Coliform High Island Creek: Unnamed Creek to Minnesota River | Source |  | Individual Daily WLA | Page # |
|  | CAFOs | 30-32 |
|  | Brad Baumgardt Farm Sec 2 | 129-103300 | 0 |  |
|  | Tesch Farms | 143-50002 | 0 |  |
|  | Five Star Dairy LLC | 143-60460 | 0 |  |
|  | Daniel Thoele Farm | 143-89168 | 0 |  |
|  | Larry Baumgardt Farm | 143-89746 | 0 |  |
|  | TOTAL | 0 |  |
|  | Source | Permit # | Individual Daily WLA |  |
|  | WWTF |  |
|  | Arlington | MN0020834 | 0.05 |  |
|  | TOTAL | 0.05 |  |
|  | Source | Permit # | Individual Daily WLA |  |
|  | Straight-Pipe Septics |  |
|  | Illegal Discharges | NA | 0 |  |
|  | TOTAL | 0 |  |
| Wasteload Allocation Fecal Coliform High Island Creek: JD 15 to Unnamed Creek | Source | Permit # | Individual Daily WLA | Page # |
|  | CAFOs | 33-35 |
|  | Brad Baumgardt Farm Sec 2 | 129-103300 | 0 |  |
|  | Larry Baumgardt Farm | 143-89746 | 0 |  |
|  | TOTAL | 0 |  |
|  | Source | Permit # | Individual Daily WLA |  |
|  | WWTF |  |
|  | None | NA | 0 |  |
|  | TOTAL | 0 |  |
|  | Source | Permit # | Individual Daily WLA |  |
|  | Straight-Pipe Septics |  |
|  | Illegal Discharges | NA | 0 |  |
|  | TOTAL | 0 |  |

TMDL Summary Table 3 of 5

| Wasteload Allocation Fecal Coliform Buffalo Creek: Unnamed Creek to High Island Creek | Source | Permit # | Individual Daily WLA | Page # |
| --- | --- | --- | --- | --- |
|  | CAFOs | 36-38 |
|  | Tesch Farms | 143-50002 | 0 |  |
|  | Five Star Dairy LLC | 143-60460 | 0 |  |
|  | Daniel Thoele Farm | 143-89168 | 0 |  |
|  | TOTAL | 0 |  |
|  | Source | Permit # | Individual Daily WLA |  |
|  | WWTF |  |
|  | None | NA | 0 |  |
|  | TOTAL | 0 |  |
|  | Source | Permit # | Individual Daily WLA |  |
|  | Straight-Pipe Septics |  |
|  | Illegal Discharges | NA | 0 |  |
|  | TOTAL | 0 |  |
| Wasteload Allocation Fecal Coliform High Island Creek: High Island Ditch 2 – Unnamed Creek to High Island Creek | Source | Permit # | Individual Daily WLA | Page # |
|  | CAFOs | 50-52 |
|  | None | NA | 0 |  |
|  | TOTAL | 0 |  |
|  | Source | Permit # | Individual Daily WLA |  |
|  | WWTF |  |
|  | None | NA | 0 |  |
|  | TOTAL | 0 |  |
|  | Source | Permit # | Individual Daily WLA |  |
|  | Straight-Pipe Septics |  |
|  | Illegal Discharges | NA | 0 |  |
|  | TOTAL | 0 |  |
| Wasteload Allocation Fecal Coliform Buffalo Creek: High Island Ditch 5 to Unnamed Stream | Source | Permit # | Individual Daily WLA | Page # |
|  | CAFOs | 39-41 |
|  | Five Star Dairy LLC | 143-60460 | 0 |  |
|  | Daniel Thoele Farm | 143-89168 | 0 |  |
|  | TOTAL | 0 |  |
|  | Source | Permit # | Individual Daily WLA |  |
|  | WWTF |  |
|  | None | NA | 0 |  |
|  | TOTAL | 0 |  |
|  | Source | Permit # | Individual Daily WLA |  |
|  | Straight-Pipe Septics |  |
|  | Illegal Discharges | NA | 0 |  |
|  | TOTAL | 0 |  |
| Wasteload Allocation Fecal Coliform Rush River: South Branch Rush River to Minnesota River | Source | Permit # | Individual Daily WLA | Page # |
|  | CAFOs | 42-45 |
|  | Warren Krohn Farm | 103-50002 | 0 |  |
|  | Waibel Pork Inc | 103-50003 | 0 |  |
|  | Corey Hotovec Farm | 103-50007 | 0 |  |
|  | Christensen Farms Site C016 | 103-50008 | 0 |  |
|  | Josie’s Pork Farm Inc - Gaylord | 103-50017 | 0 |  |
|  | Bruce & Laurie Platz Farm – Sec 10 | 103-97452 | 0 |  |
|  | Duane & David Gran Farm – Sec 19B | 103-97625 | 0 |  |
|  | Adam Gleisner Farm Sec 2 | 103-97632 | 0 |  |
|  | Pinpoint Research – Sec 29 | 103-97780 | 0 |  |
|  | Paul and Donita Platz Farm | 143-50001 | 0 |  |
|  | MG Waldbaum – Golden Egg Farm | 143-50004 | 0 |  |
|  | Minnesota Pullets | 143-50005 | 0 |  |
|  | TOTAL | 0 |  |

TMDL Summary Table 4 of 5

| Wasteload Allocation Fecal Coliform Rush River: South Branch Rush River to Minnesota River (cont) | Source | Permit # | Individual Daily WLA | Page # |
| --- | --- | --- | --- | --- |
|  | WWTF | 42-45 |
|  | Altona | MN0067610 | 0.004 |  |
|  | Gaylord | MN0051209 | 0.167 |  |
|  | Gibbon | MNG580020 | 0.019 |  |
|  | Lafayette | MN0023876 | 0.007 |  |
|  | Starland | MN0067334 | 0.002 |  |
|  | Waldbaums | MN0060798 | 0.03 |  |
|  | Winthrop | MN0051098 | 0.079 |  |
|  | TOTAL | 0.31 |  |
|  | Source | Permit # | Individual Daily WLA |  |
|  | Straight-Pipe Septics |  |
|  | Illegal Discharges | NA | 0 |  |
|  | TOTAL | 0 |  |
| Wasteload Allocation Fecal Coliform Rush River: South Branch Unnamed Ditch to Rush River | Source | Permit # | Individual Daily WLA | Page # |
|  | CAFOs | 46-49 |
|  | Warren Krohn Farm | 103-50002 | 0 |  |
|  | Waibel Pork Inc | 103-50003 | 0 |  |
|  | Corey Hotovec Farm | 103-50007 | 0 |  |
|  | Christensen Farms Site CO16 | 103-50008 | 0 |  |
|  | Josie’s Pork Farm Inc - Gaylord | 103-50017 | 0 |  |
|  | Bruce & Laurie Platz Farm – Sec 10 | 103-97452 | 0 |  |
|  | Duane & David Gran Farm – Sec 19B | 103-97625 | 0 |  |
|  | Adam Gleisner Farm Sec 2 | 103-97632 | 0 |  |
|  | Pinpoint Research – Sec 29 | 103-97780 | 0 |  |
|  | Paul and Donita Platz Farm | 143-50001 | 0 |  |
|  | TOTAL | 0 |  |
|  | Source | Permit # | Individual Daily WLA |  |
|  | WWTF |  |
|  | Gibbon | MNG580020 | 0.019 |  |
|  | Lafayette | MN0023876 | 0.007 |  |
|  | TOTAL | 0.026 |  |
|  | Source | Permit # | Individual Daily WLA |  |
|  | Straight-Pipe Septics |  |
|  | Illegal Discharges | NA | 0 |  |
| Margin of Safety | Because the allocations are a direct function of monthly flow, accounting for potential flow variability is the appropriate way to address the MOS explicitly for the fecal coliform impairments. This is done within each of five flow zones. The MOS was determined as the difference between the median flow and minimum flow in each zone. | Page # |
|  |  | 53 |
| Seasonal Variation | Monitoring data show an apparent relationship between season and fecal coliform bacteria concentration. Typically the highest bacterial concentrations are found in the summer and early fall. In the spring, concentrations are typically lower, despite the fact that significant manure application occurs during this time and that fields have little crop canopy to protect against water erosion. | 19 |
| Reasonable Assurance | The source reduction strategies detailed in the implementation plan section have been shown to be effective in reducing pathogen transport/survival. Many of the goals outlined in this TMDL study run parallel to objectives outlined in the local Water Plans. Various program and funding sources will be used to implement measures that will be detailed in an implementation plan to be completed. Through existing permit programs fecal coliform impairments are being addressed and monitored. In the future, it can be assumed that this will continue. | 76 |

TMDL Summary Table 5 of 5

| Monitoring | A detailed monitoring plan will be included in the Implementation Plan to be completed. Currently, there are monitoring efforts in the watershed. | Page # |
| --- | --- | --- |
|  |  | 53 |
| Implementation | A summary of potential management measures was included. More detail will be provided in the implementation plan. | 73-75 |
| Public Participation | Public participation opportunities were provided during the project in the form of public open houses, news releases and a project newsletter. The project worked closely with a broad array of county, state and individual stakeholders. | 78 |
|  | Public Comment period: |  |  |
|  | Meeting location: |  |  |
|  | Comments received: |  |  |

Executive Summary

The High Island Creek and Rush River Watersheds are located in the Lower Minnesota Watershed, in south central Minnesota. The watersheds are located across 410,000 acres in portions of McLeod, Nicollet, Renville and Sibley counties. High Island Creek and Rush River outlet into the Minnesota River near Henderson, Minnesota. According to the State of the Minnesota River annual reports, these rivers rank among the highest for fecal coliform bacteria concentrations in the entire Minnesota River Basin.

This document contains the TMDLs for five impaired stream reaches in the High Island Creek Watershed and two in the Rush River Watershed. These stream reaches are listed as impaired for failure to meet their swimming designated uses due to excessive fecal coliform concentrations.

Water quality data collected in both watersheds show elevated fecal coliform concentrations at all monitored stream sites. Monitoring data indicate an 80%-90% reduction in fecal coliform levels will be needed to meet surface water quality standards. The data indicate fecal coliform bacteria levels are typically the highest in the summer months of June and July, particularly during storm runoff events. The document describes the likely major contributors of fecal coliform contamination separated into two major categories - dry conditions and wet conditions. Under dry conditions, when there is limited dilution in the streams, direct or continuously discharging bacteria sources might be dominant. Under wet conditions, runoff-related sources are more important.

Applied manure and inadequately functioning septic systems appear to be the primary sources of fecal coliform contamination based on source inventory assessments and water quality testing. While there is considerable uncertainty about the actual magnitude of these sources, these are the areas where increased focus would seem to have the most potential for water quality improvements. The following statements from the Minnesota Generic Environmental Impact Statement on Animal Agriculture (2001) supports attention on land application of manure – “Thus, from a policy perspective, the primary water quality impact of animal manure is from land applied manure. Non-compliant feedlot runoff or seepage, and illegal spills have a negligible overall impact on regional water quality patterns. Without considering this, there is the real potential that the federal, state, and local governments will spend millions of dollars fixing noncompliant feedlots, without the prospect of making much difference in regional water quality problems.”  While there is state and local regulatory authority related to septic systems, addressing land application will be primarily through research, education, and the promotion of voluntary BMPs.

While pollutant runoff from urban landscapes can be as great or greater than that from agricultural areas, only about two percent of the land area of the Rush and High Island watersheds are in commercial, industrial and residential use. As such, the overall contribution of bacteria from other land use is believed to be relatively small. In addition, the sewage treatment for the cities and towns in the watersheds includes disinfection which results in the discharge of treated wastewater with very low bacteria levels.

Livestock manure represents nearly 99% of the fecal matter produced in each watershed. The vast majority of this manure is contained in pits, basins or barns; or stockpiled on lots or pads, until it can be used as a fertilizer. The manure is either incorporated into or surface applied, on farm fields. As such, the majority of fecal material that is produced in the basin is land applied manure. Land application of this manure has three potential pathways to reach surface waters; 1) overland runoff, 2) open tile intakes and 3) macropores/preferential flow. The majority of livestock producers in the watersheds are probably handling their manure and conducting land application consistent with current rules, guidelines, and University recommendations. These practices, however, do not typically result in total containment of manure under all conditions. Even if less than 1% of the land applied manure enters surface waters through one or more of the pathways mentioned, it could account for violations of the bacterial water quality standard. It should be noted that agricultural field runoff generally contains at least some fecal bacteria even in the absence of recent manure application or grazing. There are several explanations for this including the presence of wildlife, the survival of bacteria in soils for long periods of time, and the possible colonization in the soil by “indigenous” coliform bacteria that have no direct link to humans, wildlife or livestock. These factors should reinforce the value of controlling soil erosion and sediment runoff as a “multi-benefit” water quality improvement strategy.

It is important to note that livestock and livestock manure have environmental and economic benefits that must be taken into account and weighed against potential bacterial water quality impacts. Livestock manure reduces commercial fertilizer demand, while adding organic matter to the soil. Soil rich in organic matter is less prone to erosion. There are also significant numbers of beef and dairy cattle in the watersheds. The pasture and hay land supported by these ruminants may result in further soil erosion reduction, particularly if it is located on steeper lands.

Primary sources of fecal coliform contamination during low flows appear to be “straight pipe” septic systems, systems that discharge untreated sewage directly or through tile drainage to surface waters. There are estimated to be over 500 of these systems in High Island Creek watershed, and nearly 900 in Rush River Watershed. Direct discharge of these systems to surface waters during low flow periods can be a major contributor of fecal coliform contamination.

A third significant source during both wet and dry periods appears to be the stream channel itself. A portion of fecal coliform contamination from human and animal sources may stay in the stream channel sediments and act as a reservoir. Increases in flow during storm runoff can cause resuspension of sediments that contain fecal coliform bacteria. In some situations, exceedances of water quality standards during low flow periods may also partially be attributed to release of fecal coliform bacteria from streambed sediments.

The document also describes conditions when bacterial concentrations are highest in High Island Creek and Rush River. Monitoring data show bacterial concentrations appear to increase as air and water temperature increases. The data also show a strong correlation between suspended sediment and bacterial concentrations, with high bacterial concentrations found with high sediment concentrations.

This document describes the above sources and dynamics in more detail. The document also describes applicable water quality standards for fecal coliform bacteria, population source inventories, TMDL allocations and suggested implementation strategies.

During the time this TMDL is on public notice, it is anticipated that Minnesota’s bacterial water quality standard will change from fecal coliform to E. coli. E. coli is a sub-group of fecal coliform. Because the E. coli standard was developed to be “equivalent” to the fecal coliform standard in terms of protectiveness, the loading capacity, allocations, reduction estimates, and general implementation activities developed to attain the fecal coliform water quality standards should also result in attainment of the new E. coli standard.

TABLE OF CONTENTS

Cover Page										i

Acknowledgements									ii

TMDL Summary Table								iii

Executive Summary									viii

Table of Contents									xi

List of Figures									xiii

List of Tables									xiv	List of Appendices								xv

Acronyms										xv

Section 1.0 – Introduction								1

1.1 - Overview								1

1.2 - Purpose									3

Section 2.0 - Background Information						5

2.1 - Study Area Overview							5

2.2 - Land Use and Cover (1990)						5

2.3 - Temperature								8

2.4 - Precipitation								8

2.5 - Stream Flow Characteristics						10

2.6 - Streambed Sediments							10

2.7 - DNA Fingerprinting Results for High Island Creek Watershed		11

Section 3.0 – Applicable Water Quality Standards and Water Quality		12

Numeric Targets

3.1 - Description of Fecal Coliform Bacteria					12

3.2 - Applicable Minnesota Water Quality Standards			12

3.2.1 - Class 2B waters; aquatic life and recreation			12

3.3 - Impairment Assessment:  Fecal Coliform Impairments			13

3.4 - Fecal Coliform and Flow						16

3.5 - Fecal Coliform and Total Suspended Solids				17

3.6 - Geographic Scope of Impairment					19

3.7 - Seasonality 								19

3.8 - Trends in Fecal Coliform Surface Water Quality			20

3.9 - TMDL Endpoints							20

Section 4.0 – Explanation of Load Allocations, Wasteload Allocations 		22

and Margin of Safety

Section 5.0 – TMDL Allocations for Individual Impaired Reaches		30

5.1 - High Island Creek; Unnamed Creek to Minnesota River		30

5.1.1 - Water Quality Data and Required Reductions		32

5.2 - High Island Creek; JD 15 to Unnamed Creek				33

5.2.1 - Water Quality Date and Required Reductions		35

5.3 - Buffalo Creek; Unnamed Creek to High Island Creek			36

5.3.1 - Water Quality Data and Required Reductions		38

5.4 - Buffalo Creek; High Island Ditch 5 to Unnamed Stream		39

5.4.1 - Water Quality Data and Required Reductions		41

5.5 - Rush River; South Branch Rush River to Minnesota River		42

5.5.1 - Water Quality Data and Required Reductions		45

5.6 - Rush River; South Branch Rush River to Minnesota River		46

5.6.1 - Water Quality Data and Required Reductions		49

5.7 - Rush River; South Branch Rush River to Minnesota River		50

5.7.1 - Water Quality Data and Required Reductions		52

Section 6.0 – Margin of Safety							53

Section 7.0 – Monitoring Plan							53

Section 8.0 – Bacteria Source Assessment and Implemenation Activities 	53

8.1 – Source Assessment - Humans						53

8.1.1 - Human Populations						54

8.1.2 - Noncompliant Individual Sewage Treatment Systems 	55

8.1.3 - Unsewered Communities					56

8.1.4 - MS4 Communities – Stormwater				56

8.1.5 - Municipal Waste Water Treatment Facility Bypasses	56

8.1.6 - Municipal Waste Water Treatment Facility Violations	57

8.1.7 - Application of Sewage Sludge to Agricultural Lands		57

8.2 – Source Assessment - Livestock						57

8.2.1 - Overland Runoff and Open Tile Intakes			59

8.2.2 - Macropores/Preferential Flow					60

8.3 – Source Assessment - Pets						64

8.4 – Source Assessment - Wildlife and Natural Background		64

8.5 - Targeted Sources							65

8.5.1 - Fecal Coliform Produced (by source)				65

8.5.2 - Delivery Assumptions						72

8.5.3 - Target Areas							72

8.6 – Implementation Activities						73

8.6.1 - Feedlot Runoff Controls					73

8.6.2 - Manure Management Planning				74

8.6.3 - Non-Conforming Septic Systems				74

Section 9.0 – Reasonable Assurance						76

9.1 - Feedlot Runoff Controls							76

9.2 - Land Application of Manure						76

9.3 - Individual Sewage Treatment Systems					76

9.4 - Municipal Waste Water Disinfection					76

9.5 - Erosion Control and Sediment Reduction				77

9.6 - Planned Rotational Grazing						77

9.7 - Urban Stormwater Management						77

Section 10.0 – Public Participation							78

10.1 - Stakeholder Involvement						78

10.2 - Results of TMDL Survey  						79

10.3 - Input and Comments							82

FIGURES

Section 1.0 – Introduction

Figure 1.1 - Impaired Reach Locations and River Assessment IDs		2

Section 2.0 - Background Information

Figure 2.2a - HICW Landuse and Cover Map				6

Figure 2.2b - RRW Landuse and Cover Map					7

Figure 2.3 - Average Monthly Temperature by Month			8

Figure 2.4 - Map of Average Precipitation for Minnesota 			9

Figure 2.5 - Mean  Monthly Flow for High Island Creek, near Henderson	10

Section 3.0 – Applicable Water Quality Standards and WQ Numeric Targets

Figure  3.3a - FC Bacteria Monitoring Sites in HICW and RRW  		14

Figure  3.3b – Rush River Monthly FC Geometric Means			15

Figure 3.3c – High Island Creek Monthly Fecal Coliform GMs 		15

Figure  3.4a - Flow Duration Curve for HIC, near Henderson		16

Figure  3.4b - Load Duration Curve for HIC, near Henderson		17

Figure  3.5 - TSS Load Duration Curve HIC, near Henderson		18

Figure  3.7 - Beauford Creek – Fecal Coliform vs. Stream Temperature	20

Section 4.0 – Explanation of Load Allocations, Wasteload Allocations

and Margin of Safety

Figure 4.0a - High Island Creek Flow Duration Curve 			24

Figure 4.0b - High Island Creek Flow Duration Curve with TMLC/MOS	25

Section 5.0 – TMDL Allocations for Individual Impaired Reaches

Figure 5.1 - High Island Creek; Unnamed Creek to Minnesota River	30

Figure 5.1.1 - Monthly GM FC Concentrations			32

Figure 5.2 -  High Island Creek; JD 15 to Unnamed Creek			33

Figure 5.2.1 - Monthly GM FC Concentrations			35

Figure 5.3 - Buffalo Creek; Unnamed Creek to High Island Creek		36

Figure 5.3.1 - Monthly GM FC Concentrations			38

Figure 5.4 - Buffalo Creek; High Island Ditch 5 to Unnamed Stream	39

Figure 5.4.1 - Monthly GM FC Concentrations			41

Figure 5.5 - Rush River; South Branch Rush River to Minnesota River	42

Figure 5.5.1 - Monthly GM FC Concentrations			45

Figure 5.6 - Rush River; South Branch; Unnamed Ditch to Rush River	46

Figure 5.6.1 - Monthly GM FC Concentrations			49

Figure 5.7 - High Island Ditch 2, Unnamed Creek to High Island Creek	50

Figure 5.7.1 - Monthly GM FC Concentrations			52

Section 8.0 – Bacteria Source Assessment and Implementation Activities

Figure 8.2a - HICW and RRW Livestock Feedlots				58

Figure 8.2b - Potential Manure Spread Land in Sibley County		59

Figure 8.2.2 - Examples of macropore/preferential flow routes in a no	63

till tiled field in Ohio

Figure 8.5.1a - HICW FC Bacteria Produced by Animal Type		66

Figure 8.5.1b - HICW FC Bacteria Produced by Source Group		67

Figure 8.5.1c - RRW FC Bacteria Produced by Animal Type		67

Figure 8.5.1d - RRW FC Bacteria Produced by Source Group		68

Figure 8.5.1e - Est. FC Produced by Source/Application Type in HICW	71

Figure 8.5.1f - Est. FC Produced by Source/Application Type in RRW	71

TABLES

Section 1.0 – Introduction

Table 1.1 - FC Bacteria Impaired Stream Reaches				2

Section 2.0 - Background Information

Table 2.2 - Landuse and cover (1990)					5

Table 2.4 - Precipitation Data for Major Cities				9

Section 3.0 – Applicable Water Quality Standards and WQ Numeric Targets

Table 3.2.1 - Minnesota Surface Water Standard for FC Bacteria		13

Table 3.3 - Stream Monitoring Sites and Impairment Assessment Data	14

Table 3.4 - Fecal Coliform Statistics by Flow Condition			17

Table 3.5a – High Island Creek Outlet – FC vs TSS Statistics		18

Table 3.5b – Rush River Outlet – FC vs TSS Statistics			18

Table 3.7a – High Island Creek Outlet FC Statistics by Month		19

Table 3.7b – Rush River Outlet FC Statistics by Month			19

Section 4.0 – Explanation of LA, WLA and MOS

Table 4.0a – High Island Creek, Monthly Mean Flow Values		23

Table 4.0b – Flow Regimes and Values Used to Calculate Total		24

Monthly Loading Capacity

Table 4.0c -  TMDL and MOS for High Island Creek			26

Section 5.0 – TMDL Allocations for Individual Impaired Reaches

Section 5 contains the following tables for each impaired reach

- Human and Animal Population Inventory

- Wastewater Treatment Facilities

- Municipal Separate Storm Sewer System (MS4 ) Communities

- Monthly Fecal Coliform Loading Capacities and Allocation

Section 8.0 – Bacteria Source Assessment and Implementation Activities

Table 8.1.1a - Urban Population Estimates					54

Table 8.1.1b – City Populations for HICW and RRW			54

Table 8.1.2a - High Island Creek Watershed IPHT Estimates		55

Table 8.1.2b - Rush River Watershed IPHT Estimates			55

Table 8.1.5 - Number of Bypasses by Watershed and by Year 		57

Table 8.2 – HICW and RRW Livestock Statistics	 			58

Table 8.2.1 – Manure Application Rules for Minnesota			60

Table 8.5.1a – High Island Creek Population Inventory			65

Table 8.5.1b – Rush River Population Inventory				66

Table 8.5.1c - Assumptions Used to Calculate the FC Produced 		69

by Different Sources in HICW

Table 8.5.1d - Assumptions Used to Calculate the FC Produced 		70

by Different Sources in RRW

Table 8.5.2 - Delivery Assumptions						72

Table 8.5.3 - Major Contributors of FC Bacteria 				73

Appendices

Appendix A – References

Acronyms

AU – Animal Unit

CFU – Colony Forming Units

CFS – Cubic Feet Per Second

CWP – Clean Water Partnership

DNR – Department of Natural Resources

FC – Fecal Coliform

HICW – High Island Creek Watershed

ISTS – Individual Sewage Treatment System

IWMI – Interagency Watershed Monitoring Initiative

LA – Load Allocation

MOS – Margin of Safety

MPCA – Minnesota Pollution Control Agency

MS4 – Municipal Separate Storm Sewer Permit

NPDES – National Pollutant Discharge Elimination System

NRCS – Natural Resources Conservation Service

QAQC – Quality Assurance Quality Control

RRW – Rush River Watershed

TMDL – Total Maximum Daily Load

USDA – United States Department of Agriculture

USEPA – United States Environmental Protection Agency

WLA – Waste Load Allocation

WTF – Wastewater Treatment Facility

Section 1.0 – Introduction

  - Overview

High Island Creek Watershed (HICW) is a 153,222 acre watershed located across three southern Minnesota counties; Sibley (66% area), McLeod (23%) and Renville (11%). High Island Creek is part of the Lower Minnesota Watershed, a major sub-basin of the Minnesota River Basin.

The watershed topography is flat to gently rolling in the western two-thirds and steeply sloped terrain in the eastern one-third. The watershed receives an average of 27 inches of annual precipitation.  Soils range from poorly drained to well drained loamy soils. Approximately 85% of the landuse is agricultural, primarily corn and soybeans.  As of the 2002 feedlot inventory, there were 194 feedlots containing 27,612 animal units in the watershed. Livestock includes dairy, beef, swine and poultry.

The population of HICW is estimated at 5,351, with three small cities: Arlington, New Auburn and a portion of Stewart. Forty-seven percent of the population lives in rural areas.  An estimated 2,517 watershed residents utilize individual septic systems for their waste treatment, equating to roughly 1,013 rural septic systems.

The RRW is a rural watershed that drains 257,775 acres in Sibley, Nicollet and McLeod counties. Rush River has three tributaries, the north, middle and south branches of the Rush River. RRW is part of the Lower Minnesota River Watershed a major sub-basin of the Minnesota River Basin. As the largest of the Lower Minnesota River subwatersheds, the RRW comprises 22% of the total land area. The combined stream length of the north, middle, south and mainstem is 50 miles, with an additional 500 miles of public open ditches. Artificial drainage has increased stream length by 400 to 500 % of the original stream. In addition, there are several thousand miles of public and private tile and an estimated 7000 open tile intakes.

The western ¾ of the Rush River Watershed is flat to gently rolling. The three branches of Rush River converge in the eastern ¼ of the watershed, where the watershed becomes steeply sloped. An estimated 90% of the landscape is in an agricultural landuse. There are 429 feedlots with 86,329 animal units in the watershed.

Four cities are located in the watershed; Gaylord, Winthrop and Gibbon in Sibley County and Lafayette in Nicollet County. The population of the watershed is estimated at approximately 9,010 (44.7% rural). Fifty-five percent or an estimated 4,027 residents utilize an individual septic treatment system (ISTS).

Fecal coliform bacteria levels in High Island Creek and Rush River are among the highest  of all monitored streams in Minnesota. As of fall 2007 there were five stream reaches in High Island Creek Watershed and two in Rush River Watershed listed on the 303d list of impaired streams. Table 1.1 presents the impaired stream reaches for fecal coliform bacteria in the watersheds.

Table 1.1 - Fecal Coliform Bacteria Impaired Stream Reaches

| Stream Name | Description | Year Listed | Target Completion | MPCA River Assessment Unit ID |
| --- | --- | --- | --- | --- |
| High Island Creek Watershed |  |  |  |  |
| Buffalo Creek | Unnamed Cr to High Island Cr | 2006 | 2009 | 07020012-578 |
| Buffalo Creek / County Ditch 59 | High Island Ditch 5 to Unnamed Stream | 2006 | 2009 | 07020012-598 |
| High Island Creek | JD 15 to Unnamed Cr | 2002 | 2008 | 07020012-535 |
| High Island Creek | Unnamed Cr to Minnesota R | 2006 | 2009 | 07020012-589 |
| High Island Creek Ditch 2 | Unnamed Cr to High Island Cr | 2008 |  | 07020012-588 |
| Rush River Watershed |  |  |  |  |
| Rush River, South Branch | Unnamed Ditch to Rush R | 2008 |  | 07020012-553 |
| Rush River | S Br Rush R to Minnesota R | 2002 | 2008 | 07020012-521 |

Figure 1.1 displays the location of the seven impaired stream reaches.  The mainstem High Island Creek is divided into two impaired reach segments, splitting at High Island Lake outlet.  Buffalo Creek also has two impaired reach segments which split at the confluence of county ditches 5 and 59.

Figure 1.1 – Impaired Reach Locations and River Assessment ID’s

1.2  Purpose

Section 303(d) of the federal Clean Water Act and US Environmental Protection Agency’s (EPA’s) Water Quality Planning and Management Regulations (40 CFR Part 130) require states to develop Total Maximum Daily Loads (TMDLs) for waterbodies which are violating water quality standards.

A TMDL represents the maximum amount of pollutant a waterbody can receive and still meet water quality standards and designated uses. The TMDL process establishes the allowable loading of pollutants for a waterbody based on the relationship between pollution sources and in-stream water quality conditions.

The EPA specifies that in order for a TMDL to be considered complete and approvable, it must include the following eight elements:

- It must be designed to meet applicable water quality standards;

- It must include a total allowable load as well as individual waste load allocations and load allocations;

- It must consider the impacts of background pollutant contributions, such as wildlife;

- It must consider critical environmental conditions, such as stream flow, precipitation, temperature, etc;

- It must consider seasonal environmental variations;

- It must include an implicit or explicit margin of safety to account for uncertainties inherent to the TMDL development process;

- It must provide opportunity for public participation; and

- It should consider reasonable assurance in the attainment of allocations.

In general, the TMDL is developed according to the following relationship:

TMDL =  WLA + LA + MOS

Where (for fecal coliform TMDLs):

WLA	= 	Waste Load Allocation, which is the sum of all point sources, including:

Permitted Wastewater Treatment Facilities

Communities Subject to MS4 NPDES Requirements

Livestock Facilities Requiring NPDES Permits

“Straight Pipe” Septic Systems

LA	=	Load Allocation, which is the sum of all nonpoint sources, including;

Runoff from fields receiving manure application

Runoff from feedlots without runoff controls

Overgrazed pastures near streams and waterways

Urban Stormwater

Wildlife

MOS	=	Margin of Safety (may be implicit and factored into conservative WLA or

LA, or explicit.)

This document provides the information used to develop TMDLs for five impaired reaches in HICW and two impaired reach in RRW. These stream reaches are listed as impaired for failure to meet their swimming designated beneficial uses due to excessive fecal coliform concentrations.

The criteria used for determining stream reach impairments is outlined in the Minnesota Pollution Control Agency (MPCA) document, Guidance Manual for Assessing the Quality of Minnesota Surface Waters for Determination of Impairment – 305(b) Report and 303(d) List), January 2003. The applicable water body classifications and water quality standards are specified in Minnesota Rules Chapter 7050. Minnesota Rules Chapter 7050.0407 lists water body classifications and Chapter 7050.2222 subp. 5 lists applicable water quality standards for the impaired reaches.

The assessment protocol includes pooling of data by month over a 10-year period. A geometric mean is then calculated for each month, April through October, with a minimum of five samples used for each monthly calculation.

There are two scenarios when a stream reach will qualify to be listed as impaired. If any monthly geometric mean value exceeds 200 organisms per 100 ml the stream qualifies to be listed as impaired. The other scenario involves combining the entire ten year data set and assessing the percent of samples that exceed 2000 organisms per 100 ml. If more than 10% of the samples exceed 2000 org/100ml, the stream qualifies as listing as impaired.

Table 3.3 represents the analysis of 336 fecal coliform bacteria samples collected from five monitoring sites in the High Island Creek watershed and 370 samples from five sites in Rush River Watershed (1997 though 2005). These samples were collected as part of the High Island Creek Assessment Project Clean Water Partnership (CWP) and the Rush River Assessment Project CWP.

The CWP projects used MPCA standard quality assurance quality control (QAQC) procedures in collection of samples, which includes collection of samples in sterilized bottles, shipping samples at 4 degrees C and delivery of samples to a certified laboratory within the 24 hour holding period. Fecal coliform samples were analyzed at Minnesota Valley Testing Laboratory in New Ulm.

Monitoring data from the CWP projects indicate frequent violations of the monthly fecal coliform standard. The magnitude of these violations, especially during the summer months, suggest serious water quality impairments that will require substantial bacterial reductions in waterbodies.

Section 2.0 - Background Information

  - Study Area Overview

Fecal Coliform bacteria contamination is a significant water quality concern in High Island Creek Watershed (HICW), with five stream reaches listed on the US EPA 303 (d) impaired waters list. Since monitoring began in the late-1990’s, the HICW has ranked near the highest for fecal coliform bacteria levels among Minnesota River Basin tributaries. Fecal Coliform bacteria counts frequently exceeded the surface water standard of 200 colony forming units per 100 ml at all monitored sites in the watershed.  Runoff from feedlots, manure applied lands and noncompliant septic systems were indicated as significant sources of bacterial contamination in the HICW CWP Final Report.

Elevated fecal coliform bacteria concentrations are also a concern in the RRW with the mainstem Rush River being listed on the 303(d) list. The Rush River CWP Final Report indicated the primary sources for FC contamination to be applied manure, runoff from noncompliant feedlots and sewage discharges from noncompliant septic systems.

2.2  Land Use and Cover (1990)

HICW and RRW’s are dominated by cultivated land at 84.3% and 90.1% respectively. In HICW the other significant land use categories are woodland (4.8%), grassland (4.6%) and urban/rural development (2.1%). In RRW, the other major land use categories include woodland (3.6%), urban/rural development (2.3%) and grassland (1.6%).

Table 2.2 – High Island Creek and Rush River Watersheds Land Use and Cover (1990)

|  | High Island Creek Watershed | Rush River Watershed |
| --- | --- | --- |
| Land Use and Cover | Acres | Percent | Acres | Percent |
| Conservation | 1,686 | 1.1% | 1,821 | 0.7% |
| Cultivated Land | 129,197 | 84.3% | 232,337 | 90.1% |
| Grassland | 7,178 | 4.7% | 4,050 | 1.6% |
| Gravel/Pit/Rock/Sand | 13 | 0.0% | 32 | 0.0% |
| Urban/Rural Development | 3,242 | 2.1% | 5,804 | 2.3% |
| Water | 2,560 | 1.7% | 1,899 | 0.7% |
| Wetlands | 1,996 | 1.3% | 2,561 | 1.0% |
| Woodland | 7,351 | 4.8% | 9,272 | 3.6% |
| Total Acres | 153,223 | 100.0% | 257,776 | 100.0% |

Figures 2.2a and 2.2b present land use and cover for both watersheds based on 1990 landuse statistics.

2.3  Temperature

Figure 2.3 presents the average monthly temperatures at Gaylord, Minnesota (located in RRW) during the monitoring season months of April through October. Ice out conditions in the watersheds typically occur between the end of March and early April. Temperatures reach peak levels during July/August and then gradually decline. Monitoring data indicate that temperature does have an association with bacterial concentrations in surface waters. Monitoring data indicate that very cold stream water during early spring often is below surface water standards for fecal coliform bacteria.

Figure 2.3 – Average Monthly Temperature by Month

2.4  Precipitation

The watersheds average 29 to 30 inches of precipitation annually. The monitoring season months of April through October represent 80% of the annual average precipitation with totals of 23 to 24 inches. In a typical year, the western portions of the watersheds receive less precipitation than the east. Table 2.4 presents the average monthly precipitation values for three locations in or near HICW and RRW.

Figure 2.4 – Map of Average Precipitation for Minnesota

Table 2.4 – Precipitation Data for Cities in HIRR Watersheds

Review of monitoring data collected during the CWP projects show a strong relationship between fecal coliform bacteria concentration and rainfall intensity. The highest bacterial concentrations of any particular year are usually associated with the highest intensity precipitation events. This is especially true during the spring when farm fields are not protected by crop canopy. Crop canopy significantly reduces rainfall runoff and associated soil erosion and pollutant movement.

  - Stream Flow Characteristics

The surface water standard for fecal coliform bacteria applies to the months of April through October. On average, the month with the highest flow volume is April, due to the combination of snowmelt runoff and runoff from precipitation. June, the month with the greatest precipitation totals has the second highest mean monthly flow.

Figure 2.5 – Mean Monthly Flow for High Island Creek near Henderson (1973-2005)

  - Streambed Sediments

A potential source of fecal coliform bacteria in streams/rivers that is often overlooked is resuspension of streambed sediments. Several studies have reported significantly increased concentrations of water column fecal coliform density after disturbance of the surface sediments. Weiskel et al. (1996) reported greatly increased values of fecal coliform density after artificial disturbance of the surface 2 cm of sediments in Buttermilk Bay, Massachusetts. Ewert (2005) in a study conducted in southern Minnesota, found that physical raking of streambed sediments resulted in bacteria concentrations several factors higher than the water column values before resuspension.  Jolley et al. (2004) reported bottom sediment reservoirs of indicator bacteria in surface water increase surface water levels at base flow and should be considered sources of surface water contamination. Davis et al. (2005) reported that in stream observations in Arkansas indicated it is possible for E. coli to survive in certain streambed sediments for at least four months with no fresh external inputs.

As runoff during a storm event begins, the discharge and velocity increase, in turn scouring bacteria from the benthic areas of the stream (Yagow and Shanholtz, 1998). This scouring causes increased levels of bacteria in the water column and decreased levels in stream sediments.

  - DNA Fingerprinting Results for High Island Creek Watershed

In 2001 and 2002, the University of Minnesota used a library of DNA fingerprints, created by rep-PCR and HFERP techniques, in an attempt to define sources of fecal bacterial pollution, E. coli, in three Minnesota watersheds; High Island Creek, Minneopa Creek and Vermillion River. The U of M partnered with HICW CWP in collection of water samples from 10 sites in 2001 and 2002. A total of 1,651 E. coli isolates were DNA fingerprinted from the HICW.

Results of the study indicated that each of the ten sites had a variety of possible sources of fecal coliform contamination, with no one animal type dominating. The U of M reported that the results of the study revealed the known source library size was not large enough to accurately determine sources in High Island Creek with any certainty. Accordingly, results of this study were not used for the development of this TMDL report.

The report did stress that when isolates were categorized into larger source groups, the accuracy improved. Overall the U of M found it was probable that about 16% of the isolates identified were human with the remaining 84% non-human.

Results of this project are available online at www.ecolirep.umn.edu and were published in a final report titled Determination of Fecal Pollution Sources in Minnesota Watersheds (Sadowsky, 2004).

Section 3.0 – Applicable Water Quality Standards and

Water Quality Numeric Targets

  - Description of Fecal Coliform Bacteria

Fecal coliform bacteria are a bacteria group that are found in the intestines of warm blooded animals. While usually not harmful themselves, fecal coliforms are considered an indicator of the presence of other disease causing bacteria, viruses, and/or protozoans.

Fecal coliform bacteria are passed through the fecal excrement of humans, livestock and wildlife. These bacteria can enter streams and ditches through direct discharge of waste from mammals and birds, from agricultural and urban stormwater runoff and from poorly or untreated human sewage. Agricultural practices such as spreading manure during wet periods and allowing livestock uncontrolled access to streams can contribute to high levels of fecal coliform bacteria. Wildlife can also be a contributor of fecal coliform bacteria, especially during low flow conditions.

In addition to bacteria and other pathogens, human and animal waste contain high levels of other pollutants such as phosphorus, nitrogen, and oxygen demanding organic material. Additionally, some of the same soil erosion processes and delivery pathways that lead to sediment pollution of streams and rivers also contribute to human and animal waste entering the water. As such, efforts to contain sewage and animal waste, and to control soil erosion and sedimentation, result in better overall water quality.

  - Applicable Minnesota Water Quality Standards

Minnesota Rules Chapter 7050 provides the water quality standards for bacterial concentrations in Minnesota waters. The rules are as follows for class 2B surface waters, which include all of the impaired reaches covered in this report.

3.2.1 Class 2B waters

The quality of Class 2B surface waters shall be such as to permit the propagation and maintenance of a healthy community of cool or warm water sport or commercial fish and associated aquatic life, and their habitats. These waters shall be suitable for aquatic recreation of all kinds, including bathing, for which the waters may be usable.

Fecal coliform organisms not to exceed 200 organisms per 100 milliliters as a geometric mean of not less than five samples in any calendar month, nor shall more than ten percent of all samples taken during any calendar month individually exceed 2000 organisms per 100 milliliters. The standard applies only between April 1 and October 31.

Table 3.2.1 summarizes the fecal coliform bacteria standards for all classes of water in Minnesota.

Table 3.2.1 – Minnesota Surface Water Standards for Fecal Coliform Bacteria

  - Impairment Assessment:  Fecal Coliform Impairments

Preliminary monitoring of fecal coliform bacteria was conducted in the late 1990’s by the MPCA and Sibley County to determine levels of contamination in the both watersheds. The monitoring data revealed elevated fecal coliform concentrations across the watersheds and the need for thorough diagnostic watershed studies. This led to the High Island Assessment Project (2000-2003) and Rush River Assessment Project (2003-2004) CWPs. These studies involved the monitoring at several stream locations for sediment, nutrients and fecal coliform bacteria. Bacterial monitoring of these watersheds continued in 2005 as part of the HIRR Fecal Coliform TMDL. As of fall 2005, 720 samples had been collected at the ten HICR/RRW monitoring sites. Prior to these projects little water quality data exists for these watersheds. Figure 3.3 displays the location of diagnostic study monitoring sites.

Figure 3.3a – Fecal Coliform Bacteria Monitoring Sites in HICW and RRW

Table 3.3 presents a summary of fecal coliform data collected between 1998 through 2005. The data show elevated fecal coliform concentrations across both watersheds. As of fall 2007, High Island Creek (sites 2P, 3P, 5P and 10P), Buffalo Creek (8P and 9P) and the Rush River (sites 1RP and 4RP) all have segments listed as impaired on the 303(d) list.

Table 3.3 – Stream Monitoring Sites and Impairment Assessment Data (1998-2005 data)

Figures 3.3b and 3.3c present monthly geometric mean values for each HIRR monitoring site based on data collected between 1998 through 2005.

Figure 3.3b – Rush River Monthly Fecal Coliform GMs (1998-2005 data)

Figure 3.3c – High Island Creek Monthly Fecal Coliform GMs (1998-2005 data)

  - Fecal Coliform and Flow

There is a significant relationship between flow and fecal coliform concentration in both watersheds. On average, as flows increase fecal coliform bacteria concentration also increase. This relationship is evident by charting flow and bacterial concentrations using a method called the duration curve. The duration curve method involves obtaining average daily flow values for a stream monitoring site over its entire record. For High Island Creek this period extends from 1973 through 2005 for a total of over 10,700 data points. Next, the daily flow values are sorted from maximum to minimum flow and plotted on a chart. Figure 3.4a displays the flow duration curve for the High Island Creek outlet monitoring site. The chart depicts the percentage of time any particular flow is exceeded. For example, 330 CFS has only been exceeded by 10% of daily flow values, and thus is considered the beginning of the “high flow” category. A value of 2 CFS was exceeded by 90% of daily flow values and represents “low flow” conditions.

Figure 3.4a – Flow Duration Curve for High Island Creek, near Henderson

Next, samples that have been collected over the flow record are plotted on the flow duration curve. Daily flow values are multiplied by the surface water quality standard of 200 cfu/100 ml for fecal coliform bacteria. Samples are plotted by multiplying the daily mean flow of the sample date by the sample concentration. The 123 samples collected from High Island Creek (Site 10P) from 1998 through 2005 are plotted on the chart, resulting in a “Load Duration Curve”. This method is useful for determining the frequency and severity of surface water quality standard exceedances during varying flow conditions.

Chart 3.4b shows that 90% of samples (36 of 40) collected from High Island Creek at flows above 280 CFS exceeded 200 cfu/100 ml. The geometric mean of these high flow samples was 1,889 cfu/100 ml. In contrast, only 50% of samples collected during “dry conditions exceeded 200 cfu/100 ml, with a much lower geometric mean of 160 cfu/100 ml.

Figure 3.4b – Load Duration Curve for High Island Creek, near Henderson

Table 3.4 provides statistics relating fecal coliform concentration and flow conditions. The data indicate the majority of bacterial load that moves through these systems occurs during high flow conditions.

Table 3.4 – Fecal Coliform Statistics by Flow Condition

  - Fecal Coliform and Total Suspended Solids

A second significant relationship is between fecal coliform concentrations and total suspended solid concentrations. Figure 3.5 displays the High Island Creek outlet load duration curve with samples above 100 mg/L TSS drawn out. The value of 100 mg/L was chosen as water samples testing above this threshold are usually deriving much of the flow from stormwater. At concentrations above 100 mg/L, significant erosion is occurring from overland, streambank and gully erosion.

Figure 3.5 – TSS Load Duration Curve for High Island Creek, near Henderson

Tables 3.5a and 3.5b present statistics relating fecal coliform bacteria and TSS for the High Island Creek and Rush River outlet sites. As total suspended solids increase bacterial concentrations also increase.

This data show there is a strong relationship of bacterial transport and soil erosion. Thus, best management practices that reduce soil erosion will often reduce bacterial transport to streams. The data may also indicate in channel resuspension of streambed sediments that are laden with fecal coliform bacteria as a potential source (as discussed in section 2.6).

Table 3.5a – High Island Creek Outlet – FC vs. TSS Statistics

Table 3.5b – Rush River Outlet – FC vs. TSS Statistics

  - Geographic Scope of Impairment

Every stream reach in the HICW and RRW with adequate monitoring data qualifies to be listed as impaired for fecal coliform bacteria. Furthermore, these sites greatly exceed recommended water quality standards during the summer and fall months.

  - Seasonality

Tables 3.7a and 3.7b provide monthly fecal coliform bacteria statistics for High Island Creek and Rush River outlets monitoring sites. Monitoring data show a clear relationship between season and fecal coliform bacteria concentration. Typically the highest bacterial concentrations are found in June through September. April is usually the monitoring month with the lowest bacteria concentrations, despite the fact that significant manure application occurs during this time and that fields have little crop canopy to protect against water erosion. The lower FC concentrations in August are explained by lack of flow, as both HIC and RR are usually at nearly no flow condition. During these dry periods, groundwater is often the only source of flow and fecal coliform concentrations are much lower.

Table 3.7a – High Island Creek Outlet FC Statistics by Month

Table 3.7b - Rush River Outlet FC Statistics by Month

The apparent seasonality of fecal coliform bacteria concentrations appears to be associated strongly with stream water temperature. Seasonal changes in landuse, such as timing of manure application, appear to have little correlation with seasonality of bacterial concentrations. Fecal coliform bacteria are the most productive at temperatures similar to their origination environment in animal intestines. Therefore fecal coliform bacteria are at their highest concentrations during warmer temperatures, possibly due to reproduction in numbers. However, at lower temperatures it is probable the metabolism of organisms slow, therefore prolonging their existence (Chapelle, 2001; Cullimore, 1993). Thus, while bacterial concentrations may be lower during colder periods, survival rates are increased.

As part of the HICW and RRW CWP diagnostic studies, stream water temperature monitoring was not conducted. However, monitoring projects conducted by the WRC near these watersheds have shown the relationship of bacteria and stream temperature. Figure 3.7 provides an example of this association at the Beauford Creek Watershed (10 miles south of Mankato, Minnesota). The figure displays the percentage of baseflow samples that exceeded the surface water standard of 200 cfu/100 ml based on stream temperature classification. The data set included 76 samples collected during the 2000, 2004, and 2005 monitoring seasons and excluded all samples collected within 48 hours of greater than 0.5 inches of precipitation. The data show a significant association between stream temperature and fecal coliform bacteria concentration. The higher bacterial concentrations during the warm summer/fall months may also be associated with greater nutrient and algae concentrations at that time of year. Nutrients and algae may support bacterial growth and therefore temperature may be a secondary factor.

Figure 3.7 – Beauford Creek – Fecal Coliform vs. Stream Temperature

  - Trends in Fecal Coliform Surface Water Quality

It is not possible to assess trends in bacterial concentrations as monitoring data only exists since the late 1990’s.

  - TMDL Endpoints

TMDL endpoints will meet the 200 organism/100 ml “chronic” standard and 2000 “acute” standard for fecal coliform bacteria. Section 4.0 outlines the process used to determine monthly and daily TMDL allocations for each of the impaired streams. This process involved using long term flow data from three USGS flow gauging stations and incorporating the two numeric water quality standards for fecal coliform bacteria.

The first numerical standard is that streams will have a monthly geometric mean below 200 org/100 ml. This standard was incorporated to calculate the monthly loading capacity and allocations. The second numerical standard is that no more than 10% of samples may exceed 2000 org/100 ml and was used to calculate the daily loading capacity and allocations. Daily loading capacity and allocations were determined as 1/3rd the monthly loading capacity and allocations. This relates to the 2000 numerical standard being a factor of 10 times the 200 numerical standard. Neither the monthly or daily loading capacities (nor individual allocations) may be exceeded.

Section 4.0 – Explanation of Load Allocations (LA)

Wasteload Allocations (WLA) and Margin of Safety (MOS)

The following section provides background information, water quality data and load/wasteload allocations for the seven impaired stream reaches. The TMDL assessment process was modeled after the approach used in the Regional Total Maximum Daily Load Evaluation of Fecal Coliform Bacteria Impairment in the Lower Mississippi River Basin in Minnesota, (MPCA, 2006).

The TMDLs consist of three components; WLA, LA and MOS as defined in section 1.2 on page 2. The WLA includes three subcategories: permitted wastewater treatment facilities; livestock facilities requiring NPDES permits, and “straight pipe” septic systems. The LA, reported as a single category includes manure runoff from farm fields, pastures, and smaller non-NPDES-permitted feedlots, runoff from non-MS4 communities, and fecal coliform bacteria contributions from wildlife. The LA includes land-applied manure from livestock facilities requiring NPDES permits, provided the manure is applied in accordance with a permit. The third component, MOS, is the part of the allocation that accounts for uncertainty that the allocations will result in attainment of water quality standards.

The three components were calculated as monthly loads of fecal coliform organisms. The fecal coliform load limits were calculated for five flow regimes, from near drought to flood condition. This method is referred to as the duration curve approach.  By adjusting the WLA, LA and MOS to a range of five discrete flow intervals at each reach, a closer correspondence is obtained between the flow-specific loading capacity and the TMDL components at the range of flow conditions experienced historically at each site.

The duration curve approach involved using long term (1973-2005) flow monitoring data from the High Island Creek outlet USGS gaging site. Monthly mean flow values were obtained for April through October, from 1973 through 2005. The April through October period was selected as this corresponds with the fecal coliform standard. Table 4.0a presents the USGS monthly flow values for High Island gaging site.

Table 4.0a – High Island Creek, Monthly Mean Flow Values, CFS (1973-2005)

The resulting 224 monthly flow values were then sorted by flow volume, from highest to lowest to develop a flow duration curve (similar to the “daily” flow duration curve described in section 3.4). Figure 4.0a displays the flow duration curve for the High Island Creek outlet monitoring site. The chart depicts the percentage of time any particular flow is exceeded. For example, during the flow record 366 CFS was exceeded by 10% of monthly flow values, and thus represents “high flow” conditions. A value of 3 CFS was exceeded by 90% of monthly flow values and represents “low flow” conditions.

Figure 4.0a – High Island Creek Flow Duration Curve (based on mean monthly flows)

Flow regimes were determined for high flow, moist, mid-range, dry, and low flow conditions. The mid-range flow value for each flow regime was then used to calculate the total monthly loading capacity (TMLC). Thus, for the “high flow” regime, the loading capacity is based on the monthly flow value at the 5th percentile. At this flow value, the mean monthly flow would be exceeded by 5% of all flow values in the dataset. Table 4.0b presents the flow regimes that were determined for the High Island Creek gaging site, along with the flow value used to calculate the TMLC.

Table 4.0b – Flow Regimes and Values Used to Calculate Total Monthly Loading Capacity

The flow used to determine loading capacity for each flow regime was multiplied by a conversion factor of 146,776,126,400. This conversion factor is defined by the following equation:

Load Capacity (org/month) = Concentration (org/100mL) X Flow (cfs) X (200 cfu/100ml)

Multiply by 3,785.2 to convert mL per gallon to cfu/100 gallons

Divide by 100 to convert to cfu/gallon

Multiply by 7.48 to convert gallon per ft3 to org/ft3

Multiply by 86,400 to convert seconds per day to ft3/day

Multiply by 30 to convert day per month to ft3/month

Multiply by the water quality standard of 200 cfu/100 ml

Load Capacity (cfu/month) = 733,880,632 X Flow

Next, a Margin of Safety was determined for each flow regime. The purpose of the MOS is to account for uncertainty that the allocations will result in attainment of water quality standards. Because the allocations are a direct function of monthly flow, accounting for potential flow variability is the appropriate way to address the MOS.  This is done within each of 5 flow zones. The MOS was determined as the difference between the median flow and minimum flow in each zone. For example, the MOS for the high flow zone is the 95th percentile flow value subtracted from the 100th percentile flow value. The resulting value was converted to a load and used as the MOS. The values that were used to calculate the TMLC and MOS are presented in figure 4.0b.

Figure 4.0b – High Island Creek Flow Duration Curve with TMLC and MOS

Table 4.0c presents the resulting TMDL Allocation (WLA+LA) and MOS for the High Island Creek outlet impaired reach based on the five flow regimes. The values expressed are in total organisms per month. For each of the five flow regimes, the monthly flow volume was multiplied by the water quality standard of 200 organisms/100 ml. This usually produces loading capacities in the trillions of organisms per month (T-org/month).

Table 4.0c – TMDL and MOS for High Island Creek

The remaining four HICW impaired stream reaches lack long term flow monitoring data.  Flow values for these impaired watersheds were calculated by normalizing data from the High Island Creek USGS gage station. For example, the Buffalo Creek impaired stream reach is approximately 11% of the watershed area monitored by the High Island Creek gaging station. To determine flow zones for the Buffalo Creek site, mean monthly flows were assumed to be 11% of the flow volumes at the High Island Creek outlet gaging station. These values were then checked against available flow data for Buffalo Creek (which had flow data for 2001, 2002, 2004 and 2005). Generally, normalized monthly flow values based the USGS sites were very close to actual monitored flows. The method was also used to estimate monthly mean values for the Rush River Watershed, which only had flow data for 2003-2005.

The TMDL is divided into WLA and LA components. A description of the process used to determine the WLA and LA is provided below. The process is taken directly from the Regional Lower Mississippi TMDL report:

WASTELOAD ALLOCATION

- Wastewater treatment facility (WWTF) allocations were calculated by multiplying wet-weather design flows for all facilities in an impaired reach watershed by the permitted discharge limit (200 organisms per 100ml) that applies to all WWTFs. As long as WWTFs discharge at or below this permit limit, they will not cause violations of the fecal coliform water quality standard regardless of their fecal coliform load.

- A number of smaller NPDES-permitted WWTF’s are stabilization ponds systems.  Unlike the larger (and some smaller) mechanical treatment systems which have continuous discharges, pond systems typically discharge over a 1-2 week period in the spring and in the fall. Because the discharge volumes from these pond systems are small, and to provide an extra margin of safety in the event they need to discharge outside of the spring or fall window, the WWTF wasteload allocation assumed that these facilities could discharge for an entire month under any flow conditions.

- Straight-pipe septic systems are illegal and un-permitted, and as such are assigned a zero wasteload allocation.

- Since wet-weather design flows represent a “maximum” flow for a facility, the WWTF allocations are conservative in that they are substantially greater than what is actually required.

- For the Rush River and High Island outlet impaired stream reaches WWTF design flow exceeded minimum stream flow for the low flow zone. Of course, actual WWTF flow can never exceed stream flow as it is a component of stream flow. To account for this unique situation, the wasteload and load allocations are expressed as an equation rather than an absolute number. That equation is simply:

Allocation = (flow contribution from a given source) X (200 orgs./100ml.)

In essence, this amounts to assigning a concentration-based limit to the nonpoint source load allocation sources. While this might be seen as overly stringent, these sources tend not to be significant contributors under dry and low flow conditions. The contribution of fecal coliform from straight-pipe septic systems could be substantial under these conditions; however these systems are still assigned a zero allocation, as are livestock facilities with NPDES permits.

- Livestock facilities that have been issued NPDES permits are assigned a zero wasteload allocation. This is consistent with the conditions of the permits, which allow no pollutant discharge from the livestock housing facilities and associated site. Discharge of fecal coliform from fields where manure has been land applied may occur at times. Such discharges are covered under the load allocation portion of the TMDLs, provided the manure is applied in accordance with the permit.

LOAD ALLOCATION

- Once the WLA and MOS were determined for a given reach and flow zone, the remaining loading capacity was considered load allocation. The load allocation includes nonpoint pollution sources that are not subject to NPDES permit requirements, as well as “natural background” sources such as wildlife. The nonpoint pollution sources are largely related to livestock production, inadequate human wastewater treatment, and municipal stormwater systems. Straight-pipe septic systems and communities covered by MS4 NPDES permits, are included in the wasteload allocation.

Daily Loading Capacity and Allocations

The TMDLs are expressed in both monthly and maximum daily terms. This is to ensure that both the monthly geometric mean and upper 10th percentile portions of the water quality standard are addressed. All maximum daily loading capacity and allocation values are set at 1/3 rd of the monthly loading capacity and allocation values based on the following rationale:

The upper 10th percentile criterion is 10 times the geometric mean criterion (2000 org ./ 100ml = upper 10th percentile; 200 org./100ml = geometric mean). Thus, assuming average daily loading capacities and allocations are 1/30th of the monthly values, 10 times the average daily values could be allocated as maximum daily loading capacities and allocations under the upper 10th percentile standard. In mathematical terms the maximum daily value = 10 x 1/30th of the monthly value = 10/30th or 1/3 rd of the monthly value.

It is important to note that neither the daily or monthly loading capacities should be violated. In conceptual terms, 3 days of bacteria loads that approach the maximum daily capacities will "use up" most of the monthly capacity.

Impacts of Growth on Allocations and Need for Reserve Capacity

As a result of population growth and movement, changes in the agricultural sector, and other land use changes in the HICW and RRW, sources and pathways of bacteria to surface waters will not remain constant over time. The potential impact of these changes on specific bacteria sources are discussed below.

Straight-Pipe Septic Systems

As a result of state and local rules, ordinances, and programs, the number of straight pipe septic systems will decrease over time. Because these systems constitute illegal discharges, they are not provided a load allocation for any of the impaired reaches covered in this report. As such, other elements of the TMDL allocation will not change as these systems are eliminated.

Wastewater Treatment Facilities

Flows at some wastewater treatment facilities are likely to increase over time with increases in the populations they serve. As long as current fecal coliform discharge limits are met at these facilities, however, such increases will not impact the allocation provided to other sources. This is because increased flows from wastewater treatment facilities add to the overall loading capacity by increasing river flows.

Livestock

Along with humans, the other major source of fecal coliform in the watersheds are livestock. While there have been changes in the sizes and types of facilities, there do not appear to be clear trends in overall livestock numbers. With changes in facility size and type, a continuing shift in focus from the facilities themselves to land application practices may be warranted in the future. If growth in livestock numbers does occur, newer regulations for facility location and construction, manure storage design, and land application practices should help mitigate potential increases in fecal coliform loading to the streams and rivers of the basin.

For the reasons discussed above, no explicit adjustments were made to the waste load or load allocations, and no reserve capacity was added, to account for human or livestock population growth. The MPCA will monitor population growth, urban expansion, and changes in agriculture, and reopen the TMDLs covered in this report if and when adjustments to allocations may be required.

Section 5.0 - TMDL Allocations for Individual Impaired Reaches

5.1  High Island Creek; Unnamed Creek to Minnesota River

This 28.9 mile reach of High Island Creek extends from the outlet of High Island Creek at the Minnesota River to upstream at the confluence with High Island Lake outlet. The stream reach was placed on the impaired waters list in 2006. The majority of monitoring conducted on this portion of the river was from 2000 through 2006 by the High Island Creek Clean Water Partnership. Figure 5.1 displays the impaired stream reach, the watershed, and location of the monitoring site where water quality data were collected.

Figure 5.1 – High Island Creek; Unnamed Creek to Minnesota River

The impaired reach watershed includes all of High Island Creek Watershed.  The watershed is 153,222 acres (239 square miles) in size and includes the communities of Arlington, New Auburn and a portion of Stewart. Wastewater from Arlington discharges into High Island Creek, ½ mile southeast of town (table 5.1a). New Auburn does not discharge treated wastewater as they utilize a spray irrigation system. The community of Stewart discharges wastewater outside the watershed. The watershed also includes five livestock facilities that have been issued NPDES permits (table 5.1b).

Table 5.1a - Wastewater Treatment Facilities

Table 5.1b - Livestock Facilities with NPDES Permits

Table 5.1c describes the monthly fecal coliform loading capacities, as well as the component wasteload allocations, load allocations and margin of safety for this reach of High Island Creek.

Table 5.1c - Monthly Fecal Coliform Loading Capacities and Allocations – High Island Creek; Unnamed Creek to Minnesota River

5.1.1 Water Quality Data and Required Reductions

The following reduction represents the percentage reduction in bacterial concentration that would be required to meet the 200 cfu/100 ml water quality standard. This reduction percentage is only intended as a rough approximation, as it does not account for flow. It serves to provide a starting point based on recent water quality data for assessing the magnitude of the reduction needed in the watershed to achieve the surface water standard. This reduction percentage does not supersede the allocations provided for the TMDL.

Table 5.1.1 – Required Fecal Coliform Reductions; Site 10P – High Island Creek Outlet

Month		Monthly GM (cfu/100ml)  	Required Reduction

April		218				8.3%

May		549				63.6%

June		1,996				90.0%

July		1,273				64.3%

August		180				None Required

September	2,563				92.2%

Figure 5.1.1 - Monthly Geometric Mean Fecal Coliform Concentrations (1996-2005)

5.2  High Island Creek; JD 15 to Unnamed Creek

This 17.6 mile reach of High Island Creek extends from confluence of High Island Lake outlet and High Island Creek upstream to the headwaters of High Island Creek. The stream reach was placed on the impaired waters list in 2002. The majority of monitoring conducted on this portion of the river was from 2000 through 2002 by the High Island Creek Clean Water Partnership. Monitoring during this period was conducted at two sites along the impaired reach. Figure 5.2 displays the impaired stream reach, the watershed, and location of monitoring sites where water quality data were collected.

Figure 5.2 - High Island Creek; JD 15 to Unnamed Creek

The impaired reach watershed includes the upper portion of High Island Creek watershed. The impaired watershed is 83,121 acres (130 square miles) and includes the south portion of the City of Stewart. Stewart discharges wastewater outside the watershed, thus no wasteload allocation is included in this TMDL. The watershed also includes two livestock facilities that have been issued NPDES permits (table 5.2b).

Table 5.2a - Wastewater Treatment Facilities

Table 5.2b - Livestock Facilities with NPDES Permits

Table 5.2c describes the monthly fecal coliform loading capacities, as well as the component wasteload allocations, load allocations and margin of safety for the impaired reach of High Island Creek.

Table 5.2c - Monthly Fecal Coliform Loading Capacities and Allocations – High Island Creek; JD 15 to Unnamed Creek

5.2.1 Water Quality Data and Required Reductions

The following reduction represents the percentage reduction in bacterial concentration that would be required to meet the 200 cfu/100 ml water quality standard. This reduction percentage is only intended as a rough approximation, as it does not account for flow. It serves to provide a starting point based on recent water quality data for assessing the magnitude of the reduction needed in the watershed to achieve the surface water standard. This reduction percentage does not supersede the allocations provided for the TMDL.

Table 5.2.1a - Required Fecal Coliform Reductions; Site 2P – Upstream Bakers Lake

Month		Monthly GM (cfu/100ml)  	Required Reduction

April		Inadequate Data		Inadequate Data

May		223				10.3%

June		943				78.1%

July		963				79.2%

August		Inadequate Data		Inadequate Data

September	Inadequate Data		Inadequate Data

Table 5.2.1b - Required Fecal Coliform Reductions; Site 3P – Downstream Bakers Lake

Month		Monthly GM (cfu/100ml)  	Required Reduction

April		Inadequate Data		Inadequate Data

May		85				None Required

June		560				64.3%

July		381				47.5%

August		Inadequate Data		Inadequate Data

September	Inadequate Data		Inadequate Data

Figure 5.2.1 - Monthly Geometric Mean Fecal Coliform Concentrations (1996-2005)

5.3  Buffalo Creek; Unnamed Creek to High Island Creek

This 6.8 mile reach of Buffalo Creek extends from the outlet at High Island Creek, upstream to the confluence of county ditch 59. The stream reach was placed on the impaired waters list in 2006. Water quality monitoring of this reach was conducted from 2000 through 2006 by the High Island Creek Clean Water Partnership. Figure 5.3 displays the impaired stream reach, the watershed, and location of the monitoring site where water quality data were collected.

Figure 5.3 - Buffalo Creek; Unnamed Creek to High Island Creek

The impaired reach includes the entire Buffalo Creek watershed.  The impaired watershed is 18,003 acres (28 square miles). The watershed contains no cities and thus no wasteload allocation is included in the TMDL. The watershed also includes three livestock facilities that have been issued NPDES permits (table 5.3b).

Table 5.3a - Wastewater Treatment Facilities

Table 5.3b - Livestock Facilities with NPDES Permits

Table 5.3c describes the monthly fecal coliform loading capacities, as well as the component wasteload allocations, load allocations and margin of safety for this reach of Buffalo Creek.

Table 5.3c - Monthly Fecal Coliform Loading Capacities and Allocations – Buffalo Creek; Unnamed Creek to High Island Creek

5.3.1 Water Quality Data and Required Reductions

The following reduction represents the percentage reduction in bacterial concentration that would be required to meet the 200 cfu/100 ml water quality standard. This reduction percentage is only intended as a rough approximation, as it does not account for flow. It serves to provide a starting point based on recent water quality data for assessing the magnitude of the reduction needed in the watershed to achieve the surface water standard. This reduction percentage does not supersede the allocations provided for the TMDL.

Table 5.3.1 – Required Fecal Coliform Reductions; Site 9P – Buffalo Creek Outlet

Month		Monthly GM (cfu/100ml)  	Required Reduction

April		100				None Required

May		354				43.5%

June		1,938				89.7%

July		1,461				86.3%

August		263				24.0%

September	1,060				81.1%

Figure 5.3.1 - Monthly Geometric Mean Fecal Coliform Concentrations (1996-2005)

5.4  Buffalo Creek; High Island Ditch 5 to Unnamed Stream

This 3.2 mile reach of Buffalo Creek extends from county ditch 59 upstream to the confluence with High Island Ditch 5. The stream reach was placed on the impaired waters list in 2006. Monitoring was conducted on this impaired reach in 2001 and 2002 by the High Island Creek Clean Water Partnership. Figure 5.4 displays the impaired stream reach, the watershed, and location of the monitoring site where the water quality data were collected.

Figure 5.4 - Buffalo Creek; High Island Ditch 5 to Unnamed Stream

The impaired reach encompasses the upper portion Buffalo Creek watershed. The impaired reach watershed is estimated to be 12,350 acres (19 square miles). The watershed contains no cities and thus no wasteload allocation is included in the TMDL. The watershed also includes two livestock facilities that have been issued NPDES permits (table 5.4b).

Table 5.4a - Wastewater Treatment Facilities

Table 5.4b - Livestock Facilities with NPDES Permits

Table 5.4c describes the monthly fecal coliform loading capacities, as well as the component wasteload allocations, load allocations and margin of safety for this reach of Buffalo Creek.

Table 5.4c - Monthly Fecal Coliform Loading Capacities and Allocations – Buffalo Creek; High Island Ditch 5 to Unnamed Stream

5.4.1  Water Quality Data and Required Reductions

The following reduction represents the percentage reduction in bacterial concentration that would be required to meet the 200 cfu/100 ml water quality standard. This reduction percentage is only intended as a rough approximation, as it does not account for flow. It serves to provide a starting point based on recent water quality data for assessing the magnitude of the reduction needed in the watershed to achieve the surface water standard. This reduction percentage does not supersede the allocations provided for the TMDL.

Table 5.4.1 – Required Fecal Coliform Reductions; County Ditch 59 (Upper Buffalo Creek)

Month		Monthly GM (cfu/100ml)  	Required Reduction

April		Inadequate Data		Inadequate Data

May		243				17.7%

June		2,369				91.6%

July		1,299				84.6%

August		Inadequate Data		Inadequate Data

September	Inadequate Data		Inadequate Data

Figure 5.4.1 - Monthly Geometric Mean Fecal Coliform Concentrations (1996-2005)

5.5  Rush River; South Branch Rush River to Minnesota River

This 8.1 mile reach of Rush River extends from the Minnesota River upstream to the rivers confluence with the South Branch Rush River. The stream reach was placed on the impaired waters list in 2002. Monitoring of this portion of the river was conducted in 1998 and 1999 by the MPCA and 2003 through 2006 by the Rush River Clean Water Partnership. Figure 5.5 displays the impaired stream reach, the watershed, and location of the monitoring site where the water quality data were collected.

Figure 5.5 - Rush River; South Branch Rush River to Minnesota River

The impaired reach includes the entire Rush River Watershed, which is 257,775 acres (403 square miles). The watershed contains communities of Gaylord, Gibbon, Lafayette and Winthrop (table 5.5a), all of which discharge treated wastewater within the impaired watershed. The watershed also contains two unincorporated Hutterian Colonies, Starland and Altona, that have permitted waste water treatment facilities that discharge within the watershed. Lastly, MG Waldbaums, a large poultry processing plant located near Gaylord also has their own WWTP that discharges to the north Branch Rush River. The watershed includes 12 livestock facilities that have been issued NPDES permits (table 5.5b).

Table 5.5a - Wastewater Treatment Facilities

Table 5.5b - Livestock Facilities with NPDES Permits

Table 5.5c describes the monthly fecal coliform loading capacities, as well as the component wasteload allocations, load allocations and margin of safety for this reach of Rush River.

Table 5.5c - Monthly Fecal Coliform Loading Capacities and Allocations – Rush River; South Branch Rush River to Minnesota River

5.5.1 Water Quality Data and Required Reductions

The following reduction represents the percentage reduction in bacterial concentration that would be required to meet the 200 cfu/100 ml water quality standard. This reduction percentage is only intended as a rough approximation, as it does not account for flow. It serves to provide a starting point based on recent water quality data for assessing the magnitude of the reduction needed in the watershed to achieve the surface water standard. This reduction percentage does not supersede the allocations provided for the TMDL.

Table 5.5.1 – Required Fecal Coliform Reductions; Site 1RP – Rush River Outlet

Month		Monthly GM (cfu/100ml)  	Required Reduction

April		216				7.4%

May		438				54.3%

June		855				76.6%

July		937				78.7%

August		428				53.3%

September	1,018				80.4%

Figure 5.5.1 - Monthly Geometric Mean Fecal Coliform Concentrations (1996-2005)

5.6  Rush River, South Branch; Unnamed Ditch to Rush River

This 32.6 mile reach of Rush River extends from the confluence of the mainstem and South Branch Rush River to the headwaters of the South Branch Rush River. The stream reach was placed on the impaired waters list in 2008. Monitoring of this portion of the river was conducted in 1998 by the MPCA and 2003 through 2006 by the Rush River Clean Water Partnership. Figure 5.6 displays the impaired stream reach, the watershed, and location of the monitoring site where the water quality data were collected.

Figure 5.6 - Rush River, South Branch; Unnamed Ditch to Rush River

The impaired reach watershed includes 117,918 acres (184 square miles) in the southern Sibley and northern Nicollet counties. The watershed contains communities of Lafayette and southern portion of Gibbon (table 5.6a), both of which discharge treated wastewater within the impaired watershed. The watershed includes 10 livestock facilities that have been issued NPDES permits (table 5.6b).

Table 5.6a - Wastewater Treatment Facilities

Table 5.6b - Livestock Facilities with NPDES Permits

Table 5.6c describes the monthly fecal coliform loading capacities, as well as the component wasteload allocations, load allocations and margin of safety for this reach of Rush River.

Table 5.6c - Monthly Fecal Coliform Loading Capacities and Allocations – Rush River, South Branch; Unnamed Ditch to Rush River

5.6.1 Water Quality Data and Required Reductions

The following reduction represents the percentage reduction in bacterial concentration that would be required to meet the 200 cfu/100 ml water quality standard. This reduction percentage is only intended as a rough approximation, as it does not account for flow. It serves to provide a starting point based on recent water quality data for assessing the magnitude of the reduction needed in the watershed to achieve the surface water standard. This reduction percentage does not supersede the allocations provided for the TMDL.

Table 5.6.1 – Required Fecal Coliform Reductions; Site 4RP – South Branch Rush River

Month		Monthly GM (cfu/100ml)  	Required Reduction

April		231				13.4%

May		558				64.2%

June		758				73.6%

July		716				71.1%

August		1,130				82.3%

September	3,584				94.4%

Figure 5.6.1 - Monthly Geometric Mean Fecal Coliform Concentrations (1996-2005)

5.7  High Island Ditch 2, Unnamed Creek to High Island Creek

This 1.9 mile impaired reach is a watershed district ditch system that outlets into High Island Creek, ½ mile north of Arlington. The stream reach was placed on the impaired waters list in 2008. Monitoring of this portion of the river was conducted in 1999 by the MPCA and 2000 and 2001 by the High Island Creek Clean Water Partnership. Figure 5.7 displays the impaired stream reach, the watershed, and location of the monitoring site where the water quality data were collected.

Figure 5.7 - High Island Ditch 2, Unnamed Creek to High Island Creek

The impaired reach watershed includes 10,517 acres (16 square miles) in north Sibley County. The ditch watershed contains no communities and thus no wasteload allocations are provided in the TMDL. (This watershed also contains no livestock facilities with NPDES permits).

Table 5.7a - Wastewater Treatment Facilities

Table 5.7b - Livestock Facilities with NPDES Permits

Table 5.7c describes the monthly fecal coliform loading capacities, as well as the component wasteload allocations, load allocations and margin of safety for this impaired reach.

Table 5.7c - Monthly Fecal Coliform Loading Capacities and Allocations – High Island Ditch 2, Unnamed Creek to High Island Creek

5.7.1 Water Quality Data and Required Reductions

The following reduction represents the percentage reduction in bacterial concentration that would be required to meet the 200 cfu/100 ml water quality standard. This reduction percentage is only intended as a rough approximation, as it does not account for flow.  It serves to provide a starting point based on recent water quality data for assessing the magnitude of the reduction needed in the watershed to achieve the surface water standard. This reduction percentage does not supersede the allocations provided for the TMDL.

Table 5.7.1 – Required Fecal Coliform Reductions; Site 6S – High Island Ditch #2

Month		Monthly GM (cfu/100ml)  	Required Reduction

April		Inadequate Data		Inadequate Data

May		Inadequate Data		Inadequate Data

June		957				79.1%

July		885				77.4%

August		692				71.1%

September	Inadequate Data		Inadequate Data

Figure 5.7.1 - Monthly Geometric Mean Fecal Coliform Concentrations (1996-2005)

Section 6.0 – Margin of Safety

The margin of safety is established to account for uncertainty that the load and wasteload allocations will result in attainment of water quality standards. The MOS in TMDLs usually includes "implicit" and "explicit" components. The implicit MOS includes conservative approaches to sampling and conservative assumptions made during load calculation. The explicit MOS takes into account a lack of knowledge concerning flow limitations and water quality. An explicit MOS is incorporated by setting aside a portion of the TMDL as the MOS.

The margin of safety for the five TMDL reaches were the difference between the calculated loading capacity at the mid-point of each flow regime and the minimum flow in each zone. This method insures that allocations will not exceed the load associated with the minimum flow in each zone. As load is directly related to flow (conc. X flow = load), a MOS that varies by flow is the appropriate approach.

Section 7.0 – Monitoring Plan

Continued bacterial monitoring will be needed in HICW and RRW to assess if reductions in fecal contamination are being achieved. This monitoring will rely on the current phase HICW and RRW Phase II Implementation CWP projects. These projects focus efforts on implementing best management practices that will improve surface water quality. The projects also involve surface water monitoring to assess how BMP implementation is impacting water quality. This monitoring includes fecal coliform bacteria and/or E. coli bacteria. HICW CWP is funding through 2009 and RRW CWP through 2008. Monitoring after the end of these projects will be dependant on future funding.

Section 8.0 –Bacteria Source Assessment and Implementation Activities

The purpose of the bacteria source assessment work conducted for this project is to suggest the most reasonable bacteria reduction activities on which to focus. The source assessment is not directly related to the total maximum loading capacities and allocations, which are simply a function of the water quality standards, stream flow (i.e. dilution capacity), and NPDES permit limits for point sources. The authors of this report acknowledge substantial uncertainty associated with source identification.

8.1  Source Assessment-Humans

Human waste can be a significant source of fecal coliform contamination during low flow periods. Contamination from individual sewage treatments systems that are not functioning properly can allow untreated or partially treated sewage into waterways.  Emergency bypasses from wastewater treatment facilities are an occasional source of bacteria and pollutants. A high priority should be placed on preventing human waste from entering waterways, as human pathogens are often found to be highly communicable.

    - Human Populations

The 2000 census data indicate HICW has a population of 5,351 and RRW a population of 9,010. Table 8.1.1a presents population statistics for both watersheds. Table 8.1.1b presents estimated populations for each city based on 2000 census figures.

Table 8.1.1a – Population Statistics for HICW and RRW

HICW contains three cities, Arlington, New Auburn and a portion of Stewart.  RRW encompasses four communities, Gaylord, Winthrop, Gibbon and Lafayette.

Table 8.1.1b – City Populations for HICW and RRW

HICW has 10.5 and RRW 10.0 persons per square mile living in rural areas. Arlington Township, which splits the western half of both watersheds has the highest rural population density at 14.8 persons per square mile. In general, the western portions of both watersheds have lower rural population densities than the eastern townships.

8.1.2 Noncompliant Individual Sewage Treatment Systems (ISTS)

An estimated 53% of Individual Sewage Treatment Systems (ISTS) in HICW and 55% of ISTS in RRW are allowing inadequately treated wastewater into waterways. These systems are often connected directly into county tile drainage which outlet into the nearest ditch or stream.  These systems are often called “straight pipe” systems. Under Minnesota statutes, a straight pipe discharge that has no soil treatment is an “imminent threat to public health or safety” (ITPHS) and when discovered, must be upgraded to acceptable standards within ten months.

There are an estimated 533 “straight pipe” systems in HICW and 880 systems in RRW. These estimates are highly subjective however, as the method of inventorying varies from one county to the next. The estimates were obtained from county Environmental Services offices, which often have varying methods of determining the number of ITPHS systems. Tables 8.1.2a and 8.1.2b present statistics on the estimated number of ITPHS septic systems in both watersheds.

Table 8.1.2a – High Island Creek Watershed IPHT Estimates

Table 8.1.2b – Rush River Watershed IPHT Estimates

Sewage from these systems are a significant contributor to fecal coliform bacteria in streams, especially during low flow conditions. These systems are illegal, un-permitted systems pursuant to Minnesota Rules Chapter 7080.

8.1.3 Unsewered Communities

There are no unsewered communities in either HICW or RRW.

8.1.4 MS4 Communities – Stormwater

Pursuant to the TMDL allocation process, cities with populations greater than 5000 are to be provided a wasteload allocation for stormwater discharges. The communities are required to have MS4 stormwater permits. However, there are no MS4 communities in either HICW or RRW.

8.1.5 Municipal Waste Water Treatment Facility Bypasses

Municipal bypasses are emergency discharges of partially or untreated human sewage from waste water treatment facilities. Municipal bypasses usually occur during periods of heavy precipitation, when waste water treatment facilities become overloaded.

Municipal bypasses typically last from a few hours to a few days. Table 8.1.5 provides the city and date of bypasses that have occurred from 2000 through 2004.

Table 8.1.5 – WWTP Bypasses in HICW and RRW by Year (2000-2004)

8.1.6 Municipal Wastewater Treatment Facility Violations

Municipal wastewater treatment facilities (WWTF) are required to test fecal coliform bacteria levels in effluent on a weekly basis. Facilities report a geometric mean fecal coliform level for each month, April through October. The geometric mean for all samples collected in a month must not exceed 200 cfu/100 ml fecal coliform bacteria.  Exceedance of the 200 cfu/100 limit is considered a WWTF violation.

According to MPCA records no wastewater treatment facility violations for fecal coliform bacteria were reported from 2001 through 2005.

8.1.7 Application of Sewage Sludge to Agricultural Lands

WWTP and sewage disposal contractors are required to properly treat and disinfect sludge and septage through processing or lime stabilization. Treated sewage is then usually disposed of onto agricultural lands. The rules and procedures related to sewage handling and application are intended to insure pathogens have been destroyed.

  - Source Assessment - Livestock

Runoff from land application areas, pastures and livestock feedlots has the potential to be a significant source of fecal coliform bacteria and other pollutants. Based on population inventories and the assessment procedures outlined in section 8.5.1, nearly 99% of the fecal matter produced (not what is delivered to waterways) in HICW and RRW is from livestock manure. Of the fecal matter produced by livestock, over 97% is applied to cropland as a fertilizer. In HICW an estimated 65% is incorporated manure and 31% is surface applied manure. In RRW an estimated 74% of livestock manure is incorporated and 24% surface applied. In both watersheds an estimated 2% of livestock manure remains in feedlots or stockpiles without runoff controls. Information on how manure application values were derived is available in section 8.5.1.

Based on county feedlot inventories, there are an estimated 261 feedlots in HICW with 24,848 animal units. RRW has an estimated 502 feedlots with 78,596 animal units.  Swine are the dominate animal type in both watersheds, followed by beef and dairy operations. Table 8.2 provides livestock statistics for both watersheds.

Table 8.2 – HICW and RRW Livestock Statistics

Figure 8.2a displays the location of inventoried feedlots in the both watersheds. The majority of these facilities are confined operations with little runoff to surface water. However, there are a number of open feedlots, some of which have pollution problems and pose a risk of fecal contamination. In portions of the watersheds runoff from these feedlots may be a significant source of fecal coliform contamination during periods of heavy precipitation. According to county feedlot officers and MPCA reports, most feedlots store and manage manure adequately to avoid runoff problems.

Figure 8.2a – HICW and RRW Livestock Feedlots (2004)

As part of the feedlot inventory process counties require feedlot operators to keep records on the location and amount of manure applied to agricultural land. For Sibley County this information was mapped in year 2000 to show locations of potential manure spread land. The Sibley County inventory and those from neighboring counties indicate roughly 25% of the total land area in the HIRR watersheds is available as manure spread land.

Figure 8.2b presents potential manure spread lands in Sibley County based on the 2000 manure spread inventory.

Figure 8.2b  - Potential Manure Spread Land in Sibley County

As applied manure is the primary source of fecal material produced in the HICW and RRW, it also has the potential as being a major source of contamination to waterways. There are three potential pathways of fecal coliform transport from fields with applied manure to waterways; 1) overland runoff, 2) open tile intakes and 3) macropores/preferential flow.

    - Overland Runoff and Open Tile Intakes

During storm events runoff of fecal coliform bacteria from fields with applied manure can occur by direct surface runoff to waterways or indirectly through field tile open intakes. To help address manure runoff concerns, manure application rules were put into place in Minnesota under state rule 7020 (table 8.2.1). This rule requires a setback of 300 feet for surface applied manure from streams, ditches and open tile intakes. The setback of manure application for incorporated fields is 25 feet from streams and ditches and 0 feet from open intakes. The Minnesota statutes represent the minimum setbacks for manure. Counties may develop ordinance with setback rules that are more restrictive. Of counties that are part of the HICW and RRW, only McLeod County has setbacks that are more restrictive than the Minnesota statutes.

Setbacks for field applied manure reduce the movement of manure solids, which in turn reduces bacterial transport to surface waters. The effectiveness of current setbacks for applied manure related to bacterial contamination is largely unknown. Setback distances are primarily based on research involving nutrients (phosphorus), not bacterial transport.  It is unclear whether current setbacks for surface applied and incorporated manure are appropriate for preventing bacterial transport to tile drainage systems. According to county and state feedlot officers, it is also difficult to monitor whether setback distance are being observed. As open intakes have the capacity of being a significant route for bacteria transport, further research into setback distances is recommended.

Table 8.2.1 - Manure Application Rules for Minnesota

8.2.2  Macropores/Preferential Flow

Transport of fecal coliform bacteria and associated pathogens may be enhanced by field tile systems. The retardation and retention of bacteria in soils is apparently less effective than previously believed, primarily due to preferential flow processes, which can aid in the rapid transport of bacteria from manure application (Smith et al, 1998; Geohring et al, 1999). Field studies in various locations across the United States have shown significant transport of fecal coliform bacteria to tile drainage through soil macropores. Beven and Germann (1982) outlined the main processes which contribute to the formation of macropores in natural soils:

- Pores formed by soil fauna such as earthworms, insects, mole and gophers.

- Crack and fissures formed during the shrinkage of clay soils and freeze/thaw cycles.

- Pores formed by plant roots.

- Natural soil pipes that form due to erosive action of subsurface flows.

In Minnesota there has been limited research on macropores and bacterial transport.  Earthworms, which are one of the primary creators of macropores, are in lower numbers in Minnesota compared with other portions of the country. Research has shown earthworm macropores are most common in no-till soils, not commonly utilized in south-central Minnesota. Also, soil types/conditions and climate may be different in Minnesota as compared to where other studies have taken place.

The only significant research in Minnesota related to assessing fecal coliform transport to tile drainage was two separate studies conducted by Gyles Randall at the University of Minnesota Southern Experiment Station in Waseca. The first study (Randall, 2000) conducted from 1995-1997 involved collection of tile water samples from a series of 13.5 by 15 meter plots that had received moldboard incorporation of fall applied dairy manure. The following spring samples were collected within three days of precipitation events that caused significant drainage. The study found 100% of samples to test positive for fecal coliform bacteria, yet e. coli was only detected in five of the 30 samples over the three year period. Fecal coliform concentrations were implied to be low and the authors speculated that significant winter die-off may have occurred.

The second study, (Randall, 2003) involved spring tile monitoring of fall applied (2002/2003) injected swine manure. The study involved comparing field plots with applied manure vs. urea treatments. The authors found the number of fecal coliform bacteria to be similar in both urea-treated and manure treated plots. They suggested organisms did not survive over winter in the added manure and that levels seen during the six-week drainage sampling period were probably background concentrations.

Studies from other parts of the country have shown that the transport of fecal bacteria under conditions of ideal matrix flow is inversely related to particle size. Soil consisting of primarily silt and clay particles are very effective in physically filtering bacterial cells under conditions of matrix flow. However, column and field experiments have indicated that macropore flow is the dominant transport pathway for fecal bacteria. Therefore, soils more susceptible to shrinking or cracking, such as clays, could be less effective than sandy soils in terms of limiting bacterial transport (Jamieson, 2002).

Research by Dan Janyes (USDA) at the National Soil Tilth Laboratory in Aims, Iowa has looked at movement of tracers, similar to nitrate, through preferential flow. Four tracers were surface applied to a field at staggered time intervals. The area of tracer application was then lightly irrigated (3mm/hr) and the subsurface tile was monitored for preferential flow. Tracer movement from surface to tile line varied from 2 hours to 15 minutes, occurring quicker as soil conditions became wetter. Janyes estimates preferential flow accounts for about 1% of the mass loss of surface applied chemicals.

Work by the Agricultural Resource Service (USDA) Martin Shipitalo in Ohio have traced macropores made by earth worms from the surface to 4 feet deep. In many cases, these burrows end at a drain tile. Shipitalo and Frank Gibbs of Natural Resources Conservation Service (NRCS) in Ohio have demonstrated the connectivity of the soil surface and tile line via macropores by forcing smoke up tile lines when not flowing.

Fecal coliform bacteria can survive for long periods of time in soils under certain conditions. Gerba et al. (1975) reported survival times of fecal-associated bacteria in soils to range from 2 to 4 months. The survivability of fecal bacteria in soil is largely dependant on moisture, soil type, temperature, pH, and nutrient availability. Crane et al. (1981), Zhai et al. (1995) found manure application rate does not appear to influence bacterial survival, although little research has been done on fields that received excessive applications of manure.

Management strategies to reduce bacterial transport include tillage methods that disrupt preferential flow pathways. Methods of preventing preferential flow may be at odds with other strategies intended to mitigate other environmental impacts. For example, tillage methods that disrupt preferential flow may cause increased soil erosion and nutrient losses when compared to no till and conservation tillage.

Figure 8.2.2 – Examples of macropore/preferential flow routes in a no till tiled field in Ohio

8.3  Source Assessment - Pets

The American Veterinary Medical Association estimates there are 0.66 cats and 0.58 dogs per household in the United States. Based on an average household of 2.52 people, this equates to 1,401 cats and 1,232 dogs in HICW and 2,360 cats and 2,074 dogs in RRW. High densities of pets in isolated areas can lead to bacterial contamination of waterways; however pets are normally a minor contributor of fecal coliform bacteria contamination at a watershed scale.

8.4  Source Assessment - Wildlife and Natural Background

Deer, pheasant, Canadian goose and wild turkey density estimates were obtained from the Minnesota Department of Natural Resources – Wildlife Section.

Deer density is estimated annually by the DNR for each hunting permit area.  HICW and RRW encompass portions of four permit areas. The average deer density based on this data is 3.26 deer per square mile. This equate to 779 deer in HICW and 1,314 deer in RRW.

Pheasant population estimates were provided for each county in both watersheds, based on estimates made in August of each year. A ten-year average density (1995-2004) was calculated for each county. Based on DNR estimates, there is an average of 50 pheasant per square mile in both watersheds. This equates to an estimated 11,950 pheasants in HICW and 20,150 in RRW. The DNR report that April populations are about ¼ August estimates.

Canadian goose populations are estimated by ecoregion. Estimates are based on 2001-2004 data for the prairie ecoregion. The DNR estimates a prairie ecoregion density of 4.5 geese per square mile. This equate to 1,065 geese in HICW and 1,795 in RRW. The DNR estimate is for the resident geese population, not including migrating geese in the fall. Migrating geese in the fall season can concentrate in lakes and wetlands contributing large quantities of fecal waste. Geese are one of the largest wildlife sources of fecal contamination, simply because they are found directly on waterways.

The DNR bases wild turkey population estimates on harvest. Similar to deer densities, turkey estimates are based on permitted hunting areas. The mean wild turkey density in this region is 1.09 per square mile. However, like other wildlife, they are not equally distributed, instead clumping towards forested areas and ravines. The HICW and RRW have an estimated wild turkey population of 261 and 439 respectively.

Population estimates and monitoring data support that wildlife normally are not a significant contributor of fecal coliform bacteria contamination in these watersheds. Conditions when wildlife can be a significant source include isolated areas of high density and during low flow/drought conditions.

  - Targeted Sources

Sections 8.5.1 through 8.5.4 detail the process that was used to estimate the primary sources of fecal coliform contamination in HIW and RRW. This procedure has no bearing on TMDL allocations and has no regulatory implications.

8.5.1 Fecal Coliform Produced (by source)

The first step was compiling population estimates and fecal coliform produced by each animal type. Tables 8.5.1a and 8.5.1b present the estimated population figures (number of individuals or animal units) for the major animal types in each watershed. Figures 8.5.1a and 8.5.1b display the estimated fecal coliform produced by animal type and source groups.

Population figures were obtained from state feedlot inventories, the U.S. Census Bureau and the Wildlife section of the Minnesota Department of Natural Resources. The daily fecal coliform production was obtained from a variety of sources that are all recommended in the EPA’s guidance document Protocol for Developing Pathogen TMDLs (2002). Total fecal coliform produced by each animal type is calculated by multiplying the population by the daily fecal coliform produced per individual or animal unit. These figures represent the total fecal coliform available, not the amount delivered to surface waters.

Table 8.5.1a – High Island Creek Population Inventory

Table 8.5.1b – Rush River Population Inventory

Figure 8.5.1a – High Island Creek Watershed Fecal Coliform

Bacteria Produced by Animal Type

Figure 8.5.1b – High Island Creek Watershed

Fecal Coliform Bacteria Produced by Source Group

Figure 8.5.1c – Rush River Watershed Fecal Coliform

Bacteria Produced by Animal Type

Figure 8.5.1d – Rush River Watershed Fecal

Coliform Bacteria Produced by Source Group

Next, the total fecal coliform bacteria produced by each animal type was categorized by application type/method. For humans, this meant calculating the number of people that had adequately treated and inadequately treated wastewater. For livestock, assumptions were derived from the Generic Environmental Impact Statement (GEIS) on Animal Agriculture (Mulla, et all, 2000), prepared by the Minnesota Environmental Quality Board. This document provides general guidelines on how and where livestock manure is applied to farmland in Minnesota. (Slight modifications were made for swine assumptions; changing incorporated swine manure from 80% to 95% and surface applied swine manure from 20% to 5%. These modifications reflect a continuing shift from surface applied to incorporated swine manure). Tables 8.5.1c and 8.5.1d present the assumption used for each watershed and the resulting categories.

Table 8.5.1c – Assumptions Used to Calculate the FC Produced by Different Sources in HICW

Table 8.5.1d – Assumptions Used to Calculate the FC Produced by Different Sources in RRW

Figures 8.5.1e and 8.5.1f display the source/application type for fecal coliform bacteria in the HICW and RRW respectively. The data indicate most fecal material is applied to agricultural land. Again note that the figure represents the estimated fecal coliform bacteria produced by source and application type, not the fecal coliform that is actually delivered to surface water.

Figure 8.5.1e - Estimated Fecal Coliform Produced by Source/Application Type in HICW

Figure 8.5.1f - Estimated Fecal Coliform Produced by Source/Application Type in RRW

8.5.2 Delivery Assumptions

To help identify what the primary sources of fecal coliform bacteria contamination for HICW and RRW, the delivery ratios in table 8.5.2 were used. The ratios were obtained from Appendix C of the Regional TMDL Evaluation of Fecal Coliform Bacteria Impairments in the Lower Mississippi River Basin in Minnesota, 2002 (revised 2006). While the report did not include delivery estimates, the source contribution process used in the original report still has utility.

These ratios presented in table 8.5.2 were based on expert opinions and should be considered in relative rather then absolute terms. Thus, while 1% of surface applied manure was assumed to be delivered to waterways, only 0.1% of incorporated manure was considered delivered.  Straight pipe septic systems were given the highest delivery ratio, at 8%.

Table 8.5.2 – Delivery Assumptions

8.5.3 Target Areas

Delivery ratios used in section 8.5.2 come with a degree of uncertainty. The amount of fecal material delivered from any one source will vary depending on numerous factors. Because of this uncertainty, it is difficult to accurately break down the percentage contribution of bacterial contamination from each source. Instead, categories were used to list the sources of bacterial contamination in the impaired stream reaches. Table 8.5.3 presents the likely major sources of bacterial loading in HICW and RRW, during wet and dry conditions. Wet conditions are defined as those during and following precipitation events that cause overland flow. Dry conditions are when overland flow is not occurring. A greater percentage of days would be considered dry; however the majority of bacterial loading to streams occurs during wet conditions. Categories were defined as <5% being a low contributor, 5%-20% a moderate contributor and >20% a high contributor.

Table 8.5.3 – HICW and RRW Major Contributors of FC Bacteria

8.6  Implementation Activities

Source inventories and water quality testing as part of this project indicate sources of fecal coliform contamination to streams can vary by a number of factors, especially weather and flow. These analyses indicate the primary sources of fecal coliform contamination during wet conditions to be livestock manure (land applied manure and runoff from feedlots without controls). The primary sources during low flow conditions are inadequately functioning septic systems. Implementation activities will be targeted towards these sources.

An Implementation Strategy Planning meeting was held November 30th, 2006 to solicit recommendations for implementation activities. The below strategies are broad in scope and will be refined in a more thorough implementation plan.

8.6.1  Feedlot Runoff Controls

State rules for feedlot runoff control will reduce, but not eliminate, bacteria transport to waters from open lots by October 2010. At that time, the bacteria contributions from open lot runoff will need to be reassessed. The Environmental Quality Incentive Program assists feedlots that have a high risk for runoff problems. This cost share funding typically goes for high cost fixes, such as manure storage basins.

One issue discussed at the Implementation Strategy Planning meeting was a lack of grant funding for low cost feedlot fixes. It was noted that typically the county Soil and Water Conservation Districts receive only $10,000 to $20,000 annually for cost share practices (this includes practices such as terraces, diversions, sediment control basins, feedlot control structures, etc.) through the State Cost Share program from the Board of Soil and Water Resources (BWSR). When funding is spread across these various practices, funding is quickly expended. The group agreed that additional cost share for feedlot fixes would be beneficial.

8.6.2 Manure Management Planning

State rules dictate that feedlots larger than 300 animal units are required to develop manure management plans. However, the majority of feedlots in the watersheds are under the 300 animal unit limit. The committee recommended promotion of manure management plans for smaller feedlots that are not required to develop plans. Members of the TMDL technical committee suggested obtaining grant dollars to provide 80-90% cost share for livestock operators to develop manure management plans. These plans could be developed by private consultants, co-ops, or the U of M extension. As part of this process, follow-up would be a key.

Manure management education for horse owners was also suggested by the committee.  There are currently around 200 homesteads in Sibley County alone that have horses, (between 700-1000 animal units between both watersheds). Two ideas from the group were cost share for construction of composting structures for horse manure and educational activities.

Representatives from the MPCA feedlot division made the following recommendations regarding applied manure implementation activities:

- Monitoring and research to determine which soils, soil management practices and land application timing practices prevent bacteria movement vertically into tile lines.

- Conduct a promotional campaign of sweep injection and other effective manure incorporation techniques onto soils which are found not to transmit bacteria through preferential flow into tile lines. This type of practice can also be promoted as a way to conserve manure nitrogen and thereby potentially save fertilizer costs.

- Develop a set of economically viable BMPs for reducing bacteria transport in situations where injection/incorporation alone may lead to bacteria entering tile lines. Practices may consider various combinations of:  manure storage, fall timing of manure applications, composting, grass buffers, runoff and erosion control, careful timing of manure application to reduce the likelihood of rainfall within a few days after application;

- Keep track of adoption of the above practices to evaluate progress in achieving implementation goals.

8.6.3 Non-Conforming Septic Systems

Septic upgrades to noncompliant septic systems are occurring at a faster rate now than in the past due to county and watershed initiatives. Still, the group agreed that more effort could be put towards upgrading of non-compliant septic systems if additional resources were available.

It was noted that over the past several years, counties have received only $1,500 to $3,000 for the septic program administration. Administrative dollars will be increased this coming year to around $9,000 for Sibley County (a one-time increase due to Clean Water Legacy dollars). While this was felt to be a positive change, the funding is still inadequate to allow for proper inventorying and educational activities related to septic systems.

Some ideas given during the meeting included:

- Demonstration projects across the watersheds, perhaps one per township. Local landowners would be invited to see how the septic systems are installed and how they function. Contractors would be available to answer questions and researchers would be present with information that shows the impact of septic discharges to our streams.

- It was also stressed that the regulatory side would progress faster if additional investigative funding were available for:

- Dye Testing

- Digging up of tile lines for investigation purposes

- Costs associated with the water quality sampling that is  needed for legal purposes

- The costs of inventorying noncompliant septic systems (walking the ditches and documenting the obvious straight pipe systems.)

The recommendation of the committee was to hire a full time coordinator for the two watersheds to work on these compliance or regulation issues and education/information activities.

Existing implementation plans and cost estimates for the Lower Mississippi and Greater Blue Earth Fecal Coliform TMDLs can be used to generate a rough estimate of the cost for implementing the practices outlined above at the scale of the Rush and High Island watersheds. Implementing the same suite of practices as called for in the Lower Mississippi and Greater Blue Earth, and accounting for the size of the combined High Island and Rush River watersheds, approximately $20,000,000 over 15 years would be necessary to meet the water quality standards. Though a very large sum of money, it should be noted that many of the practices called for could also help address additional water quality concerns in the watershed including turbidity and elevated nutrient levels.

Section 9.0 – Reasonable Assurance

As a requirement of TMDLs, reasonable assurance must be provided demonstrating the ability to reach and maintain water quality endpoints. The source reduction strategies detailed in section 8.0 have been shown to be effective in reducing pathogen transport and survival and to be capable of widespread adoption by land owners and local resource managers.

9.1  Feedlot Runoff Controls

These are evaluated by professional engineers through the Feedlot Evaluation Model referenced in Minn. R. ch. 7080. These rules are implemented by the MPCA staff and by local counties via a delegation agreement with the Agency. In Minnesota, feedlot rule 7020 requires the registration of feedlots and manure storage areas having a capacity of 50 animal units (AU) or more and 10 AU or more in shoreland areas.

9.2  Land Application of Manure

Buffer strips, immediate incorporation, observance of setback rules, and maintenance of surface residue have been demonstrated to reduce manure and pathogen runoff (Environmental Quality Board, General Environmental Impact State for Feedlots). Minnesota Rules Chapter 7020 require manure application record keeping and manure management planning, with requirements varying according to size of operation and pollution risk of application, based on method, time and place of application.

Section 8.2.1 and 8.2.2 detail the possible routes of transport of fecal coliform bacteria from lands receiving manure application. Current manure application rules are based on the best available research. However, in Minnesota, relatively little research has been conducted examining manure application setback rules related to fecal coliform bacteria. Further research should be put towards refining current manure application rules, especially setback distances for applied manure from open tile intakes.

9.3  Individual Sewage Treatment Systems

ISTS with proper drain fields provide virtually complete treatment of fecal coliform bacteria. Straight-pipe septics discharge untreated wastewater to surface water. Acceptable designs are described in Minn. R. ch. 7080. Minnesota counties in the basin are delegated to implement these rules, which require conformance with state standards for new construction and disclosure of the state of the ISTS when property transfers ownership. Several counties require ISTS upgrades at property transfer.

9.4  Municipal Waste Water Disinfection

Disinfection with chlorine or ultraviolet radiation is required of all NPDES municipal wastewater permittees.

9.5  Erosion Control and Sediment Reduction

Conservation tillage and riparian buffer strips have been demonstrated to be effective in reducing sediment delivery to streams. Since embedded sediment can serve as a substrate for fecal coliform survival, reduction of sediment is considered an effective measure of controlling fecal coliform bacteria in streams.

9.6  Planned Rotational Grazing

Sovell et al, 2000, demonstrated that rotational grazing, in contrast to conventional grazing, significantly reduces both sedimentation and fecal coliform concentrations in water downstream of study sites in southern Minnesota.

9.7  Urban Stormwater Management

Practices such as runoff detention, infiltration, and street sweeping have been shown to be effective in reducing urban runoff and associated pollutants.

Section 10.0 – Public Participation

10.1 Stakeholder Involvement

Public participation opportunities were provided during the project in the form of public open houses, new releases and a project newsletter. The project worked closely with a broad array of county, state and individual stakeholders. The joint HICW and RRW CWP technical committee served as the advisory and review role for the project. This group is comprised of staff from the following groups:

- High Island Watershed District

- Soil and Water Conservation Districts

- Natural Resources Conservation Service

- City of Lafayette

- County Water Planners

- County Commissioners

- Minnesota Pollution Control Agency

- Board of Soil and Water Resources

The technical committee also formed a smaller TMDL subcommittee which assisted in reviewing the project workplan, outreach material and review of the draft TMDL report. The technical committee was updated quarterly on the progress of the project. Key findings were discussed and input was gathered from the group. In addition to this group, presentations regarding the project were also given to the Sibley County Water Resources Advisory Committee in July 2005, December 2005 and July 2006.

Public outreach for this project also included the following activities:

Dec. 2005	Conservation Promotions meeting held in Buffalo Lake. As part of these open houses, information on the TMDLs is provided to the public.

May 2006	A six page newsletter detailing the project is sent to citizens in both watersheds. The newsletter detailed what fecal coliform is, the major sources and information on three June open houses. The newsletter also includes a short survey (see below).

Jun. 2006	Public open house meetings held in the communities of Henderson, Gaylord and Stewart explaining TMDLs, fecal coliform bacteria, associated health risks, potential sources of fecal coliform and water quality monitoring data. This open house is combined with a free well water testing clinic to help draw in citizens. A total of 112 citizens attended these three open houses.

Dec 2006	The draft High Island Creek - Rush River Fecal Coliform TMDL report is submitted for public/agency review. News releases submitted to newspapers in the project area.

10.2  Results of TMDL Survey

The following survey questions were distributed May 2006 to approximately 1,930 rural households in the High Island Creek and Rush River Watersheds as part of a six page project newsletter. A total of 156 surveys were returned, a response rate of 8.1%.

When was your septic system installed?

How often do you pump your septic system?

Have you had your well tested for Fecal Coliform Bacteria in the past?

High Island and Rush River have high levels of Fecal Coliform Bacteria. What do you think is/are the source(s)?

What will it take to upgrade your septic system?

Other comments written on the surveys:

- Current mound systems are worthless and costly-Forced upgrades should be criminal

- Get a good system and get rid of mounds

- Tie the farm payment program (USDA) into the compliance or property tax at a higher rate for non-compliance

- Elderly can’t afford to do it alone

- Five wrote that wildlife are a major source

- Four wrote that pesticides/fertilizers are a major source

Eighty-seven (56%) of the respondents indicated that their septic system had been installed prior to 1996. The below chart shows how often these older systems were pumped.

Appendix A - References

Alderisio, K.A., & DeLuca, H.  1999.  Seasonal Enurmeration of Fecal Coliform Bacteria from the Feces of Ring-Billed Gulles (Larus delewarensis) and Canada Geese (Branta Canadensis).  Applied and Environmental Microbiology.

American Society of Agricultural Engineers (ASAE).  1998.  ASAE Standards, 45th Edition. Standards, Engineering Practices, Data.

Beven, K. and P. Germann, 1982.  Macropores and water flow in soils.  Water Resources Research 18:1311-1325.

Chapelle, F.H., 2001.  Ground-Water Microbiology and Geochemistry (Second Edition).  John Wiley and Sons, Inc., New York, New York, 424 pp.

Crane, S.R., P.W. Westerman and M.R. Overcash.  1981  Dieoff of fecal indicator organisms following land application of poultry manure.  Journal of Environmental Quality 9:531-537.

Cullimore, R.D., 1993.  Practical Manual of Groundwater Microbiology.  Lewis Publishers, Chelsea, Michigan, 412 pp.

Davis, R.K., S. Hamilton, and J.V. Brahana.  2005.  Escherichia Coli Survival in Mantled Karst Springs and Streams, Northwest Arkansas Ozarks, USA

Ewert, Jason, MPCA, personal communication, December 20, 2005.

Ganske, L., 2005.  Regional Total Maximum Daily Load Evaluation of Fecal Coliform Bacteria Impairment in the Lower Mississippi River Basin in Minnesota.

Geohring, L.D, P.E. Wright, T.S. Steenhuis and M.F. Walter.  1999.  Fecal coliforms in tile drainage effluent.  ASAE Paper No. 992203. St. Joseph, MI: ASAE

Gerba, C.P., C. Wallis and J.L. Melnick.  1975.  Fate of wastewater bacteria and viruses in soil.  Journal of Irrigation and Drainage Engineering 101:157-174.

Horsley and Witten, Inc.  1996.  Identification and evaluation of nutrient and bacterial loadings to Maquoit Bay, New Brunswick and Freeport, Maine.  Final Report

Jamieson, R.C., 2002.  Movement and persistence of fecal bacteria in agricultural soils and subsurface drainage water: A review.

Jolley, L.W., J.W. Pike, M. Goddard.  2004  The Role of Bottom Sediments in the Storage and Transport of Indicator Bacteria.  Department of Forestry and Natural Resources, Clemson University.  Poster Presentation.

Metcalf and Eddy.  1991.  Wastewater Engineering:  Treatment, Disposal, Reuse. 3rd ed.  McGraw-Hill, Inc., New York.

Minnesota Easement GIS data layer, provided by Minnesota Board of Soil and Water Resources, January 2006.

Minnesota Pollution Control Agency.  2003.  Guidance Manual for Assessing the Quality of Minnesota Surface Water for the Determination of Impairment.

Mulla, D. J., and A.S. Birr, G. Randall, J. Moncrief, M. Schmitt, A. Sekely, and E. Kerre.  2001.  “Technical Work Paper: Impacts of Animal Agriculture on Water Quality,” Department of Soil, Water and Climate, University of Minnesota, Prepared by the Minnesota Environmental Quality Board and Citizen Advisory Committee.

National Climatic Data Center, 1971-2000.

Randall, G. W., T.K. Iragavarapu and M.A. Schmitt.  2000.  Nutrient Losses in Subsurface Drainage Water from Dairy Manure and Urea Applied for Corn.  Journal of Environmental Quality 29: 1244-1252

Randall, G.W., S. Goyal, J.A. Vetsch and S. Meharchandani.  2003.  Nutrient and Pathogen Losses to Tile Lines as Influenced by Source of N.

Smith, M.S., M.S. Coyne and J.H. Grove.  1998.  Fecal bacteria survival and infiltration through shallow agricultural soil:  Timing and tillage effects.  Journal of Environmental Quality 27:1516-1523.

U.S. Environmental Protection Agency.  2001.  Protocol for Developing Pathogen TMDLs.  EPA 841-J-00-002.  Office of Water (4503F), United States Environmental Protection Agency, Washington, DC.  132 pp.

Wieskel, P.K., B.L. Howes, and G.R. Heufelder.  1996.  Coliform contamination of a coastal embayment:  sources and transport pathways.  Environmental Science Technology 30(6):  1872-1881.

Yagow, G. and V Shanholtz. 1998.  Targeting sources of fecal coliform in Mountain Run.  An ASAE Meeting Presentation.  98-2031.  July 12-26, 1998.

Zhai, Q., M.S Coyne and R.I. Barnhisel.  1995.  Mortality rates of fecal bacteria in subsoil amended with poultry manure.  Bioresource Technology 54:165-169.

# Text boxes

Site

10P

In Ohio, Shipitalo and Gibbs pump smoke into a tile line to show the connectivity of the surface to tile.line.

The pictures depict a conventionally tilled, clayey soil where earthworms appear to preferentially burrow towards the drains.  The tile in this photo is 4 feet deep.

Open tile intake in road ditch, receiving

runoff from field with surface applied manure.

An open tile intake along the edge of an agricultural field.

Straight pipe septic systems usually discharge to the nearest stream, ditch or lake.

Systems that discharge partially or untreated sewage directly to surface water are often referred to as “straight

pipe systems”.

6S

07020012-553

07020012-588

Figure 1.2 – Fecal Coliform Bacteria Impaired Streams

Site

3P

Site

8P

Site

9P

Site

2P

Figure 1.2 – Fecal Coliform Bacteria Impaired Streams