Drycleaner Form DC-07

MONITORING LOG FOR

CARBON ADSORBER (CA)

04/11/00

Use colorimetric detector tube for PERC concentration (PERC CONC) measurement, follow the manufacturer's instructions on operation and measurement.

TEST DATE is the WEEKLY concentration measurement date.

Make copies of this form for future use.

PERC CONC 1 is recorded if you use a CA on a dry-to-dry or a transfer machine to meet the required control; or you use a supplemental CA on a dry-to-dry machine and the exhaust passes through the CA immediately upon door opening. Accuracy should be 25 ppm by volume. PERC CONC 1 should be less than or equal to 100 ppm. Measurement should be made after the last dry cleaning cycle prior to desorption of CA. A sampling port for monitoring within the exhaust outlet of the CA must be provided that is easily accessible; located at least eight times the diameter of the stack or duct downstream from any flow disturbance (bend, expansion, contraction, or outlet); not downstream from any other inlet and two times the diameter of the stack or duct upstream from any flow disturbance.

FOR NEW MAJOR SOURCES ONLY:

PERC CONC 2 is recorded if you use a supplemental CA on a dry-to-dry machine and the exhaust passes through the CA before the machine door is opened. Accuracy should be 75 ppm by volume. PERC CONC 2 should be less than or equal to 300 ppm. Measurement should be made at the end of the dry cleaning cycle. For measurement, insert the colorimetric tube into the open space above the cloth articles at the rear end of the drum immediately after opening the door.

|  | TEST DATE | PERC CONC 1 (ppm) | PERC CONC 2 (ppm) |
| --- | --- | --- | --- |
|  | TEST DATE | PERC CONC 1 (ppm) | PERC CONC 2 (ppm) |
| 1 |  |  |  |
| 1 |  |  |  |
| 2 |  |  |  |
| 2 |  |  |  |
| 3 |  |  |  |
| 3 |  |  |  |
| 4 |  |  |  |
| 4 |  |  |  |
| 5 |  |  |  |
| 5 |  |  |  |
| 6 |  |  |  |
| 6 |  |  |  |
| 7 |  |  |  |
| 7 |  |  |  |
| 8 |  |  |  |
| 8 |  |  |  |
| 9 |  |  |  |
| 9 |  |  |  |
| 10 |  |  |  |
| 10 |  |  |  |
| 11 |  |  |  |
| 11 |  |  |  |
| 12 |  |  |  |
| 12 |  |  |  |

# Text boxes

Minnesota Pollution Control  Agency

Small Business Assisstance Program

1-800-657-3938

(651)282-6143