Minnesota Pollution Control Agency

Air Quality Division

520 Lafayette Road

St. Paul, Mn 55155-4194

Registration Permit Form - RP-D2

Option D Control  Equipment Form

Final 11/08/94

PART I.  Introduction.

This form is for a stationary source qualifying for a registration permit under Option D, and using listed pollution control equipment in Minn. Rules 7011.0070, table A to reduce emissions.

PART II.  Listed Pollution Control Equipment.

CONTROL EQUIPMENT EFFICIENCY-TABLE A

| ID # | CONTROL EQUIPMENT DESCRIPTION |
| --- | --- |

CONTROL

| EFFICIENCY |
| --- |
| TOTAL ENCLOSURE | HOOD |

POLLUTANT CONTROLLED

PM, PM10

( if

Applicable

# of

Units

( if

Applicable

# of

| Units |
| --- |
| CYCLONES means a device where airflow is forced to spin in a vortex through a tube. |
| 007 | Centrifugal Collector (cyclone) - high efficiency means: a cyclonic device with parameters stated in drawing 1 and table 1 below. | q | ___ | 80% | q | ___ | 64% |
| 008 | Centrifugal Collector (cyclone) - medium efficiency means: a cyclonic device with parameters stated in drawing 1 and table 1 below. | q | ___ | 50% | q | ___ | 40% |
| 009 | Centrifugal Collector (cyclone) - low efficiency means: a cyclonic device with parameters stated in drawing 1 and table 1 below. | q | ___ | 10% | q | ___ | 8% |
| 076 | Multiple Cyclone without Fly Ash Re injection means: a cyclonic device with more than one tube where fly ash is not re-injected. | q | ___ | 80% |
|  | NA |
| 077 | Multiple Cyclone with Fly Ash Re injection means: a cyclonic device with more than one tube where fly ash is re-injected. | q | ___ | 50% |
|  | NA |
| 085 | Wet Cyclone Separator or Cyclonic Scrubbers means: a cyclonic device that sprays water into a cyclone | q | ___ | 50% | q | ___ | 40% |
| 012 | ELECTROSTATIC PRECIPITATORS means: a control device in which the incoming particulate matter receives an electrical charge and is then collected on a surface with the opposite electrical charge. |
|  | - assumed efficiency for boiler fly ash control | q | ___ | 40% |
|  | NA |
|  | - assumed efficiency for other applications | q | ___ | 70% | q | ___ | 56% |
|  | OTHER CONTROLS |
| 016 | Fabric Filter means: a control device in which the incoming gas stream passes through a porous fabric filter forming a dust cake. | q | ___ | 99% | q | ___ | 79% |
| 052 | Spray Tower means: a control device in which the incoming gas stream passes through a chamber in which it contacts a liquid spray. | q | ___ | 20% | q | ___ | 16% |
| 053 | Venturi Scrubber means: a control device in which the incoming gas stream passes through a venturi into which low pressure liquid is introduced. | q | ___ | 90% | q | ___ | 72% |

| 055 | Impingement Plate Scrubber means: a control device in which the incoming gas stream passes a liquid spray and is then directed at high velocity into a plate. | q | ___ | 25% | q | ___ | 20% |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 058 | Mat or Panel Filter means: a control device in which the incoming gas stream passes through a panel of coarse fibers. Panels are removable for cleaning or replacement and provide little resistance to air flow. | q | ___ | 92% |
|  | NA |

POLLUTANT CONTROLLED

| VOC |
| --- |
| 019 | Afterburners (thermal or catalytic oxidation) means: a device used to reduce VOCs to the products of combustion through thermal (high temperature) oxidation or catalytic (use of a catalyst) oxidation in a combustion chamber. | q | ___ | 95% | q | ___ | 76% |
| 023 | Flaring or Direct Combustor means: a device in which air, combustible organic waste gases, and supplementary fuel (if needed) react in the flame zone (e.g., at the flare tip) to destroy the VOCs. | q | ___ | 98% | q | ___ | 78% |

PART III. Supplemental Information.

q For each pollution control equipment unit a copy of the portion of the manufacturers specification or test plan with the

operating parameters required to be monitored under Minn. Rules 7011.0080 highlighted.

q If any pollution control equipment unit uses a hood to capture air emissions, then form  RP-D3 (Hood Certification) must

be submitted.

DRAWING 1

TABLE 1

| Ratio Dimensions* | High Efficiency | Medium Efficiency | Low Efficiency |
| --- | --- | --- | --- |
| Height of inlet, H/D | (0.44 | >0.5 and <0.8 | (0.8 |
| Width of inlet, W/D | (0.2 | >0.2 and <0.375 | (0.375 |
| Diameter of gas exit, De/D | (0.4 | >0.4 and <0.75 | (0.75 |

Length of vortex

| finder, S/D | (0.5 | >0.5 and <0.875 | (0.875 |
| --- | --- | --- | --- |

*If one or more of the "ratio dimensions," as listed in table 1, are in a different efficiency category (high, medium, low),    then the lowest efficiency category shall be applied.