Composting of Petroleum Contaminated Soil

Fact Sheet #3.18

August 1996

The Minnesota Pollution Control Agency (MPCA) requires that excavated petroleum contaminated soil be treated or disposed of properly.  Composting is a safe and effective method that takes advantage of naturally occurring micro-organisms to biodegrade petroleum.

The MPCA defines composting as the controlled microbial degradation of petroleum contaminated soil.  This is usually done by building a compost pile (sometimes referred to as a bio-pile) which is a pile of petroleum contaminated soil that is constructed in such a way that provides optimum conditions for microbial growth through the addition of oxygen, water and nutrients.  Pipes distribute oxygen through the pile.  Bulking agents such as wood chips, sawdust or straw can also be added to the pile to facilitate the movement of air through the pile.  Nutrients in the form of fertilizers or manure may also be added.  The pile is watered or kept moist.  The pile is covered to keep moisture loss to a minimum, to keep the pile warm and to prevent volatilization.  Under these conditions, micro-organisms, such as bacteria and fungi, flourish.  These organisms then break down the petroleum wastes by consuming them and transforming them into harmless substances consisting mainly of carbon dioxide, water and fatty acids.

Composting of petroleum contaminated soil is regulated by the Solid Waste Rules and is required to be permitted.  Usually, the permitting process is an involved and often lengthy process that can take up to six months.  However, the MPCA has developed a general permit to cover composting of petroleum contaminated soil at facilities that meet the following conditions (applicability criteria):

A.	The proposed facility will only be used for the composting of petroleum contaminated soil.

B.	No more than 1,500 cubic yards of petroleum contaminated soil will be present at the proposed facility at any one time (this does not include any soil that has been spread on the site).

C.	The proposed facility meets the following setback distances requirements if the compost pile(s) are not going to be placed on an impervious surface:

a.	200 feet from an intermittent stream, drainage ditch, tile drain inlet, sinkhole, known underground cave, and the ordinary high water level of a surface water or wetland;

b.   500 feet from a residential development or recreational area;

Composting of Petroleum Contaminated Soil

Page 2

August 1996

c.	200 feet from an adjacent property or place of habitation without written permission; and

d.	four foot separation distance to the seasonal high water table as listed in the Soil Conservation Survey or as verified by a certified soil scientist, geologist, or hydrogeologist, with mapping experience based on an on-site investigation.

D.	The proposed facility meets the following setback distances requirements if the compost pile(s) are to be placed on an impervious surface:

a.  100 feet from an adjacent property or place of habitation without written 			     permission; and

b.	200 feet from a recreational area.

E.	Compost pile(s) are protected from run-on and run-off.

F.	The proposed facility is not located in a 100-year floodplain.

G.	The proposed facility is not located in an area with a slope of greater than two percent.

In addition to the applicability criteria above, persons wishing to compost petroleum contaminated soil at any facility under this general permit also need to submit plans and specifications for their proposed facility which show that they can meet all the requirements of the general permit such as:

A.	An operation and maintenance plan that ensures the compost pile(s) will be watered, aerated and fertilized as necessary to ensure optimal microbial activity.

B.	A description of run-on and run-off controls to be used.

C.	A plan for the end use and location of the composted material following confirmation of treatment.  Compost may be used as controlled fill (except near residences, wetlands or other sensitive areas), spread on site or other purposes as approved by the MPCA Commissioner.

MPCA staff then reviews each application to determine if the facility can be permitted under the general permit for composting of petroleum contaminated soil.  If the information contained in the application for a composting general permit indicates that the proposed facility meets the applicability criteria listed above and can meet the requirements of the permit, the MPCA will send a letter of approval and a copy of the general permit to the applicant, who then becomes a permittee.  The permit is a legal, binding, enforceable document.

Upon request, this document can be made available in other formats, including Braille, large print and audio tape.  TTY users call 612/282-5332 or Greater Minnesota 1-800/657-3864.

Printed on recycled paper containing at least 10 percent fibers from paper recycled by consumers.

MINNESOTA POLLUTION CONTROL AGENCY

520 LAFAYETTE ROAD NORTH

ST. PAUL, MINNESOTA  55155-4194

August 1996

General Permit Application for the Construction and Operation of

A Petroleum Contaminated Soil Composting Facility (Form A)

Persons wishing to compost petroleum contaminated soil at any facility under this general permit shall complete this permit application and submit it to the Tanks and Emergency Response Section of the Minnesota Pollution Control Agency (MPCA) and meet all the applicable criteria listed in fact sheet #3.18, "Composting of Petroleum Contaminated Soil."  Facilities which do not meet all of these applicable requirements will need to be evaluated for issuance of an individual Solid Waste Permit under Minn. R. chs. 7000, 7001, and 7035, in the Solid Waste Section of the MPCA.

For pre-approval of a site for composting, number VII., Petroleum Contaminated Soil Sampling Results, is not required.  However, for batch approval of leaded gasoline or used oil, number VII. part C. is required.  If the applicant is anticipating composting soil, it is recommended you plan ahead by completing this form.

Please note that numbers III. and IV. do not need to be completed if you have already obtained a permit for the composting facility and you are using this application only for subsequent batch approval.  To submit follow-up soil monitoring results for composted petroleum contaminated soil, use Form B attached at the end of this document.

I.	BACKGROUND

| A. Responsible Party for Soil | B. Site from which soil originated |
| --- | --- |
|  | *MPCA Site ID#: LEAK0000______ |
| Contact: | *if applicable |
| Company name: | Company name: |
| Street/Box: | Street: |
| City, Zip: | City, Zip: |
| State: | County: |
| Telephone: | State: |

| C. Landowner of Compost Site | D. Composting Facility Operator |
| --- | --- |
|  | Name: | Name: |
| Street/Box: | Street/Box: |
| City, Zip: | City, Zip: |
| Telephone: | Telephone: |
|  | Signature: _____________________________ | Signature: _____________________________ |
|  | Date: _________________________________ | Date: _________________________________ |

Composting Application

Page 2

August 1996

E. Consultant (or other) who has completed this application:

Name:

Business name:

Street/Box:

City, State Zip:

Telephone:

II.  SOIL STORAGE INFORMATION

A.	Current location of proposed soil batch to be composted(check one):

______ stockpiled on storage area at proposed composting site

______ stockpiled on the property from which the soil originated

______ not yet excavated

______ other: explain __________________________________________________

B.	Date soil stockpiled (if applicable): ____________________

C.	Type of stockpile run-off controls in place (if applicable):      _______________________

_______________________________________________________________________

D.	Volume of soil of proposed batch to be composted:  __________ cubic yards

E.	Projected date of soil composting: ____________________

F.	Soil type to be treated (i.e.: sand, loamy clay):___________________________________

III.  PROPOSED LOCATION OF COMPOST FACILITY:

City or Town:

Address:

County:

Township:

Legal Description of Compost Treatment Site (rural sites only):

______ ¼ of ______ ¼ of Section ______, Township ______, Range ______, Township

Name ____________________ , County ____________________

Composting Application

Page 3

August 1996

IV.  COMPOST FACILITY CHARACTERISTICS

Complete the following:

A.  Soil volume amount to be permitted at this facility			__________________

(1500 cubic yards maximum per facility)

B.  Distance to nearest intermittent stream, drainage ditch,

tile drain inlet, or the ordinary high water level of a stream,

river, sinkhole, lake pond, wetland or flowage: 			__________________

C.   Distance to nearest place of habitation:				__________________

D.  Distance to nearest residential development or recreational area:	__________________

E.  Distance to nearest property line:					__________________

F.  Site Slope:								__________________

G.   Depth to seasonal high water table if not on an impervious

surface (Soil Conservation Survey interpretations, excavation

observations, or boring logs):					_________________

H   Is this site located within 500 feet of the ordinary high levels of a trout stream, trout

lake, or outstanding resource value water (or an intermittent stream, drainage ditch, or

tile drainage inlet that directly outlets to one) as indicated in part 7037.1000, subpart 2?

______ YES   ______ NO

I.   Has this site been used for treatment or disposal of wastes (not including petroleum

contaminated soil)?  ______ YES   ______ NO      If YES, explain.

V.   COMPOST METHOD AND MONITORING

Attach a compost system description that includes the following:

A.  Copy of county plat map or standard 7.5 minute series quadrangle map with clear road

directions to the site.

B.	 A schematic drawing (including cross section of the compost system which includes;

compost pile dimensions, perforated pipe spacing, if used, poly thickness (should be at

least 6 mil) and coloration.

Composting Application

Page 4

August 1996

C.  A site map (scale:  1 inch =10 to 50 feet) indicating the following:

borders of treatment site (indicate dimensions of each side in feet)

delineate proposed area for this batch of soil (in feet)

delineate all other areas previously used for treatment (in feet and indicate with leak site number)

north arrow

D.	An operation and maintenance plan that ensures the compost pile(s) will be watered,

aerated and fertilized as necessary to ensure optimal microbial activity.

E.	Estimated ratio of soil to bulking agent and/or nutrients, if proposed, and the procedure

that will be used for the mixing bulking agent and/or nutrients.

F.	A description of run-on and run-off controls to be used.

G.	A description of the field method for monitoring moisture.

H.	A plan for the end use and location of the composted material following confirmation of treatment.  Compost may be used as controlled fill (except near residences, wetlands or other sensitive areas), spread on site or other purposes as approved by the MPCA Commissioner.

VI.	INFORMATION REGARDING PREVIOUSLY APPROVED CONTAMINATED SOIL

Provide the following for contaminated soil that has been composted or land applied at this

treatment site:

Site (name, city)

Leak Site or Spill Site Number

(if applicable)

Soil Volume

| (cu. yds.) |
| --- |
| _________________________________________________ | ______________ | __________ |
| _________________________________________________ | ______________ | __________ |
| _________________________________________________ | ______________ | __________ |
| _________________________________________________ | ______________ | __________ |

Total soil volume of Sites already composted at this facility:		________ cubic yards

Composting Application

Page 5

August 1996

VII.  PETROLEUM CONTAMINATED SOIL SAMPLING RESULTS

A.  Type(s) of petroleum contamination (i.e.: unleaded gas, regular

gas, diesel fuel, etc.):						________________

B.  Indicate method of sample soil collection. (i.e.:  Soil boring,

stockpile sample or other):						__________________

C.  Provide analytical results for the petroleum contaminated soil that is to be composted, if   available (analytical results are required if the soil is contaminated with used or waste oil).  Attach analytical results to the application.

Sample

Code

TPH as

gas or FO

ppm

(circle one)

Benzene

ppm

Ethyl-

benzene

ppm

Toluene

ppm

Xylene

ppm

Lead

| ppm |
| --- |
| _________ | _________ | _________ | _________ | _________ | _________ | _________ |
| _________ | _________ | _________ | _________ | _________ | _________ | _________ |
| _________ | _________ | _________ | _________ | _________ | _________ | _________ |
| _________ | _________ | _________ | _________ | _________ | _________ | _________ |
| Average | _________ | _________ | _________ | _________ | _________ | _________ |

VIII.  NOTIFICATION OF COUNTY AND LOCAL GOVERNMENTS

A.  Prior to or concurrent to submittal of this application to the MPCA, the applicant must submit a copy of the application to the appropriate county and local officials and be able to provide a copy of certified mail receipts to the MPCA.  Please provide the names and addresses of the officials notified with this application below:

| County official: | Township, City, or Tribal official: |
| --- | --- |
| Title: | Title: |
| Street/Box: | Street/Box: |
| City, Zip: | City, Zip: |
| Telephone: | Telephone: |

Composting Application

Page 6

August 1996

B.   The applicant is responsible for obtaining all necessary county and local approvals.

The issuance of a Solid Waste General Permit allowing a petroleum contaminated soil

composting facility does not release the applicant from the duty to comply with

applicable county and local regulations.

C.    Please provide copies of written permission from adjacent land owners, if compost

treatment is to be done closer than 200 feet on a non-impervious surface or closer

than 100 feet on an impervious surface.

IX.  MPCA REVIEW AND APPROVAL

All applications shall be reviewed for completeness and adequacy by MPCA staff.  If the application is found to be incomplete or inadequate, a letter detailing staff comments will be sent to you after staff review has been completed.  Further processing of the application will be suspended until the applicant has provided the necessary information or resolved the inadequacy.  Contaminated soil may NOT BE COMPOSTED until this application is submitted and a permit obtained.

X.  CERTIFICATION

I certify under penalty of law that I am familiar with this document and all attachments submitted herein and based on my inquiry of those individuals immediately responsible for obtaining the information I believe the submitted information is true, accurate and complete.  I understand that under Minn. R. 7000.0300 I may be subject to civil penalty of up to $10,000 for failure to act in good faith and complete truthfulness, accuracy, disclosure and candor.

__________________________________________________	________________________

Applicant's Signature							Date

Composting Application

Page 7

August 1996

XI.  SUBMISSION OF THE APPLICATION

Mail completed application and all attachments to the project manager at the central office or at the appropriate regional office listed below:

Minnesota Pollution Control Agency

Central Office

Tanks and Emergency Response Section		Detroit Lakes - Northwest Office

520 Lafayette Road North				714 Lake Avenue, Suite 220

St. Paul, Minnesota  55155-4194			Detroit Lakes, Minnesota  56501

Duluth - Northeast Office				Marshall - Southwest Office

320 West Second Street				700 North Seventh Street

Duluth, Minnesota  55802				Marshall, Minnesota 56258

Brainerd - North Central Office			Rochester - Southeast Office

1601 Minnesota Drive				           2116 Campus Drive Southeast

Brainerd, Minnesota  56401				Rochester, Minnesota 55904

Upon request, this document can be made available in other formats, including Braille, large print and audio tape.  TTY users call 612/282-5332 or 1-800/657-3864 (voice/TTY)

Printed on recycled paper containing at least 10 percent from paper recycled by consumers.

Soil Monitoring Results For Composted Petroleum Contaminated Soil

(Form B)

August 1996

Compost Facility Information

| ID# |
| --- |
|  | Contact Name and Phone # | ( ) - |
| Facility Name |
|  | Address |
|  | City or Township, Zip |

Soil Batch Information

| Site ID# (if applicable) |
| --- |
|  | RP Name and Phone # | ( ) - |
| Site Name |
|  | Address |
|  | City, State Zip |

| Volume of Soil Composted (yds) |
| --- |
|  | Date Composting of Soil Began |
|  | Number of Soil Samples Collected |
|  | Date Soil Samples Were Collected |
|  | Date Soil Samples Were Analyzed |

Soil Sample Results

| Sample Number | DRO (ppm) | GRO (ppm) |
| --- | --- | --- |
| 1 |
| 2 |
| 3 |
| 4 |
| 5 |
| 6 |
| 7 |
| 8 |
| 9 |

Along with the above information, please include the following:

A map indicating the location from where the soil samples were collected

Copies of the analytical results from the laboratory

Copy of the soil sample chain of custody

| Name of Person Completing This Form (Print) |
| --- |
|  | Signature of Person Completing This Form |
|  | Date |