LAND TREATMENT OF PETROLEUM CONTAMINATED SOIL:

LAND TREATMENT SITES

Fact Sheet #3.8

May 1996

The Minnesota Pollution Control Agency (MPCA) requires that excavated petroleum contaminated soil be treated or disposed of properly.  Land treatment, which is incorporation of petroleum contaminated soil into the top four to six inches of native soil, can be an effective treatment option.  This method takes advantage of naturally occurring soil micro-organisms to biodegrade petroleum.  Some volatilization of petroleum hydrocarbons does result.

The specific technical and administrative requirements for land treatment of petroleum contaminated soil at land treatment sites are provided in Minn. R. ch. 7037.  The purpose of this fact sheet is to provide an overview of the requirements in the rules to aid in completing an application.  This fact sheet, however, is not intended as a substitute for the rules.

The following is a step-by-step guide which the MPCA staff has developed to assist the land treatment site owner/operator and/or responsible party/consultant  in completing Forms A, B, C and D for land treatment of petroleum contaminated soil.  In order for a land treatment site to be pre-approved and a batch of petroleum contaminated soil to be approved, the owner/operator of the land treatment site must submit a completed Form A and receive a written pre-approval for the land treatment site from the MPCA staff.  In addition, the responsible party for the leak site must submit a completed Form B for each individual batch of petroleum contaminated soil and receive a written approval to land apply the batch of petroleum contaminated soil on the pre-approved site.  The Form A Pre-approval is for the actual land treatment site and the Form B Approval is for the specific batch of petroleum contaminated soil.  Both the site Pre-approval and batch Approval need to be issued by MPCA staff for treatment of petroleum contaminated soil to occur.  The forms may be submitted individually or together.

FORM A INSTRUCTIONS

The following instructions are intended to assist you in completing the application for a petroleum contaminated soil land treatment site (Form A).

I.  Background

Part A-B:  Complete all of the land treatment site owner and operator information as

outlined.

Part C:       Please indicate the name and relationship of any person who is in possession

of the proposed site where land application is going to occur.

Part D:       Please indicate the name, address and telephone number of the person completing the

form in case MPCA staff need to ask questions about the application and so that a

copy of the approval letter can be sent to them.

Part E:       The legal description of the pre-approved land treatment site needs to be given.

Make sure to use the 1/4 of the 1/4 section.

Part F:       Please indicate the total area for proposed land treatment in square feet or

acres.

Part G:       Circle yes or no if land treatment of petroleum contaminated soil has occurred

within one-quarter mile of the proposed site in the last five years.

II.  Site and Native Soil Characteristics

The information below is intended to provide you with a general checklist of site and soil characteristics that will help determine the suitability of the proposed land treatment plot.  Please refer to the enclosed Minn. R. ch. 7037 and consult with your local Soil Conservation Service (SCS), environmental consulting firm, or a professional soil scientist in order to determine the suitability of the proposed land treatment plot for the treatment of petroleum contaminated soil.  A list of professional soil scientists is available upon request from the MPCA.  Please note that your signature at the end of the application indicates that you are taking responsibility for the contents of Minn. R. ch. 7037.

Is the proposed land treatment plot greater than the following:

A.  200 feet of an intermittent stream, drainage ditch, tile drain  inlet,                  Yes/No

and the ordinary high water level of a stream, river, lake, pond,

wetland, or flowage;

B.  200 feet from a sinkhole, exposed bedrock, and known underground cave;    Yes/No

C.  200 feet from any private water supply well;                                                  Yes/No

D.  1,000 feet from any public water supply well;                                                Yes/No

E.  200 feet from the nearest place of habitation;                                                 Yes/No

(unless you have written permission to be within 200 feet)

F.  200 feet from the nearest property line.                                                          Yes/No

(unless you have written permission to be within 200 feet)

G.  500 feet from a residential developoment or recreational area;                       Yes/No

H.  Is this site located within 500 feet of the ordinary high water levels                Yes/No

of a trout stream, trout lake, or outstanding resource value water

(or an intermittent stream, drainage ditch, or tile drainage inlet that

directly outlets to these features), as indicated in pt. 7037.1000, subpart 2?

__If YES, is a filter strip with a minimum width of 50 feet located between          Yes/No

the site and the above features?

I.  If the potential for run-on exists, describe the run-on control measures

to be used at the site (pt. 7037.1000, subpart 3)?

J.  Has the site been used for treatment or disposal of wastes (not including          Yes/No

petroleum contaminated soil)?

K.  Site slope: ________percent

L.  SCS soil series name(s) at site: Soil 1:__________________

Soil 2:__________________

M. Depth to seasonal high water table:       Soil 1:_________________feet

Soil 2:_________________feet

N.  Organic matter in upper 8 in. of soil:        Soil 1:__________________percent

Soil 2:__________________percent

O.  Depth to bedrock:  __________________feet

P.  Depth to drainage lines: ______________feet

Q.  Please use the chart below which indicates the minimum organic matter concentration in the upper 8 inches of native soil and minimum total thickness of soil with a permeability either less than 6 inches per hour or less than 0.6 inches per hour.

Required treatment zone characteristics

-------------------------------------------------------------------------------------------------------

Minimum organic matter    Minimum total thickness of    Minimum total thickness of (percentage)                          soil with a permeability less    soil with a permeability less

than 6 inches per hour              than 0.6 inches per hour

-------------------------------------------------------------------------------------------------------------

2 % to 4 %                               4 feet                                 3 feet

4 % or greater                          3 feet                                 2 feet

-------------------------------------------------------------------------------------------------------

III.  Local Government Notification Information

Please carefully read the section pertaining to proper local notification in the application.  Form A and B applications that do not have proper notifications and approvals will be returned to the applicant.

IV.  Maps and Supporting Information

Attach the information that is outlined in the Form A application.  CLEARLY MARK the exact location of the proposed land treatment site and stockpile storage area on each applicable map.  Please be aware that applications that do not have all of the supporting documentations will be returned to the applicant.  Consult with your local SCS, environmental consulting firms, or a professional soil scientist (list available upon request) for assistance with the types of reports and maps.

V.  Applicant Signature

The signatures of the land owner and site operator must be on the Form A.  The MPCA will not process the form unless both of these signatures are given.

VI.  Local Officials Mailing Addresses

Local officials mailing addresses must be given so that copies of the approval letters can be mailed to them.

FORM B INSTRUCTIONS

Following are the necessary steps to complete the Application to Land Treat Petroleum Contaminated Soil at a Pre-approved Site (Form B):

Part I.  Background

Part A-D:  Complete all of the responsible party, land treatment site owner/operator,

consultant and leak site information.  Make sure to include the leak number   		  	     and all addresses and telephone numbers.  The pre-approval number is listed on the

Form A approval letter.

Part E:      The legal description of the pre-approved land treatment site needs to be given.

Make sure to use the 1/4 of the 1/4 section.

Part F:       List all of the previous batches of soil which have been spread and/or approved

for the pre-approved land treatment site.  Be sure to give all of the information,

such as leak site name, leak site number, soil volume and date spread.

Part G:      List the amount of soil which you would like approved to spread at the land

treatment site.  Excavation of petroleum contaminated soil should follow MPCA

Fact Sheet #3-6, “Excavation of Petroleum Contaminated Soil”.  If a greater soil 	 	     volume than indicated on the Form B is generated, notification to the leak site

project manager is required prior to spreading.

Part H:      List the tentative soil spreading date.  Please note that spreading must occur

between April 1 and November 1.

II.  Soil Storage Information

Petroleum contaminated soil may be stored at land treatment sites provided that certain conditions are met.  Storage at a pre-approved land treatment site or on an approved storage area at the land treatment site may be done prior to batch approval provided that run-off control is properly provided and a Form B application is submitted within 30 days of initial soil storage.  If approval of the batch of soil is denied, the stockpiled soil must be removed within 30 days.

If the Form B application is approved, you may store the soil stockpile on the land treatment plot for up to 10 days without run-off controls.  After 10 days the stockpiled soil must either be spread (if dates and climatic conditions allow) or run-off must be controlled either by properly covering the soil or placing geotextile silt dams or straw bales around the stockpile.  Soil which does not have Form B application approval and is stored at an approved soil storage area or pre-approved land treatment site must be immediately covered.

In addition to the storage information found in Minn. R. ch.  7037.1600 which outlines proper storage on a plot and at a storage area, there is stockpiling guidance available for storage at leak sites and interim locations.  If petroleum contaminated soil is stockpiled on the leak site property where the soil is originally generated (or at an interim location), adequate run-off control must be provided and the soil must be stockpiled on an impermeable surface (concrete or asphalt without cracks, or a minimum of 40 mil plastic liner).  Also note that if petroleum contaminated soil is stockpiled at an interim location MPCA staff approval is needed and applicable requirements of the county and township/city need to be followed.

Part A:  Circle or list the location where the soil is stored.

Part B:  List the date the soil was excavated.

Part C:  List the type of run-off controls provided, i.e.  tarp, reinforced plastic (6 mil),

unreinforced plastic (10 mil), straw bales or silt dams.

III.  Petroleum Contaminated Soil Sampling Results

First, circle all types of contaminants found in the batch of petroleum contaminated soil.  If the type(s) is not listed, you should specify.

Second, list the organic matter result from the native topsoil of the proposed or pre-approved land treatment site.  You will have this information from your Form A application.

Third, determine how many soil samples need to be taken according to the amount of soil which will be land treated by using the table on page 21 of Minn. R. ch.  7037.2900 subp. 1.  In addition, determine the type(s) of laboratory analysis which need to be run according to         Minn. R. ch.  7037.0500.  Subp. 2.  After receiving the analytical reports from the stockpile soil sampling, determine the average total petroleum hydrocarbons (TPH) levels in parts per million (ppm) for all of the parameters required, then attach the lab reports and chain of custody to the Form B.

IV.  Soil Spreading Information and Soil Nutrient Information

Soil Spreading Information

Use the formula for determining the acceptable spreading thickness is:

4 x [allowable TPH, ppm]	          =  Acceptable spreading

[average TPH in batch of soil, ppm]       	    thickness, inches

Tables 8.1 and 8.2 below indicate the maximum allowable levels of gasoline or petroleum characterized as fuel oil in contaminated soil that may be spread at a thickness of four inches:    (remember the tables differ for gasoline and fuel oil, so make sure to use the correct one)

Table 8.1.  Gasoline contaminated soil

______________________________________________________________________

Average TPH as gas (ppm)

Minimum

organic 		Permeability			Minimum thickness of suitable

matter			(inches per			soil within treatment zone (feet)

(percentage)		hour)				2	         3      	      4

___________             ____________                        _____________________________

2 % to 3.9%		less than 6			NA	         NA              1,000

less than 0.6			NA	         1,000	      2,500

4 % or greater 		less than 6			NA	         1,000           2,500				           less than 0.6  			1,000	         2,500	      5,000

______________________________________________________________________

Table 8.2  Contaminated soil characterized as fuel oil.

______________________________________________________________________

Average TPH as fuel oil (ppm)

Minimum

organic 		Permeability			Minimum thickness of suitable

matter			(inches per			soil within treatment zone (feet)

(percentage)		hour)				2	         3                   4

__________		__________			___________________________

2 % to 3.9 %	            less than 6			NA               NA	       2,000

less than 0.6			NA	         2,000	       5,000

4 % or greater		less than 6			NA	         2,000	       5,000

less than 0.6			2,000 	         5,000	     10,000

______________________________________________________________________

In these tables “NA” means that petroleum contaminated soil may not be spread under the specified conditions.  Note:  Do not round up on the organic matter result, i.e. if the organic matter result is actually 3.5 percent, then it is considered to be 2 percent on the table.  The permeability can be found in the Soil Survey book for the county where the land treatment site is located.  The minimum thickness of suitable soil is defined as the total soil thickness within the treatment zone having a permeability as listed in these tables (this value was determined in     Form A).

EXAMPLE

Petroleum contaminated soil data:

Type of contaminant:  gasoline

Average TPH as gasoline:  4,000 ppm

Land treatment site data:

Organic matter:  3 percent (rounded down to 2 percent)

Permeability:  less than 0.6 inches/hour

Thickness of suitable soil within treatment zone:   4 feet or more

4 x [2,500 ppm]   =  2.5 inches

4,000 ppm

**Note:  This formula is only needed when the average TPH result for gasoline or fuel oil from

the petroleum contaminated soil sample exceeds the allowable TPH value in the table.

The formula for determining the land area required is:

[Soil volume, cubic yards] x               0.00744                 =  Acres required

[spreading thickness, inches]

A.  Give the proposed spreading thickness for the soil on the land treatment site.

B.  Give the amount of land that will be used in acres.

Soil Nutrient Information

An evaluation to determine the need for nitrogen and/or phosphorus addition must be done for soil with an average TPH concentration of 2,000 ppm or greater (spread 4 inches thick).

Note:   This requirement also applies to petroleum loading levels that are equivalent to this level (i.e. 4,000 ppm TPH spread 2 inches thick).

Nitrogen (N) fertilizer evaluation:

[spreading

A.  [avg. TPH, ppm] x  thickness,   x 0.0128 = [      ]  x  [       ]  x  0.0128  =  ________

inches]

B.  [organic matter in upper 8 inches, percent]  x  50  =  [       ]  x  50  =   ________

C.  [result from A] - [result from B]  =  ________  minimum lbs. N per acre to add

Note 1:  This amount can be reduced by 100 lbs. N per acre if the previous crop

was alfalfa; 40 lbs. N per acres if the previous crop was soybeans, clover or

other legume; or 1/3 lb. N per acre for each lb. N applied within last year.

Note 2:  If the N application rate is determined to be less than 25 lbs. N per

acre, then N need not be applied.

Note 3:  Maximum allowable N application rates and other information are

provided in pt. 7037.3600.

D.  Proposed Nitrogen application rate:    		________  lbs. N per acre

Phosphorus (P) fertilizer evaluation:

[spreading

A.  [avg. TPH, ppm]  x  thickness,  x  0.0027  =  [     ]   x   [     ]  x  0.0027  =  _______

inches]

B.  [P concentration in native soil, ppm]  x  2  =  [   ]   x  2  =  ______

C.  [result from A]  -  [result from B]  =  ________  minimum lbs. P per acre to add

Note 1:  If the P concentration in the native soil has not been tested within the

previous three years a default value of five ppm shall be used for the calculation

in B above.

Note 2:  The amount of P to apply can be reduced by 1/2 lb. P per acre for each lb. 	applied within the previous three years.

Note 3:  If the P application rate is determined to be less than 10 lbs. P per acre,

than P need not be applied.

Note 4:  Maximum allowable P application rates and other information are

provided in pt.  7037.3600.

D.  Proposed P application rate:			_______  lbs. P per acre

**Note:  If the values in D differ from the values in C, describe on Form B the factors that  	   	   resulted in the difference.

V.  Site Map and Supporting Information

Be sure to attach all of the required information, such as site map, copies of laboratory reports and chain of custody forms for contaminated soil, and native soil nutrient results for phosphorus (if conducted) with the Form B.  If this information is not included with the Form B, the information will be requested and there will be a delay in the processing of the application.

VI.  Local Government Notification Information

Be sure to attach copies of notifications and approvals which were secured for Form A unless local government has advised the MPCA in writing that they wish to review and approve each Form B application.  In this event the applicant will need to supply with this Form B application written evidence that the county has been notified of the batch and county or township has approved of this specific batch.  Refer to Form A for an explanation of local government notification information.

VII.  Applicant Signature

The signatures of the land owner, site operator and generator must be on the Form B in order for it to be complete.  The MPCA will not process the form unless all signatures are given.

VIII.  Local Officials Mailing Addresses

Local officials mailing addresses must be given so that copies of the approval letters can be mailed to them.

Operational Requirements for Approved Land Treatment Sites

A.  Dates and climatic conditions for soil spreading.   Petroleum contaminated soil may be spread only when the surface soil is not frozen, is free of snow and ponded water, and is otherwise capable of being tilled.  Spreading must not occur after November 1 or before April 1.

B.  Petroleum loading limitations.  In no case may spreading thickness exceed 4 inches (or 540 cubic yards per acre; each inch of spreading thickness corresponds to 135 cubic yards of soil per acre if spread 4 inches thick).

C.  Petroleum contaminated soil limitation.  No more than 1,500 cubic yards is allowed to be spread within a one quarter mile radius in a five year period of time.

D.  Prohibition of mixing or repeated use.  Petroleum contaminated soil originating from separate releases must not be combined or spread on the same plot.  Plots within a pre-approved land treatment site previously used for land treatment of petroleum contaminated soil may NOT  receive repeat applications of petroleum contaminated soil.

Individual plots within a pre-approved site must be separated by a minimum of 2 feet to prevent mixing of separate batches of spread soil.

E.  Maintenance of border marking.  Border markings established at the land treatment site must remain in place during spreading of the contaminated soil and until all follow-up monitoring requirements are fulfilled.

F.  Removal of large rocks and debris.  Rocks larger than 4 inches in diameter and debris must be removed from petroleum contaminated soil prior to incorporation into the native soil.  Debris includes pieces of plastic, bricks, metal, wood, etc.

G.  Spreading and incorporation of petroleum contaminated soil.  Petroleum contaminated soil must be spread uniformly.  Petroleum contaminated soil must be incorporated into the upper 4 to 6 inches of native soil as soon as feasible but no later than 48 hours after spreading.  In order to minimize soil moisture loss and volatile loss of the petroleum contaminants, initial incorporation must be conducted only to the degree that most soil clods are broken up and petroleum contaminated soil and native soil mixing occurs.  For most land treatment applications, one or two passes with a tillage implement will result in adequate incorporation during a single tillage cycle.

H.  Tillage.  Unless the plot has been seeded to a crop, tillage of the soil following the initial incorporation must be done in monthly cycles, excluding the period from November 1 to April 1, until all soil monitoring samples are less than 10 ppm TPH or until a minimum of four tillage cycles have been done, whichever is first.  Tillage of the soil must be delayed until the soil moisture is increased if the soil lacks moisture such that tillage would cause wind erosion or decreased microbial activity.

I.   Cropping.  Following the initial incorporation of petroleum contaminated soil into the native soil, the plot may be seeded to a crop.  No root crops or crops for direct human consumption may be grown during the period of time when soil monitoring is performed.  If seeding is delayed, the tillage schedule given above must be followed until seeding can be done.

FORM C INSTRUCTIONS

IX.  MPCA Notification of Soil Spreading.

The MPCA form “Notification of Spreading Petroleum Contaminated Soil at a Land Treatment Site (Form C)” must be used for this notification. The Form C must be completed and submitted to the MPCA within 10 days following spreading the soil.

Note:   If the spread date given on Form B is different than the actual spread date, then make sure 	to put the actual spread date on Form C.  Be sure to include the date the soil was spread, 	soil volume, spreading thickness, area of land used and a site map.  In addition, please 	contact the MPCA as soon as possible if a pre-approved site is not utilized for land 	treatment.

FORM D INSTRUCTIONS

X.  Monitoring and Reporting Requirements

Monitoring, i.e. periodic soil sampling following soil spreading, must be done for each plot at the land treatment site.  The number of composite soil samples for monitoring is the same as the number of grab soil samples which were required for characterizing the soil prior to treatment.  Procedures for collection of soil monitoring samples are given in Chapter 7037.2700 Subp. 2.

Monitoring of a plot in the year of spreading must be done at the times specified below or until all soil analytical results in a single sampling round are 10 ppm TPH or less.

Soil Spreading Date		Soil Sampling in First Calendar Year

Before July 1			Once in August and once in October

July 1 to September 15	Once in October

After September 15		None

Monitoring in subsequent years must continue for those plots in which all soil analytical results are not 10 ppm TPH or less.  These sampling events must be done in June, August and October.

The MPCA form “Soil Monitoring Results for Land Treated Petroleum Contaminated Soil (Form D)” must be used for reporting the results.  Be sure to list the date monitoring took place at the land treatment site and the necessary number of monitoring soil samples.  In addition, be sure to monitor the correct batch of petroleum contaminated soil if there is more than one batch at the site.

Mail applications to:

The Minnesota Pollution Control Agency

Tanks and Emergency Response Section

520 Lafayette Road

Saint Paul, Minnesota  55155-4194

Please retain all documents that you acquired to prepare the applications, including this fact sheet, in the event that the MPCA requests to review them.

Upon request, this document can be made available in other formats, including Braille, large print and audio tape.  TTY users call 612/282-5332 or 1-800/657-3864 (voice/TTY).

Printed on recycled paper containing at least 10 percent from paper recycled by consumers.