Corrective Action Design System Monitoring Worksheet

Fact Sheet #3.31

This worksheet documents ongoing system emissions and efficiency, in part to fulfill U.S. Environmental Protection Agency (EPA) requirements.  Complete and submit this monitoring worksheet quarterly for the first year and annually thereafter. Submit an annual monitoring report as described in fact sheet 3.26, Annual Monitoring Report.  [Note: Minnesota Pollution Control Agency (MPCA) staff may vary the frequency of progress reporting on a site specific basis.]

For several remedial technologies, you are asked to provide contaminant mass removal rates in terms of gallons/day.  To aid you in calculating these values, we provide a standard equation and have calculated the gallon/kilogram (gal/kg) values for various petroleum products.  Please use these values in your calculations:

| Product | gal/kg |
| --- | --- |
| gasoline | 0.37 |
| kerosene, JP4 | 0.33 |
| fuel oil #1, diesel | 0.31 |
| fuel oil #2 | 0.30 |
| fuel oil #4 | 0.29 |

MPCA Site ID #: Leak000     	Date Form Completed:

Site Name:

Facility address

Responsible party:     	RP phone:

Consultant:      	Consultant phone:

For all sites, attach a table showing uptime and downtime for each treatment system at the site. Include explanations for any downtime that occurred during the reporting period, and a discussion of actions taken to remedy operational problems.

FREE PRODUCT RECOVERY SYSTEMS

Attach a table of free product thickness in all monitoring and recovery wells (to 0.1 feet).

Free product recovery rate:       gallons/day

Total product recovered to date:       gallons

### GROUND WATER PUMP-OUT SYSTEMS

Influent/Effluent concentrations

Attach a table of cumulative ground water influent and effluent discharge concentrations (in ug/L).

Operating parameters

Pumping rate:      gallons per minute

Amount of water table drawdown:       feet

Contaminant mass removal

Estimated contaminant mass removal rate:      gallons/day

Estimated contaminant mass removal to date:      gallons

Cumulative mass removal vs. time (plot)

SOIL VENTING SYSTEMS

#### Emission concentrations

Attach a table containing field screening results for each vapor extraction point.

Attach a table of soil vent system emissions concentrations. Include all analytical samples collected since system startup.  Collect the samples from a sampling port located upstream of the blower.  Analyze the samples for benzene, ethyl benzene, toluene and xylene using EPA Method 18.  Include the Screening Emission Rates (SERs) for each compound on the table.

Operating parameters

Extraction airflow rate:       standard cubic feet/minute (scfm)

Attach a table of cumulative vacuum data from vent points and monitoring points.

Bioactivity measurements

Attach a table of cumulative extraction system CO2 and O2 concentrations.

Contaminant mass removal:

Estimated contaminant mass removal rate:      kg/day x       gal/kg =       gal/day

Estimated contaminant mass removal to date:      gallons

Cumulative mass removal vs time (plot)

SOIL VENTING/AIR SPARGING SYSTEMS

(Complete the soil venting systems section above for all air sparge/soil venting combination systems)

Attach a table of air injection rates for each sparge point in the system.

Total air injection rate:      scfm

Total air removal rate      scfm

TOTAL SITE CONTAMINANT MASS REMOVAL

Fill out this section if ground water pump-out is used in combination with a soil venting system or a soil venting/air sparging system.

Total estimated contaminant mass removal rate for the site:      gallons/day

Total estimated contaminant mass removal to date for the site:      gallons

Cumulative mass removal vs time (plot).

SYSTEM CHANGES

Describe in detail any changes in system operation or configuration made during this reporting period (attach additional pages if needed).  Also explain any periods during which the system was not operating.

RECOMMENDATIONS

List recommendations for modifying the monitoring schedule, system operation, system configuration or site closure (attach additional pages if needed):

OBSERVATIONS

Please provide observations made at the site and describe unusual circumstance that may have influenced the sampling results:

### TABLES & GRAPHS

Tables and graphs as requested above.

##### Web pages and phone numbers

MPCA staff 		http://data.pca.state.mn.us/pca/emplsearch.html

MPCA toll free		1-800-657-3864

LUST web page		http://www.pca.state.mn.us/programs/lust_p.html

MPCA Infor. Request	http://www.pca.state.mn.us/about/inforequest.html

PetroFund Web Page	http://www.commerce.state.mn.us/mainpf.htm

PetroFund Phone		651-297-1119, or 1-800-638-0418

State Duty Officer	651-649-5451 or 1-800-422-0798

Upon request, this document can be made available in other formats, including Braille, large print and audio tape.  TTY users call 651/282-5332 or Greater Minnesota 1-800/657-3864.

Printed on recycled paper containing at least 10 percent fibers from paper recycled by consumers.