## Slide 1: PFAS Plume Tracking in the East Metro Minnesota – Michigan PFAS meeting July 12, 2018
Ginny Yingling | Hydrogeologist – Minnesota Dept. of Health

## Slide 2: PFAS in Groundwater – East Metro
Over 130 sq. mi.
  4 major aquifers
  8 municipal systems (140,000+ pop.)
  >2,100 private wells
  Much larger than predicted by models
PFBA most widespread
  More PFBA in source areas
  More mobile
Distribution controlled by:
  Bedrock features (buried valleys faults )
  Groundwater divide (Mississippi & St. Croix R. )
  Groundwater - Surface water interactions
  PFAS chemical properties
  Groundwater pumping

## Slide 3: PFOS and PFOA Less Widespread
PFOS and PFOA present at high concentrations in source areas
Groundwater concentrations decrease rapidly with distance from source
Surface water concentrations
Different PFAS “signatures” in each site based on chemistry at time of disposal
  Washington Co. landfill & Woodbury Disposal Sites dominated by PFCAs
  Helped to identify transport pathways

## Slide 4: Well Sampling Effort & Drinking Water Advisories
~2,500 wells sampled since 2003
  Frequent, intensive monitoring of private wells:
    Near source areas
    Areas with high or changing PFAS concentrations
    Areas with complex geology
  Less frequent monitoring of “sentry” private wells:
    Distal portions of plumes
    Areas with low and stable PFAS concentrations
    Areas with relatively simple geology
>800 drinking water advisories issued

## Slide 5: PFAS in Surface Water – Important Transport Pathway
Groundwater flow
Surface water or
stormwater flow