## Slide 1: PFAS Analysis at MDH PHL
MDH/MPCA Interagency PFAS Meeting
Carin Huset, PhD
June 25, 2018

## Slide 2: Outline
Sample analysis workflow
Specifics on:
  Water analysis
  Serum analysis
  Other matrices
Challenges
New directions

## Slide 3: Quantitative Sample Analysis at MDH
Sample Preparation
Internal Standards
Extraction
Chromatographic Separation
Quality Control
Results

## Slide 4: Water Analysis 2004-2017
Dilute water with Acetonitrile
Inject
PFBA, PFPeA, PFHxA, PFOA, PFBS, PFHxS, PFOS
Report level: 25-35ng/L
Quality control samples
  Matrix spikes/unknown sample
  Duplicates/batch
  Ongoing Proficiency Testing

## Slide 5: New HBV in 2017
35ng/L PFOA & 27ng/L PFOS
  New report level needed
Additional analytes
  Add PFHpA, PFNA, PFDA, PFUnDA, PFDoDA, FOSA
Challenges:
  Long chained analytes can stick to plastic
    Extract entire sample
  Lower report level  concentration step

## Slide 6: EPA 537: Determination of Selected PFAAs in Drinking Water by SPE LC/MS/MS
250 mL sample
Modifications not allowed
  Limited ISTDs used
  Does not include PFBA, PFPeA

## Slide 7: New Method: 2017-future
Lower report level: 2.5 ng/L
Sorption container walls vs. long/labor intensive sample prep
Spike w/ ISTD, thoroughly mix, take aliquot and extract
Problems with subaliquotting, ISTD recovery
Analytes:
PFBA, PFPeA, PFHxA, PFHpA, PFOA, PFNA, PFDA, PFUnDA, PFDoDA, PFBS, PFHxS, PFOS, FOSA

## Slide 8: Biomonitoring Method
400ul serum or plasma
Protein precipitation
PFBA, PFPeA, PFHxA, PFOA, PFNA, PFBS, PFHxS, PFOS
Report level: 0.1ng/ml
Quality control
  NIST SRM
  QC pools
  Ongoing Proficiency Testing
Landsteiner, et al, Biomonitoring for perfluorochemicals in a Minnesota community with known drinking water contamination, Journal of Environmental Health, 2014

## Slide 9: Other Matrices
Produce-
  Vegetables and fruits from home gardens in East Metro
Soil-
  Soil from home gardens in East Metro
Dust-
  Dust from homes in East Metro
Fish
Scher, et al. Occurrence of PFAS in garden produce at homes with a history of PFAS-contaminated drinking water, Chemosphere, 2018
Scher, et al. Does soil track-in contribute to house dust concentrations of PFAS in areas affected by soil or water contamination?, In preparation

## Slide 10: Analytical Challenges
Contamination
Interferences
Isomers
  499>80
  499>99

## Slide 11: Fluorinated Alternatives
Wang, et al. Fluorinated alternatives to long-chained PFCAs, PFSAs and their potential precursors, Environment International, 2013

## Slide 12: High Resolution Analysis
Recently acquired QTOF
  High resolution mass spectrometry
  Unknown identification
  Suspect screening through library use
  Similar to instrumentation used in other PFAS labs; collaborations

## Slide 13: Acknowledgements
Betsy Edhlund
Will Backe
Andrew Mittendorf
Carin Huset
Carin.Huset@state.mn.us
651-201-5329
Stefan Saravia
Kitrina Barry
Hien Vo
Photo not available