KEY TO

MASTER TEMPLATE FOR GROUND WATER ANALYSIS

SELECTED  ANALYTICAL PARAMETERS, METHOD NUMBERS, AND REPORTING LIMITS

Last Revised:   1 September 1993

The following table lists analytical methods and associated practical quantitation limits (PQLs)

in micrograms per liter

( unless stated otherwise) for various  analytical parameters.

| Method Reference Abbreviations |
| --- |
| Method Reference |
| SW 846 |
| Test Methods for Evaluating Solid Waste; U.S. EPA SW-846 (Third Edition with updates: includes 9 Oct. 1991 update) |
|  | MWWA |
| Methods for Chemical Analysis of Water and Wastewater |
|  | Std Meth |
| Standard Methods for the Examination of Water and Waste Water |
|  | MDH |
| Minnesota Department of Health; Method 465D |
|  | EPA |
| Includes Environmental Protection Agency Methods from 40 CFR 136, NPDES, 500 Series, SDWA, or SW-846 |
|  | MDA |
| Minnesota Department of Agriculture; number that follows "MDA" signifies pesticide cross reference list #. |
| Other Abbreviations and Flags |
| Definition |
| * |
| An asterisk"*" denotes a method detection limit (MDL) or an estimated detection limit. |
|  | PQL |
| Practical Quantitation Limit |
|  | RL |
| Reporting Limit |
|  | NL |
| Not Listed in the method reference document(s) |
|  | ? |
| PQL unknown |
|  | { } |
| Parameters shown between these brackets are not specifically addressed in the Example Sampling Protocol and/or may require a separate container or different preservation requirements than other parameters in its group |
|  | N/A |
| Not applicable |
|  | mV |
| millivolts |
|  | NTU |
| Nephelometric Turbidity Units |
|  | Deg. C |
| Degrees Celsius |

| MAJOR AND MINOR IONS |
| --- |
|  | Std. |
| Flame |
| Action |
|  | MAWW | PQL | Meth | PQL | SW-846 | PQL | SW-846 | PQL | Level |
| Anions |
|  | Bicarbonate | 310.1 | 1000 |
|  | Bromide | 320.1 |
| 4500 | 100 |
|  | Carbonate | 310.1 | 100 |

| Chloride | 325.2 | 500 |
| --- | --- | --- |
|  | Fluoride | 340.1 | 0.1 |
|  | Nitrogen Species: see below |
|  | Sulfate | 375.4 | 1000 |
|  | Silicate (Silica Dissolved Method) | 370.1 | 2000* |
| Cations |
|  | Calcium | 215.1 | 200 |
|  | 7140 | 10 | 6010 | 10 |
|  | Magnesium | 242.1 | 1 |
|  | 6010 | 30 | 7450 | 1 |
|  | Sodium | 273.1 | 2 |
|  | 7770 | 2 | 6010 | 29 |
|  | Potassium | 258.1 | 10 |
|  | 7610 | 10 | 6010 | NL |
|  | Iron | 236.1 | 30 |
|  | 7380 | 30 | 6010 | 7 |
|  | Manganese | 243.1 | 1 |
|  | 7460 | 10 | 6010 | 2 |
|  | {Strontium} |
|  | 6010 | 0.3* | 7780 | 30* |
| NITROGEN SPECIES |
|  | Alternate |
| Action |
|  | MAWW | PQL | MAWW | PQL |
|  | Level |
| Nitrate plus Nitrite Nitrogen 353.1 (10) | 353.2 | 50 | 353.1 | 10 |
|  | Nitrite Nitrogen | 354.1 | 100 |
|  | Ammonia Nitrogen | 350.1 | 50000 |
| CYANIDE |
|  | Action |
|  | MAWW | PQL |
|  | SW 846 | PQL |
|  | Level |
| Cyanide (Chlorine Type Method) | 335.3 | 5 |
|  | 9010 | 200 |

| TRACE METALS | ICP |
| --- | --- |
| Flame |
| Furnace |
| Action |
|  | SW-846 | PQL | SW-846 | PQL | SW-846 | PQL | MAWW | PQL | Level |
| Aluminum | 6010 | 45 | 7020 | 100 |
|  | Antimony | 6010 | 32 | 7040 | 200 | 7041 | 3 |
|  | Arsenic | 6010 | 53 | 7060 | 1 | 7061 | 2 |
|  | Barium | 6010 | 2 | 7080 | 100 |
|  | Beryllium | 6010 | 0.3 | 7090 | 5 | 7091 | 0.2 |
|  | Boron | 6010 | 5 |
|  | Cadmium | 6010 | 4 | 7130 | 5 | 7131 | 0.1 |
|  | Chromium, total (Cr+4 and Cr+6) | 6010 | 7 | 7190 | 50 | 7191 | 1 |
|  | Chromium VI: see below |
|  | 7195 | 5 | 218.4 | 1 |
|  | Cobalt | 6010 | 7 | 7200 | 50 | 7201 | 1 |
|  | Copper | 6010 | 6 | 7210 | 20 | 7211 | 1 |
|  | Lead | 6010 | 42 | 7420 | 100 | 7421 | 1 |
|  | Mercury |
|  | 7470 | 2 |
|  | 245.1 | 2 |
|  | {Molybdenum} | 1620 | 8 | 7480 | 100 | 7481 | 1 |
|  | Nickel | 6010 | 15 | 7520 | 40 |
|  | Selenium | 6010 | 75 | 7740 | 2 | 7741 | 2 |
|  | Silver | 6010 | 7 | 7760 | 10 | 7761 | 0.2 |
|  | Thallium | 6010 | 40 | 7840 | 100 | 7841 | 1 |
|  | Tin | 1620 | 30 | 7870 |
| {Titanium} | 1620 | 3 |
|  | Vanadium | 6010 | 8 | 7910 | 200 | 7911 | 4 |
|  | Zinc | 6010 | 2 | 7950 | 5 | 7951 | 0.5 |
| CHROMIUM VI | ICP |
| Flame |
| Furnace |
| Action |
|  | SW-846 | PQL | SW-846 | PQL | SW-846 | PQL |
|  | Level |
| Chromium VI |
|  | 7195 | 5 |
| MISCELLANEOUS |
|  | STD. |
| Action |
|  | MWWA | PQL | METH. | PQL |
|  | Level |
| Specific Conductance | 120.1 |
| Total Dissolved Solids | 1030 | 1000 |
|  | Total Suspended Solids | 160.2 | 1000 |
|  | Cation/Anion Balance |
|  | 1030F | N/A |
|  | Turbidity | 180.1 | 0-40NTU | 2130 | 0.1 NTU |

| VOLATILE ORGANICS | GC |
| --- | --- |
| GC |
| GC/MS |
| Alternate |
| Action |
|  | SW-846 | PQL | MDH | RL | SW-846 | PQL | SW-846 | PQL | Level |
| Halogenated Volatiles |
|  | Acrolein | 8030 | 7 |
|  | 8260 | 100 |
|  | Acrylamide (no methods found) |
|  | Acrylonitrile | 8030 | 5 |
|  | 8260 | 5 | 8031 | 10 |
|  | Allyl Chloride | 8010 | 5 | 465D | 0.5 | 8260 | 10 | 8240 | 5 |
|  | Bromobenzene | 8021 | 0.03* | 465D | 0.2 | 8260 | 5 |  |
| Bromochloromethane | 8021 | 0.1 | 465D | 0.5 | 8260 | 5 |
|  | Bromodichloromethane | 8021 | 0.2 | 465D | 0.2 | 8260 | 5 | 8010 | 1 |
|  | Bromoform | 8021 | 16 | 465D | 1 | 8260 | 5 | 8010 | 2 |
|  | Bromomethane (Methyl bromide) | 8021 | 11 | 465D | 2 | 8240 | 5 | 8010 | 3 |
|  | Carbon Tetrachloride | 8021 | 0.1 | 465D | 0.2 | 8260 | 10 | 8010 | 1.2 |
|  | Chlorobenzene | 8021 | 0.1 | 465D | 0.2 | 8260 | 5 | 8010 | 2.5 |
|  | Chloroethane | 8021 | 1 | 465D | 1 | 8260 | 10 | 8010 | 5.2 |
|  | Chloroform | 8021 | 0.2 | 465D | 0.1 | 8260 | 5 | 8010 | 0.5 |
|  | Chloroprene | 8010 | 50 |
|  | 8260 | 20 | 8240 | 5 |
|  | 2-Chlorotoluene | 8021 | 0.1 | 465D | 0.5 | 8260 | 5 |
|  | 4-Chlorotoluene | 8021 | 0.1 | 465D | 0.5 | 8260 | 5 |
|  | Dibromochloromethane | 8021 | 0.3 | 465D | 0.5 | 8260 | 5 | 8011 | 0.1 |
|  | 1,2-Dibromo3-chloropropane (DBCP) | 8021 | 30 | 465D | 2 | 8260 | 5 | 8240 | 100 |
|  | 1,2-Dibromoethane (EDB) | 8021 | 10 | 465D | 1 | 8260 | 5 | 8011 | 0.1 |
|  | Dichlorofluoromethane |
|  | 465D | 1 |
|  | 1,2-Dichlorobenzene | 8021 | 0.2/0.5 | 465D | 0.2 | 8260 | 5 | 8121 | 2.7 |
|  | 1,3-Dichlorobenzene | 8021 | 0.2 | 465D | 0.2 | 8260 | 5 | 8121 | 2.5 |
|  | 1,4-Dichlorobenzene | 8021 | 0.1 | 465D | 0.2 | 8260 | 5 | 8121 | 8.9 |
|  | trans-1,4-Dichloro-2-butene |
|  | 8260 | 100 | 8240 | 100 |
|  | Dichlorodifluoromethane (CFC-12) | 8021 | 0.5 | 465D | 1 | 8260 | 5 |
|  | 1,1-Dichloroethane | 8021 | 0.7 | 465D | 0.2 | 8260 | 5 | 8010 | 0.7 |
|  | 1,2-Dichloroethane | 8021 | 0.3 | 465D | 0.2 | 8260 | 5 | 8010 | 0.3 |
|  | 1,1-Dichloroethene | 8021 | 0.7 | 465D | 0.5 | 8260 | 5 | 8010 | 1.3 |
|  | Halogenated Volatiles (Cont) |
|  | cis-1,2-Dichloroethene | 8021 | 0.2 | 465D | 0.2 | 8260 | 5 | 8010 | 1 |
|  | trans-1,2-Dichloroethene | 8021 | 0.5 | 465D | 0.1 | 8260 | 5 |
|  | Dichlorofluormethane |
|  | 465D | 1 |
|  | 1,2-Dichloropropane | 8021 | 0.06 | 465D | 0.2 | 8260 | 5 | 8010 | 0.4 |
|  | 1,3-Dichloropropane | 8021 | 0.3 | 465D | 0.2 | 8260 | 5 |
|  | 2,2-Dichloropropane | 8021 | 0.5 | 465D | 0.5 | 8260 | 5 |
|  | 1,1-Dichloropropene | 8021 | 0.2 | 465D | 0.2 | 8260 | 5 |
|  | cis-1,3-Dichloropropene | 8010 | 20 | 465D | 0.2 | 8260 | 5 |
|  | trans-1,3-Dichloropropene | 8010 | 5 | 465D | 0.2 | 8260 | 5 |
|  | Hexachlorobutadiene | 8021 | 0.5 | 465D | 0.5 | 8260 | 5 | 8121 | 0.014 |
|  | Hexachloroethane | 8120 | 0.3 |
|  | 8260 | 10 | 8270 | 10 |
|  | Methyl iodide (Iodomethane) | 8010 | 40 |
|  | 8260 | 10 | 8240 | 5 |
|  | Chloromethane (Methyl Chloride) | 8021 | 0.3 | 465D | 2 | 8260 | 5 | 8010 | 0.8 |
|  | Dibromomethane (Methylene bromide) | 8021 | 22 | 465D | 1 | 8260 | 5 |
|  | Dichloromethane (Methylene chloride) | 8021 | 0.2 | 465D | 0.5 | 8260 | 5 |
|  | 1,1,1,2-Tetrachloroethane | 8021 | 0.05 | 465D | 0.2 | 8260 | 5 |
|  | 1,1,2,2-Tetrachloroethane | 8021 | 0.1 | 465D | 0.2 | 8260 | 5 | 8010 | 0.3 |
|  | Tetrachloroethene (PCE) | 8021 | 0.5 | 465D | 0.2 | 8260 | 5 | 8010 | 0.3 |
|  | 1,2,3-Trichlorobenzene | 8021 | 0.3 | 465D | 0.5 | 8260 | 5 |
|  | 1,2,4-Trichlorobenzene | 8021 | 0.2/0.3 | 465D | 0.5 | 8260 | 5 | 8121 | 1.3 |
|  | 1,1,1-Trichloroethane | 8021 | 0.3 | 465D | 0.2 | 8260 | 5 |
|  | 1,1,2-Trichloroethane | 8010 | 0.2 | 465D | 0.2 | 8260 | 5 |
|  | Trichloroethene (TCE) | 8021 | 0.2 | 465D | 0.1 | 8260 | 5 | 8010 | 1.2 |
|  | Trichlorofluoromethane CFC-11 | 8021 | 0.3 | 465D | 2 | 8260 | 5 |
|  | Trichlorotrifluoromethane |  |  | 465D | 0.2 |  |  |
|  | 1,2,3-Trichloropropane | 8021 | 5 | 465D | 0.5 | 8260 | 5 |
|  | 1,2,4-Trimethylbenzene | 8021 | 0.5 | 465D | 0.5 | 8260 | 5 |
|  | 1,3,5-Trimethylbenzene | 8021 | 0.04 | 465D | 0.5 | 8260 | 5 |
|  | Vinyl chloride | 8021 | 0.2/0.4 | 465D | 1 | 8260 | 5 | 8010 | 1.8 |
| Aromatic Volatiles |
|  | Benzene | 8020 | 2 | 465D | 0.2 | 8260 | 5 | 8021 | 0.09 |
|  | n-Butylbenzene | 8021 | 0.2 | 465D | 0.5 | 8260 | 5 |
|  | sec-Butylbenzene | 8021 | 0.2 | 465D | 0.5 | 8260 | 5 |
|  | t-Butylbenzene | 8021 | 0.6 | 465D | 0.5 | 8260 | 5 |
|  | Ethylbenzene | 8020 | 2 | 465D | 0.2 | 8260 | 5 | 8021 | 0.05 |
|  | Naphthalene (also see Semi-volatiles) | 8021 | 0.6 | 465D | 0.5 | 8260 | 5 | 8270 | 10 |
|  | Isopropyl Benzene | 8021 | 0.5 | 465D | 0.5 | 8260 | 5 |
|  | n-Propyl Benzene | 8021 | 0.04 | 465D | 0.5 | 8260 | 5 |
|  | p-Isopropyltoluene | 8021 | 0.1 | 465D | 0.5 | 8260 | 5 |
|  | Tetrahydrofuran (THF) |
|  | 465D | 10 |
|  | Styrene | 8021 | 0.1 | 465D | 0.5 | 8260 | 5 |
|  | Toluene | 8021 | 0.1 | 465D | 0.2 | 8260 | 5 |
|  | m-Xylene | 8021 | 0.4 | 465D | 0.2 | 8260 | 5 |
|  | o-Xylene | 8021 | 0.4 | 465D | 0.2 | 8260 | 5 |
|  | p-Xylene | 8021 | 0.4 | 465D | 0.2 | 8260 | 5 |
| Non-halogenated Volatiles |
|  | Acetonitrile (Methyl cyanide) | 8015 | 100 |
|  | 8240 | 100 |
|  | Acetone |
|  | 465D | 20 | 8260 | 100 |
|  | Carbon Disulfide |
|  | 8260 | 100 |
|  | Ethyl Ether | 8015 | 5 | 465D | 2 | 1624 | 50 |
|  | Ethyl methacrylate | 8015 | 5 |
|  | 8260 | 10 | 8240 | 5 |
|  | Epichlorhydrin |
|  | 8240 | 10 |
|  | 2-Hexanone (MBK) |
|  | 8260 | 50 | 8240 | 50 |
|  | Isobutyl alcohol | 8015 | 50 |
|  | 8240 | 100 |
|  | Methacrylonitrile | 8015 | 5 |
|  | 8260 | 100 | 8240 | 100 |
|  | Methyl tert-Butyl ether (MTBE) |
|  | 465D | 2 |
|  | 2-Butanone (MEK) | 8015 | 10 | 465D | 10 | 8260 | 100 |
|  | Methyl methacrylate | 8015 | 2 |
|  | 8260 | 30 | 8240 | 5 |
|  | 4-Methyl-2-pentanone (MIBK) | 8015 | 5 | 465D | 5 | 8260 | 100 |

| NON- (AND SEMI-) VOLATILE ORGANICS | GC |
| --- | --- |
| GC/MS |
| HPLC |
| Alternate |
| Action |
|  | EPA | PQL | SW-846 | PQL | EPA | PQL | SW-846 | PQL | Level |
| PAHs |
|  | Acenaphthene (Acenapthylene) | 8100 | 200 | 8270 | 10 | 8310 | 18 |
|  | Anthracene | 8100 | 200 | 8270 | 10 | 8310 | 6.6 |
|  | Benzo[a]anthracene | 8100 | 200 | 8270 | 10 | 8310 | 0.13 |
|  | Benzo[b]fluoranthene | 8100 | 200 | 8270 | 10 | 8310 | 0.18 |
|  | Benzo[k]fluoranthene | 8100 | 200 | 8270 | 10 | 8310 | 0.17 |
|  | Benzo[g,h,i]perylene | 8100 | 200 | 8270 | 10 | 8310 | 0.76 |
|  | Benzo[a]pyrene | 8100 | 200 | 8270 | 10 | 8310 | 0.23 |
|  | Dibenz[a,h]anthracene | 8100 | 200 | 8270 | 10 | 8310 | 0.3 |
|  | Chrysene | 8100 | 200 | 8270 | 10 | 8310 | 1.5 |
|  | Fluoranthene | 8100 | 200 | 8270 | 10 | 8310 | 2.1 |
|  | Fluorene | 8100 | 200 | 8270 | 10 | 8310 | 2.1 |
|  | Indeno(1,2,3-cd)pyrene | 8100 | 200 | 8270 | 10 | 8310 | 0.43 |
|  | Isosafrole |  |
| 8270 | 10 |
|  | Napthalene (also see Volatile list) | 8100 | 200 | 8270 | 10 | 8310 | 18 | 8021 | 0.6 |
|  | Phenanthrene | 8100 | 200 | 8270 | 10 |
|  | Pyrene | 8100 | 200 | 8270 | 10 | 8310 | 2.7 |
|  | 7,12-Dimethylbenz[a]anthracene |
|  | 8270 | 10 |
| Haloethers |
|  | Bis(2-chloroethoxy)methane | 8110 | 5 | 8270 | 10 |
|  | Bis(2-chloroethyl)ether | 8110 | 3 | 8270 | 10 |
|  | Bis(2-chloro-1-methylethyl)ether | 8110 | 10 | 8270 | 10 |
|  | 4-Chlorophenyl phenyl ether | 8110 | 40 | 8270 | 10 |
|  | 4-Bromophenyl phenyl ether | 8110 | 25 | 8270 | 10 |
| Phthalate Esters |
|  | Bis(2-ethylhexyl)phthalate | 8060 | 200/20 | 8270 | 10 |
|  | 8061 | 2.7 |
|  | Butyl benzyl phthalate | 8060 | 3.4/150 | 8270 | 10 |
|  | 8061 | 0.42 |
|  | Di-n-butyl phthalate | 8060 | 3.6/140 | 8270 | 10 |
|  | 8061 | 3.3 |
|  | Di-n-octyl phthalate | 8060 | 310/30 | 8270 | 10 |
|  | 8061 | 0.49 |
|  | Dimethyl phthalate | 8060 | 2.9/190 | 8270 | 10 |
|  | 8061 | 6.4 |
|  | Diethylphthalate | 8060 | 4.9/310 | 8270 | 10 |
|  | 8061 | 2.5 |
| Phenols |
|  | p-Chloro-m-cresol | 8040 | 3.6 | 8270 | 20 |
|  | 2-Chlorophenol | 8040 | 3.1 | 8270 | 10 |
|  | m-Cresol (3-methyl phenol) | 8040 | 5 | 8270 | 10 |
|  | o-Cresol ( 2-methyl phenol) | 8040 | 5 | 8270 | 10 |
|  | p-Cresol (4-methyl phenol) | 8040 | 5 | 8270 | 10 |
|  | 2,4-Dichlorophenol | 8040 | 3.9 | 8270 | 10 |
|  | 2,6-Dichlorophenol | 8040 | 5 | 8270 | 10 |
|  | 3,3'-Dichlorobenzidine | 8040 | 5 | 8270 | 20 |
|  | 2,4-Dimethylphenol | 8040 | 3.2 | 8270 | 10 |
|  | 4,6-Dinitro-2-methyl phenol | 8040 | 150 | 8270 | 50 |
|  | 2,4-Dinitrophenol | 8040 | 130 | 8270 | 50 |
|  | 2-Nitrophenol | 8040 | 4.5 | 8270 | 10 |
|  | 4-Nitrophenol | 8040 | 28 | 8270 | 50 |
|  | Pentachlorophenol | 8040 | 74 | 8270 | 50 |
|  | 2,3,4,6-Tetrachlorophenol |
|  | 8270 | 10 |
|  | 2,4,5-Trichlorophenol |
|  | 8270 | 10 |
|  | 2,4,6-Trichlorophenol | 8040 | 6.4 | 8270 | 10 |
|  | Phenol | 8040 | 1.4 | 8270 | 10 |
| Nitroaromatics and Cyclic Ketones |
|  | m-Dinitrobenzene |
|  | 8270 | 20 | 8330 | 4 |
|  | 2,4-Dinitrotoluene | 8090 | 0.2 | 8270 | 10 | 8330 | 5.7 |
|  | 2,6-Dinitrotoluene | 8090 | 0.1 | 8270 | 10 | 8330 | 9.4 |
|  | Isophorone | 8090 | 157/57 | 8270 | 10 |
|  | Nitrobenzene | 8090 | 137/36 | 8270 | 10 |
| Nitrosamines |
|  | N-Nitrosodiethylamine | 8070 | 2 | 8270 | 20 |
|  | N-Nitrosodimethylamine | 8070 | 5 | 8270 | 10 |
|  | N-Nitrosodiphenylamine | 8070 | 10 | 8270 | 10 |
|  | N-Nitrosodipropylamine |
|  | 8270 | 10 |
|  | N-Nitrosomethylethylamine |
|  | 8270 | 10 |
| Other Non- (and Semi-) Volatiles |
|  | Acetophenone |
|  | 8270 | 10 |
|  | 2-Acetylaminofluorene |
|  | 8270 | 20 |
|  | 4-Aminobiphenyl |
|  | 8270 | 20 |
|  | Benzyl Alcohol |
|  | 8270 | 20 |
|  | Carbofuran (Furadan) |
|  | 8270 | 10 | 531.1 | 1.5 |
|  | p-Chloroaniline |
|  | 8270 | 20 |
|  | Chlorobenzilate | 508 | 5 * | 8270 | 10 |
|  | 2-Chloronaphthalene | 8120 | 9.4 | 8270 | 10 |
|  | 8121 | 13 |
|  | Diallate | 1618 | 0.045* | 8270 | 10 |
|  | Dibenzofuran |
|  | 8270 | 10 |
|  | Dimethoate | 8141 | 2.6 | 8270 | 20 |
|  | p-(Dimethylamino)azobenzene |
|  | 8270 | 10 |
|  | 3,3'-Dimethylbenzidine |
|  | 8270 | 10 |
|  | Dinoseb (2-sec-butyl-4,6-dinitrophenol) | 8150 | 1 | 8270 | 20 |
|  | Diphenylamine | 620 | 1.6* | 8270 | 10 |
|  | 1,2-Diphenylhydrazine |
|  | 8270 | 10 |
|  | Other Non- (and Semi-) Volatiles (Cont.) |
|  | Disulfoton | 8141 | 0.7 | 8270 | 10 |
|  | 8140 | 2 |
|  | Ethyl methanesulfonate |
|  | 8270 | 20 |
|  | Famphur | 622.1 | 19 | 8270 | 20 |
|  | Hexachlorobenzene | 8120 | 0.5 | 8270 | 10 |
|  | 8121 | 0.056 |
|  | Hexachlorocyclopentadiene | 8120 | 4 | 8270 | 10 |
|  | 8121 | 2.4 |
|  | Hexachloropropene |
|  | 8270 | 10 |
|  | 3-Hydroxycarbofuran (breakdown product)(NL) |
|  | Isodrin |
|  | 8270 | 20 |
|  | Kepone |
|  | 8270 | 20 |
|  | Methapyrilene |
|  | 8270 | 100 |
|  | 3-Methylcholanthrene |
|  | 8270 | 10 |
|  | Methyl methanesulfonate |
|  | 8270 | 10 |
|  | 2-Methylnaphthalene |
|  | 8270 | 10 |
|  | Methyl parathion | 8141 | 1 | 8270 | 10 |
|  | Methiocarb (Mesurol) |
|  | 531.1 | 4 |
|  | Methomyl (Lannate) |
|  | 531.1 | 0.5 |
|  | 1,4-Methylnaphthoquinone |
|  | 8270 | 10 |
|  | 1-Methylamine |
|  | 8270 | 10 |
|  | 2-Methylamine |
|  | 8270 | 10 |
|  | 2-Nitroaniline |
|  | 8270 | 50 |
|  | 3-Nitroaniline |
|  | 8270 | 50 |
|  | 4-Nitroaniline |
|  | 8270 | 20 |
|  | N-Nitroso-di-n-butylamine |
|  | 8270 | 10 |
|  | N-Nitrosopiperidine |
|  | 8270 | 20 |
|  | N-Nitrosopyrrolidine |
|  | 8270 | 40 |
|  | 5-Nitro-o-toluidene |
|  | 8270 | 10 |
|  | Pentachlorobenzene | 8121 | 0.38 | 8270 | 10 |
|  | Pentachloronitrobenzene |
|  | 8270 | 20 |
|  | Phenacetin |
|  | 8270 | 20 |
|  | p-Phenylenediamine |
|  | 8270 | 10 |
|  | Pronamide |
|  | 8270 | 10 |
|  | Safrole |
|  | 8270 | 10 |
|  | 1,2,4,5-Tetrachlorobenzene | 8121 | 0.095 | 8270 | 10 |
|  | Thionazin | 8141 | 5 | 8270 | 20 |
|  | 2,4,5-T (2,4,5-Trichlorophenoxyacetic acid | 8150 | 20 |
|  | (2[2,4,5-Trichlorophenoxy]-Propanoic acid) | 8150 | 1.7 |
|  | - also known as 2,4,5-TP (Silvex) |
|  | 1,2,4-Trichlorobenzene ( also see Volatiles) |
|  | 8270 | 10 |
|  | 8021 | 0.2/0.3 |
|  | O,O,O-Triethyl phosphorothioate |
|  | 8270 | 10 |
|  | sym-Trinitrobenzene |
|  | 8270 | 10 | 8330 | 7.3 |
|  | o-Toluidine |
|  | 8270 | 10 |
| Organochlorine Pesticides |
|  | Aldrin | 8080 | 0.04 | 8270 | 10 | 8081 | 0.34 |
|  | Chlordane, alpha | 8080 | 0.14 | 8270 | 50 |
|  | Chlordane. gamma | 508 | 0.15 |
|  | 8081 | 0.37 |
|  | Chlordane, delta | 508 | NL |
|  | 4,4'-DDD | 8080 | 0.11 | 8270 | 10 | 8081 | 0.5 |
|  | 4,4'-DDE | 8080 | 0.04 | 8270 | 10 | 8081 | 0.58 |
|  | 4,4'-DDT | 8080 | 0.12 | 8270 | 10 | 8081 | 0.81 |
|  | Organochlorine Pesticides (Cont.) |
|  | Dieldrin | 8080 | 0.02 | 8270 | 10 | 8081 | 0.44 |
|  | Endosulfan I | 8080 | 0.14 | 8270 | 20 | 8081 | 0.3 |
|  | Endosulfan II | 8080 | 0.04 | 8270 | 20 | 8081 | 0.4 |
|  | Endosulfan sulfate | 8080 | 0.66 | 8270 | 10 | 8081 | 0.35 |
|  | Endrin | 8080 | 0.06 | 8270 | 20 | 8081 | 0.39 |
|  | Endrin aldehyde | 8080 | 0.23 | 8270 | 10 | 8081 | 0.5 |
|  | a-BHC | 8080 | 0.03 | 8270 | 10 | 8081 | 0.35 |
|  | b-BHC | 8080 | 0.06 | 8270 | 10 | 8081 | 0.23 |
|  | d-BHC | 8080 | 0.09 | 8270 | 10 | 8081 | 0.24 |
|  | g-BHC (Lindane) | 8080 | 0.04 | 8270 | 10 | 8081 | 0.25 |
|  | Heptachlor | 8080 | 0.03 | 8270 | 10 | 8081 | 0.4 |
|  | Heptachlor epoxide (breakdown product) | 8080 | 0.83 | 8270 | 10 | 8081 | 0.32 |
|  | Methoxychlor | 8080 | 1.76 | 8270 | 10 | 8081 | 0.86 |
|  | Strobane (no methods found) |
|  | Toxaphene | 8080 | 2.4 | 8270 | N/A | 8081 | 0.86 |
| Polychorinated Biphenyls |
|  | - Arochlor 1016 | 8080 | 10 |
|  | - Arochlor 1221 | 8080 | 20 |
|  | - Arochlor 1232 | 8080 | 20 |
|  | - Arochlor 1242 | 8080 | 10 |
|  | - Arochlor 1248 | 8080 | 10 |
|  | - Arochlor 1254 | 8080 | 10 |
|  | - Arochlor 1260 | 8080 | 10 |
| Organophosphorus Pesticides |
|  | Chlorfenvinphos | 1618 | .002* | 8270 | 20 |
|  | Chlorpyrifos (Lorsban, Dursban) | 8141 | 0.07* |
|  | MDA 1 | 0.24 |
|  | Diazinon | 507 | 0.25 |
|  | Disulfoton (Disyston) | 507 | 0.3 | 8270 | 10 |
|  | Fonofos (Dyfonate) | 622.1 | 0.7 |
|  | MDA 1 | 0.16 |
|  | Malathion | 8141 | 0.11 |
|  | Methadithion (no methods found) |
|  | Parathion (ethyl Parathion) | 8141 | 0.5* | 8270 | 10 |
|  | methyl Parathion | 8141 | 0.12* | 8270 | 10 |
|  | MDA1 | 0.1 |
|  | Phorate (Thimet) | 8141 | 0.5* | 8270 | 10 |
|  | MDA 1 | 0.49 |
|  | Terbufos (Counter) | 507 | 0.5* | 8270 | 20 |
|  | MDA 1 | 0.26 |
|  | Phosphamiden |
|  | 8270 | 100 |
| Herbicides |
|  | Alachlor (Lasso) | 505 | 0.23* | 525 | 1* |
|  | MDA 1 | 0.16 |
|  | Atrazine | 505 | 2.4* | 525 | .1* |
|  | MDA 1 | 0.05 |
|  | Butylate (Sutan) |
|  | MDA 1 | 0.79 |
|  | Cyanazine (Bladex) |
|  | MDA 1 | 0.12 |
|  | EPTC (Eptam) |
|  | MDA 1 | 0.24 |
|  | Ethafluralin (Sonalan) |
|  | MDA 1 | ? |
|  | Linuron (Lorox) |
|  | MDA 1 | 0.17 |
|  | Metalochlor (Dual) |
|  | MDA 1 | 0.56 |
|  | Metribuzin (Sencor, Lexone) | 507 | 0.15* |
|  | MDA 1 | 0.17 |
|  | Pendamethalin (Prowl) |
|  | MDA 1 | ? |
|  | Herbicides (Cont.) |
|  | Propachlor (Ramrod) |
|  | MDA 1 | 0.1 |
|  | Prometon (Pramitol) | 507 | 0.3* |
|  | MDA 1 | ? |
|  | Propazine (Milogard) |
|  | MDA 1 | ? |
|  | Simazine (Princep) | 505 | 6.8* | 525 | 0.2* |
|  | MDA 1 | 0.08 |
|  | Triallate (Far-go, Avadex) |
|  | MDA 1 | 0.02 |
|  | Trifluralin (Treflan) | 508 | 0.25* | 8270 | 10 |
| Acid Herbicides |
|  | 2,4-D (2,4-Dichlorophenoxyacetic acid) |
|  | 8150 | 10 | MDA 2 | 0.21 |
|  | 2,4-DB |
|  | MDA 2 | ? |
|  | Dicamba (Banvel) |
|  | MDA 2 | 0.18 |
|  | Chloramben (Amiben) |
|  | MDA 2 | 1.6 |
|  | MCPA |
|  | MDA 2 | 0.27 |
|  | MCPB (Cantrol) |
|  | MDA 2 | ? |
|  | MCPP (Mecoprop) |
|  | MDA 2 | ? |
|  | Pentachlorophenol | 8040 | 5 | 8270 | 50 |
|  | MDA 2 | 0.28 |
|  | Pichloram (Tordon) |
|  | MDA 2 | 1.8 |
|  | 2,4,5-T (2,4,5-Trichlorophenoxyacetic acid | 8150 | 20 |
|  | 2,4,5-TP (Silvex) | 8150 | 2 |
|  | - (2[2,4,5-Trichlorophenoxy]-Propanoic acid) |
|  | Trichlorpyr |
|  | MDA 2 | ? |
| N-Methyl Carbamate Pesticides |
|  | Aldicarb (Temik) |
|  | 531.1 | 1 | MDA 3 | 0.5 |
|  | Aldicarb Sulfoxide (metabolite) |
|  | 531.1 | 2 | MDA 3 | ? |
|  | Aldicarb Sulfone (metabolite) |
|  | 531.1 | 2 | MDA 3 | ? |
|  | Carbofuran (Furadan) |
|  | 8270 | 10 | 531.1 | 1.5 | MDA 3 | 0.5 |
|  | 3-Hydroxycarbofuran (metabolite) |
|  | MDA 3 | ? |
|  | Carbaryl (Sevin) |
|  | 8270 | 10 | 531.1 | 2 | MDA 3 | 0.5 |
|  | Methiocarb (Mesurol) |
|  | 531.1 | 4 | MDA 3 | ? |
|  | Methomyl (Lannate) |
|  | 531.1 | 0.5 | MDA 3 | ? |
|  | Oxamyl (Vydate) |
|  | 531.1 | 2 | MDA 3 | ? |
|  | Propoxur (Baygon) |
|  | 531.1 | 1 | MDA 3 | ? |

| DIOXINS AND DIBENZO FURANS | GC/MS |
| --- | --- |
| GC/MS |
| Action |
| Units = nanograms per liter (ng/L) | SW-846 | PQL | EPA | PQL |
|  | Level |
|  | 2,3,7,8 - TCDD | 8290 | 2 | 8280 | 500 |
|  | 2,3,7,8 - TCDF | 8290 | 2 | 8280 | 600 |
|  | 1,2,3,7,8 - PECDD | 8290 | 2 | 8280 | 1000 |
|  | 1,2,3,7,8 - PECDF | 8290 | 2 | 8280 | 2000 |
|  | 2,3,4,7,8 - PECDF | 8290 | 2 | 8280 | 2000 |
|  | 1,2,3,4,7,8 - HXCDD | 8290 | 5 | 8280 | 2000 |
|  | 1,2,3,6,7,8 - HXCDD | 8290 | 5 | 8280 | 2000 |
|  | 1,2,3,7,8,9 - HXCDD | 8290 | 5 | 8280 | 2000 |
|  | 1,2,3,4,7,8 - HXCDF | 8290 | 5 | 8280 | 3000 |
|  | 1,2,3,6,7,8 - HXCDF | 8290 | 5 | 8280 | 3000 |
|  | 1,2,3,7,8,9 - HXCDF | 8290 | 5 | 8280 | 3000 |
|  | 2,3,4,6,7,8 - HXCDF | 8290 | 5 | 8280 | 3000 |
|  | 1,2,3,4,6,7,8 - HPCDD | 8290 | 5 | 8280 | 2000 |
|  | 1,2,3,4,6,7,8 - HPCDF | 8290 | 5 | 8280 | 3000 |
|  | 1,2,3,4,7,8,9 - HPCDF | 8290 | 5 | 8280 | 3000 |
|  | OCDD | 8290 | 10 | 8280 | 4000 |
|  | OCDF | 8290 | 10 | 8280 | 4000 |
|  | EQUILIBRIUM GEOCHEMISTRY |
|  | STD. |
| Action |
|  | MAWW | PQL | METH. | PQL |
|  | Level |
| {Dissolved Oxygen} | 360.2 | 50* | 4500-O | 0.1 mg/L |
|  | {Temperature} {no holding time allowed} | 170.1 |
| 2550 | 0.1 mg/L |
|  | {Appearance} {field observation advised} |
|  | 2110 | N/A |
|  | {Eh (Redox)} {field measurement advised} |
|  | 2580 | 1 mV |
|  | pH | 150.1 |
| 4500h | 0.1 units |
|  | Total Alkalinity | 310.1 | 10000 | 2320 | NL |
| TOTAL COLIFORMS | MF Meth |
| Action |
|  | SW-846 | PQL |
|  | Level |
| Total Coliforms | 9132 | <1CFU |
| TOTAL ORGANIC CARBON |
|  | Action |
|  | MAWW | PQL |
|  | Level |
| Total Organic Carbon | 415.1 | 1000 |
| TOTAL PHOSPHORUS |
|  | Action |
|  | MAWW | PQL |
|  | Level |
| Total Phosphorus | 365.2 | ? |
|  | SULFIDE |
|  | Action |
|  | MAWW | PQL | SW-846 | PQL |
|  | Level |
| Sulfide |
|  | 9030A | 4000 |
| RADIUM, GROSS ALPHA, GROSS BETA |
|  | Action |
| Units = Pico Curies per liter (pCi/L) | SW-846 | PQL |
|  | Level |
| Radium | 9315 | ? |
|  | Gross Alpha | 9310 | 3 |
|  | Gross Beta | 9310 | 4 |